## Slide 1
Europa is :
Sixth closest moon of planet Jupiter .
Sixth largest moon in the Solar System .
A water ocean hypothetically exists
beneath a thick shell of ice surfacing
Europa.
What is Europa?

## Slide 2
Explore a multi-node radio communications capability, such that multiple submersibles exchange information underwater with a lander and each other for the purpose of exploring Jupiter's icy moon Europa.
The exploration region of highest interest lies in the hypothesized sub glacial ocean.
Europa is a promising life harboring moon.
Project Description

## Slide 3
Develop a concept of operations describing the exploration process as it is pictured to take place after the payload has been deployed underwater.
Prototype development to test the feasibility of the proposed concept of operations and the viability of RF communication underwater.
Project Description

## Slide 4
complex process of exploring

## Slide 5
Sign of life on Europa .
Water Properties and Measurements :
pH
Pressure
Salinity
Hardness
Dissolved oxygen
Specific conductance
Water temperature
Videos and images
What are we looking for ?

## Slide 6
The scenario consists of :
A lander
A tether
A casing
Mission concept of operations

## Slide 7
The lander sends information back to earth.
The tether connects the casing with the lander.
The casing holds:
Two small autonomous
underwater vehicles.
Onboard computer.
Charging stations.
Main communication
node.
Mission concept of operation

## Slide 8
How will AUVs know where to explore?
AUVs are preprogrammed to explore ocean water and equipped with Artificial Intelligence (AI) to maneuver around obstacles.
AUVs measure data along circular paths increasing in diameter with depth.
Miniaturized side-scan sonar is used for mapping and navigating the environment.

## Slide 9
AUVs’ functions require the presence of positioning system to identify a specific location and map the surroundings. The following positioning systems were chosen:
1)Inertial Navigation system
Positioning and tracking system

## Slide 10
Positioning and tracking system
2)Acoustic system (Ultra short Baseline):
To mitigate the drifting problem of the Inertial navigation system.
It identifies the position in two dimensions only.
Main communication node holds an array of transducers.
Each AUV has a transponder mounted on it.

## Slide 11
Pressure sensor is used to calculate the third dimension.
The AUVs are equipped with Artificial Intelligence (AI) to maneuver around obstacles.
The AUVs have obstacle avoidance capabilities.
Miniaturized side-scan sonar is used for mapping and navigating the environment.
Positioning and tracking system

## Slide 12
The Communication System
Acoustic system
Radio Frequency
Long range
Low data rate
For sending simple
measurements
Short range
High data rate
For sending videos
and images
The Communication System

## Slide 13
Step1: Arrival and Release
Lander boots up the main communication node.
Main communication node turns on the 2 AUVs.
Chamber exits are open
AUVs release themselves in water.
Steps of Exploration

## Slide 14
Step 2: Initial Readings
Each AUV covers the perimeter of half a circle of radius 10 cm and takes measurements instantly after exiting the chambers.
Steps of Exploration

## Slide 15
Step 3:
The two AUVs dive to reach the same level.
They explore along a circle of 20 cm (numbers are generally subject to change but are representative of the pattern.)
Steps of Exploration
20 cm

## Slide 16
4) Step 4:
AUVs dive an extra 50 cm.
AUVs cover a circle of radius 50 cm
50 cm
Steps of Exploration

## Slide 17
AUV 1 continues taking small steps.
AUV 2 starts taking larger steps both deeper and wider.

## Slide 18
5) Step 5:
AUV 2 increases its depth and circle radius exponentially: 10m,20m,50m,100m…
Steps of Exploration

## Slide 19
6) Step 6:Heading Back
Same pattern will be followed in the reverse direction.
AUVs head back to the starting point, with radii of circles increasing with decreased depth.
Steps of Exploration
Increased
radius

## Slide 20
AUVs charge their batteries periodically from a charging station contained inside the casing connected to solar panel mounted on the surface of the moon.
Small obstacles are avoided (AI).
AUVs inspect the path
AUVs decide on totally new path in case of huge obstacles.

## Slide 21
An ROV was assembled by our team to perform as a main communication node .
It simulates the motion capability of the AUVs in the CONOPs.
Prototyping : Open ROV

## Slide 22
Open ROV Features
Control System
Beagle bone embedded
computer.
Controller board with an
Arduino microcontroller.

## Slide 23
Open ROV Features
Motion and Maneuvering System:
Three Brushless DC motors with Propellers.
Electronic Speed Controllers.

## Slide 24
Open ROV Features
Imaging System:
HD Camera with Live streaming video
LED lights
Laser for measuring
distance.

## Slide 25
The Submersibles Design
Three submersibles were designed and built by our team:
One mounted on the OpenROV (Main communication node ), while the other two are equipped with sensors and remain buoyant underwater collecting information and sending it back to the main communication node.

## Slide 26
The Submersibles Design
The design is simple and very low cost:
The main body of the submersibles is a cylindrical Acrylic tube.
Upper plate for the electronics
Chambers for placing weights( to achieve buoancy

## Slide 27
The Submersibles Design
The sensor hole
The switch hole
The antenna hole
Easy to build, and can do the job
Laser cutting was used to design the covers and the holes for sensors .

## Slide 28
The Submersibles Design
Submersibles hold:
The communication system components in the inside, as well as the external parts ( sensors, antennas and switches) .
Clear Acrylic material was chosen for the following reasons:
1) The ability to see the electronic circuit inside the submersibles.
2) The possibility of checking for any leakage.

## Slide 29
The Submersibles Design
External Parts
Antenna
Sensor
Switch
Pneumatic Fittings
Threaded to avoid leakage.
They form a sealed path for the sensors wires.
Used for pressure relief.

## Slide 30
Submersibles
Weight=1.96 Kg
Stones inside
The Submersibles Design

## Slide 31: Sensor mounted on Submersibles.
Waterproof temperature sensor
Pressure sensor

## Slide 32
Underwater RF Communication
Detailed and thorough research was conducted to explore the viability of RF communication underwater utilizing 1mw, 2.4 GHz Xbee modules.
Attenuation problems of RF led to minimal attention from scientists and engineers for usage in underwater applications.
Testing of RF communication showed promising results if it is to be used back to back with another communication system that allows for a longer range.

## Slide 33: Why Xbee
Low cost
Low Power
Easy to configure
Reliable
Supports large number of nodes

## Slide 34
First Test:
Objectives:
Find a correlation between the vertical/horizontal distance and the signal strength.
Study the effect of the antenna orientation on the signal strength.
Testing the communication system

## Slide 35
The following test involved three submersibles, two of which were stationary and the third was mounted on the OpenROV.
Main communication node sends specific commands to the two stationary submersibles to get the sensors readings.
Testing the communication system

## Slide 36
Testing the communication system
The tests involved having multiple testing points underwater.
Xbee modules were tested in different arrangements
across the points to get a relationship between depth,
distance and signal strength.
3 m
2 m

## Slide 37: Point to multi point Network
One Master Xbee module.
Two slave Xbee modules.
Inside each submersible there is a Xbee module connected to an Arduino.

## Slide 38: Pool test results
1mW Xbees were able to send data between each other when they are 35 cm apart underwater .
Using 100mW Xbee module will give a better communication range underwater.

## Slide 39
Conclusion
The viability of radio frequency for Europa mission
RF technology applied in underwater communications is an excellent candidate for providing higher data rates than those achieved by acoustic systems.

## Slide 40
Thank you