## Slide 1
Using Statistical Risk Assessment to Optimize the Design of Inflatable Membrane Structures in Low Earth Orbit
A. Chandra,
J. Thangavelautham
SpaceTREX Laboratory
School of Earth and Space Exploration
Arizona State University
A. Babuscia
Jet Propulsion Laboratory
California Institute of Technology

## Slide 2: Inflatable Antenna - Motivation
Large surface area
Low storage volume
High packing efficiency
Low weight
Low cost

## Slide 3: Challenges
Large uncertainties in outer space environment.
Complex interaction phenomenon.
Lack of understanding of underlying physics.
Robust inflatable design.
Adequate shape control.

## Slide 4: Objectives
Use statistical methods to design robust inflatable structures.
  Quantify the advantage of the design choices by assessing risk.
  Comparison in terms of architecture, membrane layer, sublimate properties.

## Slide 5: Objective
Micrometeoroid distribution data
Preliminary design
Definition of failure conditions Membrane Punctured
Critical leakage rate exceeded
Sensitivity Analysis
Optimization
Design Concepts
Robust Design

## Slide 6: Outline of procedure
Uncertainty quantification of space environment
Single bladder membrane
Multi-layer single bladder
Single-layer multi-bladder
Definition of failure conditions
Response functions and limit state analysis
Identification of critical design parameters – Sensitivity Analysis
Optimization and robustness studies
Design Options

## Slide 7: Space Environment
Micro-meteoroids and space debris
Mass and Velocity are the two parameters of primary interest

## Slide 8: Micrometeoroid mass and velocity distribution
Probability density function for micro-meteoroid mass and velocity

## Slide 9: Joint Probability distribution
Mass and velocity distributions assumed independent events
Joint mass and velocity probability distribution

## Slide 10: Outline of Analysis
Design parameters
material density ρ , vaporization heat ζ , thickness τ , no. of layers nl
Sublimate properties
molecular mass m,
Eq vapour pressure Pe
External environment
meteoroid mass mM, meteoroid velocity vM,
Temperature T
Response Function 1:
Penetration depth
Response Function 3:
Maximum gas leak rate
Theoretical failure probability
Critical Parameters
Propagation of uncertainty
Response Function 2:
Successive impacts
Limit State Surface

## Slide 11: Membrane Analysis – Definition of problem
Earth
h=370km
Cross sectional area facing earth is 1 m2
Tavg in LEO = 394K
Antenna

## Slide 12: Penetration depth
θ
τ
Layer 1
Layer 2
d
Successful penetration condition (Babuscia, 2013)
d

## Slide 13: Penetration depth
P-depth as a function of mass and velocity
P-depth as a function of no. of layers

## Slide 14: Successive Impact Deceleration
Correlation between deceleration, projectile mass and density
Hyper-velocity projectile deceleration (Pailer, 1980)

## Slide 15: Maximum Gas Leak Rate
Qin
Qout
Qout
Before Impact
After Repeated Impacts

## Slide 16: Maximum Gas Leak Rate
Max total leak area
Sublimate mobility
Condition for normal operation:

## Slide 17: Maximum Gas Leak Rate
Avg. exit flow-rate vs. membrane thickness
Total leak area vs. membrane thickness

## Slide 18: Theoretical probability of successful penetration
Probability of successful meteoroid penetration.

## Slide 19: Sensitivity Analysis
Sensitivity analysis of material properties

## Slide 20: Discussion
Yearly penetration probability converges to 65% above a membrane thickness of 2 mil
Penetration probability shows much higher sensitivity (about three times) to membrane thickness as compared to density and heat of vaporization

## Slide 21: Theoretical probability for max damage area
Probability of failure and total leakage area vs. thickness

## Slide 22: Volumetric Leak Rate
Volume and mass flow-rates for different sublimates

## Slide 23: Conclusions
Multilayer membrane better than multi-bladder system.
Volume rate of leak shows stronger sensitivity to molecular mobility than molecular mass
At Tavg= 394K, the following studied sublimates were found to perform the best:
benzoic acid
salicylic acid
o-methoxybenzoic acid

## Slide 24: Ongoing/further work
Inclusion of pre-stress into model
Promising areas: Diaphragm based actuation, Rigidization on command
Fig 12. Diaphragm based actuation (Ishimura, 2013)

## Slide 25: References
Spenvis database at www.spenvis.oma.be
Babuscia, Alessandra, et al. "CommCube 1 and 2: A CubeSat series of missions to enhance communication capabilities for CubeSat." Aerospace Conference, 2013 IEEE. IEEE, 2013.
Meteoroid Environment Model:-1969:(near Earth to Lunar Surface). Clearinghouse for Federal Scientific and Technical Information, 1969.
Pailer, N. "The penetration limit of thin films." Planetary and Space Science28.3 (1980): 321-331.