## Slide 1
Tools for Identifying OMSPA Opportunities in the DSN
Bruce E. MacNeal, Ph.D. and David P. Heckman, Ph.D.
Jet Propulsion Laboratory, California Institute of Technology
Interplanetary Small Satellite Conference
Santa Clara University
April 28, 2015
Copyright 2015. California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Identifying OMSPA Opportunities for the Demonstration
MRO
“Host” Spacecraft
Mars Odyssey
The Problem
Must find precise time periods (± 1 min) when:
MRO (host) is scheduled to be tracked by DSN
M010 is in the downlink tracking beam for MRO
MO10 is scheduled to be tracked by DSN on a different antenna (and is therefore actually transmitting)
MRO
Mars Odyssey
(MO10)
Approach
Correlation of Time Data from DSN schedules and user ephemeris files
  current, accurate tracking schedules
  good knowledge of the host and OMSPA spacecraft positions
In operational OMSPA, this link does not exist

## Slide 3: Solution Data Flow
SPS Database
(JPL)
Secure online database of current DSN tracking schedules
7-DSC
BIPS Tool
Latest tracking schedules for Host and OMSPA spacecraft
Simultaneous view periods (including occultation) for host and secondary spacecraft
Accurate start/stop times when three demonstration conditions are met
EXCEL file
EXCEL file
User ephemeris files
EXCEL VBA
MATLAB
ACCURATE location of spacecraft with time

## Slide 4: Beam Intercept Planning System (BIPS) Tool Startup Interface
MRO
“Host” Spacecraft
Mars Odyssey
BIPS contains several tools and solvers. Focus is on the animated beam-intercept analyzer and the 3-D scenario animator.
BIPS Startup Interface
Trajectory files loaded and scenario times set up here.
Other features include:
OMSPA statistical metrics
Orbit parameter plotting & trajectory file diagnostics
Interactive bar plotting of OMSPA metrics over time
Interactive coverage analyzer

## Slide 5: Beam Intercept Planning System (BIPS) MMS Example Of Tool Ops
MRO
“Host” Spacecraft
Mars Odyssey
In this MMS mission example, the “host” is the square (MMS 1). Colored dots represent the “opportunists” (MMS 2, 3, & 4.)
MMS 2, 3, & 4
Analyze with or without occultation effects. “Mars occultation” used for Mars-orbiting scenarios.
Set beamwidth value. Mousewheel scrolling changes it on the fly during animation for instant feedback!
The beamwidth is always the full circle diameter. Dot motions scale accordingly.
Axis pane shows white when the site has geometric visibility of the host.
Goldstone and Canberra simultaneous at 2015 OCT 18 02:59. No view from Madrid.
optional legend

## Slide 6: Beam Intercept Planning System (BIPS) MMS Example Mission Orbits
MRO
“Host” Spacecraft
Mars Odyssey
MMS uses highly eccentric orbits. The apparent angular spacing between the spacecraft grows large near perigee as viewed from the Earth’s surface. Animation is to-scale:
From Earth, the 4 spacecraft appear more spread-out here.
Plotted at this scale, the 4 spacecraft remain a tight group most of the time.

## Slide 7: Beam Intercept Planning System (BIPS) MMS Example Animation
MRO
“Host” Spacecraft
Mars Odyssey
The beam intercept motion animator applied to the MMS trajectories, with MMS 1 the “host” spacecraft. Beamwidth set to .242 degrees (S-Band, 34m antenna).

## Slide 8: OMSPA Demonstration: MRO and Mars Odyssey
MRO
“Host” Spacecraft
Mars Odyssey
MRO-Odyssey Orbits (Typical)
2015 APR 27 22:48 (UTC)
Direction to Earth
Odyssey (larger orbit)
MRO
At all times, 34m X-Band beam width is much larger than orbits, so the spacecraft are always “in beam”
But
Both spacecraft are periodically occluded by planet, depending on season
Occlusion is modeled in BIPS
Signal outage timing used to check accuracy

## Slide 9: 7-Day Schedule Cross-comparison Tool (7-DSC)
Results: Viable recording periods are identified to within one minute
Scheduled Host Tracking: MRO is MSPA’d with a third spacecraft, Mars Express
Scheduled Secondary Tracking: MO10 is tracked first in Madrid and then later at Goldstone
DOY-Date
hh:mm
Several 1.5-hour periods are available
Includes ≈ 9 min light time
With very fine time steps in BIPS, occultation times are accurate to about 10 seconds
1. MRO is tracked
3. MO10 is tracked on a separate antenna
SPS
SPS
BIPS
2. MRO is in beam and not occluded

## Slide 10: Conclusions and Recommendations
This approach provides recording windows for OMSPA with adequate accuracy
    Additional demonstrations needed with real cubesat users
Transition to “production” tools for Mission Users.
May involve:
    Online interfaces or tool executables
    Ephemeris file libraries