## Slide 1: Optical Communications for Deep Space Cubesats William Farr, Michael Ping, Michael Borden, Abhijit Biswas, Joseph Kovalik April-2016 Jet Propulsion Laboratory California Institute of Technology
Copyright 2012 California Institute of Technology. Government Sponsorship Acknowledged.
Copyright 2016 California Institute of Technology. Government Sponsorship Acknowledged.

## Slide 2: Why consider optical for cubesat telecom?
Versus RF telecommunications:
Freedom from spectrum regulations
  Limited spectral allocations limit data rates
  Long lead times for RF licenses
Fewer photons per bit required for direct detection than coherent detection
  Limit of 1.44 bits per photon for heterodyne
  Limit of 2.89 bits per photon for homodyne
  Unlimited bits per photon for direct detection
    17 bits per detected photon demonstrated at JPL
Smaller beam divergences from small transmitter apertures
  Higher Equivalent Isotropic Radiated Power (EIRP)
    Beam width = wavelength / antenna diameter
  In a well-designed system data rate is proportional to received power
Distance = 1
Brightness = 1
Distance = 2
Brightness = 1/4
Distance = 3
Brightness = 1/9

## Slide 3: Challenge of Deep Space Telecom
International Telecommunication Union definition of deep space for RF spectrum allocation purposes is 2 million km
  The moon is about 0.4 million km away
  The Earth-Sun L1 and L2 points are about 1.5 million km away
However, interplanetary distances are much larger than that
  Mars at typical closest range is 60 million km
    3.6 billion times larger signal loss than LEO
  Venus at typical closest range is 40 million km:
    1.6 billion times larger signal loss than LEO
Range (R) |  | Additional 1/R2 Loss Factor at 1 AU | Round-trip Light Time
LEO (1000 km) | 6.7x10-6 AU | 2.25x10-10 | 3.3 msec
GEO | .00024 AU | 17,400,000 | 0.24 secs
Moon | .0028 AU | 128,000 | 2.79 secs
Earth-Sun L2 | .01 AU | 10,000 | 10 secs
Deep Space | 1 AU | 1 | 16.6 mins

## Slide 4: Telecom under mass & power constraints
Capacity
  Is the maximum information rate achievable across a channel with arbitrarily small probability of error
  Represents the maximum mutual information between the channel input and channel output
  Examples of units of capacity are bits per second and bits per channel use
Example mass difference contours, (m(o) − m(r)) (kg), to achieve specified (R,C). Positive (negative) contours denote the kg gain of an RF (optical) terminal.
Although optical outperforms RF at high data rates, RF can outperform optical at large ranges and under high background conditions
  With photon counting direct detection the capacity goes as 1/R2 for Pr > 2 Pb ln M/M, and as 1/R4 for Pr < 2 Pb ln M/M
    with M as the peak-to-average power ratio of a symbol
  This also implies a maximum effective diameter for optical ground-based receivers
    Beyond this limit, doubling the antenna diameter only increases the achievable data rate by √2

## Slide 5: Optical Noise Rejection Challenge
When noise power dominates, capacity C scales as Ps2/Pb
  In this regime, data rate scales as 1/R4, and optical communications advantage from a narrower transmit beam are quickly lost
Background light in the optical receiver is traditionally rejected by either limiting the field-of-view or by optical bandpass filtering.
  An optical receiver located in the Earth’s atmosphere has a field-of-view limited by atmospheric turbulence, characterized by the Fried parameter r0, unless adaptive optics (complex, bulky, and costly) is utilized.
    r0 (few cm worst case, typically) represents the optical coherence length and the maximum receiver aperture diameter that can achieve a diffraction limited field of view.
  Narrowband optical interference filters with low transmission loss (< 1 dB) have tens of gigahertz bandwidths or greater.
    Alternate filter technologies such as atomic line filters and ring resonators have severe implementation challenges with respect to not only transmission loss, but also Doppler and/or effective field of view.

## Slide 6: Noise Rejection in the Time Domain
With photon-counting direct detection optical background can also be rejected in the time domain
  Time-of-arrival of every individual detected photon at the receiver is tagged with sub-nanosecond precision
Simplest scheme: polarization modulate a fixed-rate pulsed laser
  For instance, right-hand circular polarization to represent "0" and left-hand circular polarization to represent "1“
  Single "tone" of direct detection signal allows time-gated rejection of non-signal photons
  Signal can still be acquired under high loss conditions, then forward error correction coding gains applied

## Slide 7: Circular Polarization-Shift-Keying Terminals
Circular-Polarization-Shift-Keying (CirPolSK) laser transmitter is low complexity with small diameter aperture (few mm to few cm)
  Pulsed laser transform-limit bandwidth should be matched to receiver optical filter bandwidth
Background rejection performance of the Photon Counting Detector (PCD) CirPolSK receiver is set by optical filter bandwidth and timing resolution of photon arrivals
  New generation near-infrared PCD arrays with readout can operate with <200 ps timing uncertainty, > 50% efficiency, and near-zero intrinsic noise rates
Imaging Camera
DBS
λ/4
Photon Counting Array
< 2 nm BPF
Receiver Telescope
PBS
Gate Array Pre-Processor
Gate Array Pre-Processor
Data Demodulator
interfaces
Photon Counting Array
P-pol detector
S-pol detector
λ/4
Pulsed Fiber Laser
Data
Modulator
local interfaces
Beam Director
Polarization Modulator
Fiber Amplifier

## Slide 8: CubeSat PolSK Testbed
ND wheel
S-pol
detector
power meter
InGaAs camera
1550 nm LED
(flood illumination)
1550 nm 50:50 BS
1550 nm 90:10 BS
P-pol
detector
Seed Laser Tap
5 mW
Laser Amp Out
1 W
Polarization Modulator
Mode Locked Laser

## Slide 9: Initial PolSK Results
Measured performance > 8dB worse than theory due to poor polarization extinction ratio (PER) after the polarization modulator
  Obtained only 6 dB PER after modulator with mode locked laser pulses, versus measured 16.5 dB PER before modulator
  Measured 24 dB PER at modulator output with CW laser input
Established that low PER is the result of group velocity dispersion (GVD) in the polarization modulator
  The polarization modulator was implemented in a waveguide LiNbO3 technology with 5V Vπ switching voltage
  Confirmed issue by scanning a narrowband laser signal below/above 1560 nm and observing the amplitude of a single polarization
Modeled BER for ideal versus measured PER. Performance is degraded by >8 dB at 10-3 BER
Measured polarization modulation by scanning narrowband CW laser. Full polarization switch occurs with a frequency shift of 0.3 nm. Measured FWHM of mode-locked laser was 0.24 nm.

## Slide 10: Simplified PolSK Transmitter
Developed simplified laser transmitter with improved pulse rate flexibility by using “gain-switched” laser diodes (GS-LD)
  PolSK can be achieved by alignment of polarization axis of one laser to the “slow” axis of an output polarization maintaining fiber, and the other to the “fast” axis
  Simple non-linear transmission line circuit converts logic-level input pulses to sub-nanosecond, ~100 mA drive pulses with 10’s of mW average power dissipation
  Provides some redundancy in the event of a diode failure
Unlike a fixed rate mode-locked laser, can change pulse repetition frequency to accommodate different loss/background conditions
  Rate is set by external electronics
  Can also implement Pulse-Position Modulation (PPM) with demonstrated pulse rates from < 10 KHz to > 500 MHz
PM
coupler
Dispersion Compensation Fiber
Data
Gain-Switched Diode Lasers
Slow Axis
Fiber-based Amplifier
Laser Output
and
and
1
0
0
0
0
1
1
1
Clock
Fast Axis

## Slide 11: Improved PolSK Testbed
New testbed is distributed over lab, but allows more accurate emulation of expected link conditions and support use of state-of-the-art WSi superconducting single photon detectors
15 μm
Superconducting Nanowire Single Photon Detector (SNSPD). ~4 nm by ~100 nm superconducting wire biased just below the critical current. Absorbed photon creates a hot-spot: drop in current is read out as a voltage across a load resistor. Rise time is sub-ns, fall time is a few ns due to kinetic inductance. A meander placed in an optical cavity increases the detector area and probability of photon absorption. Arrays to 64 pixels and 320 µm diameter have been fabricated to date.
Gain switched laser diode. Version shown uses a electro-optic modulator driver to test wide range of pulse widths and repetition rates. <100 ps output pulse with Full Width Half Maximum spectral width of 0.1 nm at 35 dB extinction ratio.

## Slide 12: Negative SNR Photon Counting Acquisition
Demonstrated signal acquisition at -43.5 dB average signal power to average noise power ratio at 1550 nm using GS-LD at 1 MHz symbol rate and single pixel WSi SNSPD
  Signal acquisition window was 600 ps for a symbol period of 1000 ns
    32 dB background counts rejection
  Measured clock stability sufficient for100 ms integration
  Mean signal in acquisition window at 100 ms integration exceeds noise variance by 3.2 standard deviations.
Delay (ns)
Correlator output with 12.2 ps binning
Total Detected Photons
SNR
-43.5 dB
-41.7 dB
-38.9 dB
-35.6 dB
-30.1 dB
-16.9 dB
Detected signal window

## Slide 13: Estimated Error and Erasure Rates
99.8% Erasure
Fixed signal flux
Increasing background flux
ErasureRate + ErrorRate + CorrectRate = 1
High error and erasure rates will require combination of low-rate (<1/10) forward error correction codes along with spreading sequences
Case for previous slide with fixed signal and increasing background
  Error rate is a bound estimated from a single detector for a PolSK system

## Slide 14: Summary
Polarization modulation of a high peak-to-average power laser transmitter combined with photon counting direct detection can support deep space cubesat optical telecom links
  Pointing remains a dominant challenge
Acquisition in highly negative average signal power to average noise power regimes has been demonstrated
Demonstration of low-rate forward error correction codes and spreading sequences for this channel is the next step
  Protograph-based Raptor-like (PBRL) codes or punctured-node protograph-based Raptor-like (PN-PBRL) codes?
  Simple repeats or pseudo-noise spreading codes?
The work described here was performed at the Jet Propulsion Laboratory (JPL), California Institute of Technology under contract with the National Aeronautics and Space Administration (NASA)
5-cm TX dia,
1W @ 1550 nm
250 ps slot width
10 MHz repetition rate
5m RX dia. with SNSPD Array