## Slide 1: Role of small satellites in fast Mars transit
Darrin Taylor
Outer Space Colonization
outerspacecolonization@gmail.com

## Slide 2: Thank you
Thanks to Dr. Alessandra Babuscia
Thanks to the acceptance committee
Thanks for listeners patience

## Slide 3: Problem Statement
Space weather and radiation
Life-support
Hohmann Transfer- once every 26 months
Fast transit is expensive even for NASA. Fundamental limitation is economic.
5.2 km/s one way and 10.4 km/s round trip

## Slide 4: Fuel creates the cost
Space Shuttle Weight (kg)
Un-Fueled 342,000 kg
Fueled 1.7 million kg
Cargo to GTO 3810 kg
358kg fuel per 1kg cargo

## Slide 5: Rocket Equation
Each type of fuel has a fuel_const that tells us the ratio of initial mass/final mass needed to increase velocity 1 m/s
The total mass needed is then ship_mass * Fuel_const^(delta v in m/s)
Refueling n times changes this equation to n*ship_mass*Fuel_const^(delta v/n)
Refueling reduces the total fuel mass needed

## Slide 6: Specific Impulse (ISP)
Specific impulse is exhaust velocity/(9.8 m/s^2)
Rocket Fuel in vacuum: ISP of ~310 seconds
Ion Propulsion: ISP of 1,000-20,000 seconds
Cyclotron: 60% c is ISP of 18,000,000 seconds
Energy limits high ISP acceleration

## Slide 7: “Infinite” ISP options
Fuel and Energy only count if they are from Earth
Solar Sails use photons from the sun
Magnetic Sails and E-field sails use charged particles from sun
Traditional magnet uses Earth, Sun and Jupiter as the “fuel” via magnetic fields
Electrons fired into space may be able to bond with hydrogen via electronegativity and produce thrust without fuel from Earth
Photons create momentum from energy

## Slide 8: Solar Sail Ballpark numbers
Density 10 g/m^2
Peak force 8 uN/m^2
Peak thrust of 0.8 mN/kg for 100% solar sail by mass
If average thrust is 47.6% of peak this would give 1 km/s per month of delta v if 100% solar sail by mass.
A spacecraft would need 20-46% solar sail by mass to reach Mars in 26 months at 200 m/s per month
The volume of sail to move 1 Metric Ton spacecraft with 20% solar sail by mass requires 141 km by 141 km sail.

## Slide 9
Reusable Fuel

## Slide 10: Reusable ISP solves the fast transit issue
Consider a class of small interplanetary satellite named the “brick” with solar sail propulsion capable of infinite delta V at 200 m/s per month.
46% sail by mass to account for 1/r^2 at mars
Consider another spacecraft “Mother ship” attains its thrust by kinetically launching brick class spacecraft to 250m/s (900 km/hr) using a rail gun or a simple lasso type propulsion. 8 g with 400 m rail gun.
Brick spacecraft return to fueling points at 200 m/s per month after being launched and are reused for the next mission.
The kinetic thrust is Low ISP, the brick is Infinite ISP and the fuel is re-usable. The result is near infinite ISP capable of high acceleration with a low energy requirement.

## Slide 11: Saving 12.3% on fuel forever
Using 310 ISP a journey of 10.4 km/s requires 30.67 times mother ship dry weight. The return 5.2 km/s requires 5.54 times mother ship dry weight.
Launch 1 load of brick spacecraft equal to 30.67 times mother ship dry mass
Position the bricks at Mars where 30.67 times dry weight which is 5.54 times the return craft’s mass of 5.54 times the dry mass of “mother ship”.
ISP 25.5 with initial mass of 5.54 times the final mass provides 427 m/s of thrust.
Shorter 10.0 km/s trip only requires 26.89 times dry weight. Thus saving >12.3% fuel on every Mars return trip.
Breakeven for 1 brick load is ~7 missions and gives >12.3% reduction on future fuel
Breakeven if 2 brick loads is ~10 Missions and gives >15.9% reduction on future fuel

## Slide 12: Saving 100% fuel forever
ISP of 25.5 with initial mass of 1.5 times final mass gives >100m/s delta V
Refueling 52 times on the way to Mars with 0.5 times rest mass of mother ship at each stop provides 5.2 km/s delta V
This is one load of bricks equal to 26 times rest mass of “mother ship”.
The bricks would need to return to initial positions prior to return trip or we would need to send two loads of bricks in the initial step
Breakeven is 2 or 3 missions

## Slide 13: Saving 100% fueling twice
8 G acceleration 11 km rail gun gives 1300 m/s ISP 132.6 seconds
Breakeven for 1 load of bricks is 2 missions and saves >51.5% on all future fuel
Breakeven for 2 loads of bricks is 3 missions and saves >82% on all future fuel
Breakeven for 4 loads of bricks is 5 missions and saves >100% on all future fuel

## Slide 14: Conclusion
Kinetic Launch/Solar Sail Hybrid Reusable ISP can be competitive with 310 ISP fuel in terms of ISP and acceleration in the near future
If rendezvous is possible ~52 times on the way to Mars then no rocket fuel is needed for the round trip
Eliminating rocket fuel changes launched mass from 30.67 times dry mass to 1 times dry mass of mother ship reducing launch mass by 96.7%
Reusable ISP has much lower supplied energy requirements than ion propulsion allowing high acceleration and fast transit
Future fast transit at infinite seconds ISP is possible

## Slide 15: Questions
Contact info for Outer Space Colonization
outerspacecoloniztion@gmail.com
outerspacecoloniztion.com
Twitter @spacecolonize