## Slide 1: Development of the Lunar Polar Hydrogen Mapper Mission
Craig Hardgrove: Principal Investigator, Assistant Professor, ASU
ISSC 2018 – Caltech, Pasadena CA
May 7, 2018
Notes: Introduce as grad student/PSE

## Slide 2: LunaH-Map Mission Overview
NASA SMD SIMPLEx 2015 mission led by ASU
6U+ CubeSat form factor to launch on SLS EM-1
Science Objective: Map hydrogen enrichments within PSRs at the lunar south pole
Tech Objectives: Demonstrate neutron spectroscopy, deep space operations & propulsion from a small sat

## Slide 4: Neutron Detection Physics
Notes: Move to before LPNS/LEND
"hydrogen" -- hydrogen bound in water ice
Actually show the energy spectrum for FAN at altitude with 50 ppm and 500 ppm

## Slide 5: Polar Volatile Distributions from Neutron Spectroscopy
*Feldman et al., Science, 281, 1496, 1998
Neutron measurements are sensitive to bulk hydrogen distributions at 1 meter depth
Uncollimated neutron detector ‘footprints’ are approximately 1½ times orbital altitude
Lunar hydrogen abundances within PSRs broadly ranging from 200 ppm up to almost 40 wt% could be consistent with LPNS data depending on spatial distribution, extent of coverage, and burial depth [Lawrence et al 2006].
150 km2 pixels
Notes: LP – launch 1998, 30/100 km, 19 mos (12 @ 100, 7 @ 30)
LRO – launch 2009, 50/100km as low as 30

## Slide 6: Lunar Neutron Spectroscopy
Pixon-based reconstruction of LPNS data (Elphic et al 2007) reveals high WEH abundances in Cabeus (near 1 wt%) and lower abundances in Shoemaker, Haworth, and Faustini (~0.3 wt%)
Analysis of LEND data (Sanin et al 2017) reveals higher WEH abundances (~0.5 wt%) in south polar craters Shoemaker, Haworth, and Faustini
35 km2 pixels
15 km2 pixels
Notes: LP – launch 1998, 30/100 km, 19 mos (12 @ 100, 7 @ 30)
LRO – launch 2009, 50/100km as low as 30

## Slide 7: Lunar Neutron Spectroscopy
Pixon-based reconstruction of LPNS data (Elphic et al 2007) reveals high WEH abundances in Cabeus (near 1 wt%) and lower abundances in Shoemaker, Haworth, and Faustini (~0.3 wt%)
Analysis of LEND data (Sanin et al 2017) reveals higher WEH abundances (~0.5 wt%) in south polar craters Shoemaker, Haworth, and Faustini
Figure 1 Map of current day ice stability depth from Siegler et al [2015] as used in constraint map development
Notes: LP – launch 1998, 30/100 km, 19 mos (12 @ 100, 7 @ 30)
LRO – launch 2009, 50/100km as low as 30

## Slide 8: Neutron Measurements of the Moon
LunaH-Map measures only epithermal neutrons:
  Using a large (200 cm2) detector array
  To constrain abundance of hydrogen within PSRs
  To provide complementary data to LP-NS and LRO LEND
Low-altitude (< 20 km) uncollimated measurements of lunar neutrons can be used to:
  Determine the bulk hydrogen content and depth within PSRs (Diameter < ~35km)
These data can be used to constrain:
  Sources and sinks for polar volatiles
Notes: LP – launch 1998, 30/100 km, 19 mos (12 @ 100, 7 @ 30)
LRO – launch 2009, 50/100km as low as 30

## Slide 9: FAN Neutron Energy Spectrum
Increased hydrogen suppresses epithermal neutrons (E > 0.4 eV) and increases thermal neutrons (E < 0.4 eV)
LunaH-Map’s signal is the difference between dry epithermal count rate and enriched epithermal count rate

## Slide 10
Increased hydrogen suppresses epithermal neutrons (E > 0.4 eV) and increases thermal neutrons (E < 0.4 eV)
LunaH-Map’s signal is the difference between dry epithermal count rate and enriched epithermal count rate

## Slide 11
Increased hydrogen suppresses epithermal neutrons (E > 0.4 eV) and increases thermal neutrons (E < 0.4 eV)
LunaH-Map’s signal is the difference between dry epithermal count rate and enriched epithermal count rate

## Slide 12: Miniature Neutron Spectrometer
CLYC Module
Detector | 2x4 array of CLYC (elpasolite scintillator, Cs2LiYCl6:Ce) crystals, each crystal 4 cm x 6.3 cm x 2 cm
Dimensions | 25 cm x 10 cm x 8 cm
Mass | 3.3 kg
Power | 10W (min), 22W (max)
Data Acquisition | Counts binned every 1 sec
Instrument Housing and Electronics

## Slide 13: Mini-NS EDU
Test results from single EDU module exposed to Na-22 and AmBe
Notes: Yes add graphic

## Slide 14: Mini-NS Flight Unit and Calibration
Flight instrument chassis machined for fit checks in spacecraft EDU at ASU
Mini-NS Flight Unit delivery in early summer 2017
Mini-NS Flight Unit calibration at Los Alamos National Lab Neutron Free In-Air (NFIA) facility in late summer
Notes: Yes add graphic

## Slide 15: Trajectory Design
1
2
3
Period | 4.76 hour
Aposelene Altitude | 3150 km
Periselene Altitude | RAAN dependent 15-25 km
Inclination | 90°
Argument of Periselene | 273.5°
Genova, A. L. and Dunham, D. W. (2017) 27th AAS/AIAA Space Flight Mechanics Meeting 17-456.

## Slide 16: Science Phase
Period | 4.76 hour
Aposelene Altitude | 3150 km
Periselene Altitude | RAAN dependent 15-25 km
Inclination | 90°
Argument of Periselene | 273.5°
Genova, A. L. and Dunham, D. W. (2017) 27th AAS/AIAA Space Flight Mechanics Meeting 17-456.

## Slide 17: Science Phase

## Slide 18: LunaH-Map Sensitivity
Enrichments of 600 ppm +/- 120 ppm WEH are detectable for ~94% of the surface poleward of 85°S in spatial bins of 15km x 15km.
Notes: Graphic from LPSC microsymposium - LP SNR compared to ours
Maybe show count/s over mission duration

## Slide 19: South Polar Volatile Mapping
Simulations of maps made from 15x3150km science orbit. Basemap combines LEND high H regions (Sanin et al., 2017) and the Shackleton enrichment from pixon-reconstructed LPNS data (Elphic et al, 2007) to illustrate the type of map LunaH-Map will be able to create.
C
Sh
H
S

## Slide 20: LunaH-Map Spacecraft
BIT-3 Thruster
XB1-50 /
Star Tracker
Primary Coarse
Sun Sensor
Single Axis
Solar Array Drive
LGA
Separation
Connector
Mini-NS
Instrument
Solar Array
Hold Down
Arms
LGA
Coarse Sun Sensor
1:1 3D Printed Model of LunaH-Map Flight System

## Slide 21: Spacecraft Specs
Dimensions: (stowed) | 10x20x30cm
Mass | 14 kg
Power | 90W BOL 56W-hr Battery
Propulsion | Busek BIT-3 Ion Thruster
Comm. | JPL Iris Deep Space Transponder
C&DH / GN&C | BCT XB1-50

## Slide 22: Propulsion
Busek BIT-3 ion thruster
Iodine propellant
10° gimbal for momentum management

## Slide 23: Propulsion
Busek BIT-3 ion thruster
Iodine propellant
10° gimbal for momentum management

## Slide 24: PC1 – Instrument Qualification
An integration time of 8 hours enables LunaH-Map to measure the >10MeV protons (high energy bin) to an uncertainty of <1%.
During first lunar flyby, LunaH-Map will observe the lunar neutron count rate of ~3.15 cps at the PC-1 flyby altitude of ~2800 km.
LunaH-Map is below 3000 km altitude for >30 minutes. The predicted epithermal neutron count rate of 3.15 cps can be measured to +/-0.04 cps.
Demonstrate Mini-NS operation in the lunar environment
Notes: Double check TRL-9

## Slide 25: Day in the Life - Science
Tracking/Communication
Tracking/Communication
Eclipse (beta angle dependent) – no operations
Statistical aposelene manuever (every 3-5 days)
Mini-NS active ~30 min centered around periselene
Notes: Shorten blue bar....
Highlight stuff

## Slide 26: Mission/Science Operations
Co-located in ASU’s shared operations facility
JPL AMMOS/AMPCS for uplink and downlink
Science/instrument ops heritage from MER, LROC, and MSL
Science/instrument ops development coincident with Mars 2020 and Psyche missions

## Slide 27: Road to Launch
Critical Design Review – Completed June 29, 2017
Phase 2 Safety Review – August 8, 2017
Enter Assembly, Integration, and Test – Q4 2017
  AI&T Review/Workshop with review board
Launch – SLS EM-1, December 2019
LunaH-Map Program Milestones to Date |  | 
IAA | 11 December 2015 | Δ-IAA REQUIRED
Δ-IAA | 24 February 2016 | PASSED with RFAs
SRR | 8 April 2016 | PASSED with RFAs
I-PDR | 9 June 2016 | PASSED with RFAs
Phase 1 SR | 21 June 2016 | PASSED
M-PDR | 25 July 2016 | PASSED with RFAs
CDR | 29 June 2017 | COMPLETED
Phase 2 SR | 11 Nov 2017 | COMPLETED
Integration Workshop | 8 Dec 2017 | COMPLETED
Review Board Members: Dr. Andrew Klesh, Jet Propulsion Laboratory (Review Board Chair), Dr. Thomas Werne, JPL, Dr. Travis Imken, JPL, Dr. Juergen Mueller, JPL, Dr. Eric Gustafson, JPL, Dr. Thomas Prettyman, Planetary Sciences Institute, Dr. James Bell, Arizona State University, Dr. Jordi Puig-Suari, California Polytechnic State University, Richard Elphic, NASA Ames.

## Slide 28
Twitter: @lunahmap
lunahmap.asu.edu/foldyourown_lunahmap.pdf