## Slide 1: Near Earth Asteroid (NEA) Scout
Les Johnson, Tiffany Lockett, & Alex Few
NASA George C. Marshall Space Flight Center
Julie Castillo-Rogez
  NASA Jet Propulsion Laboratory

## Slide 2: Solar Sail Missions Flown (as of April 11, 2018)
NanoSail-D (2010)
NASA
Earth Orbit
Deployment Only
3U CubeSat
10 m2
IKAROS (2010)
JAXA
Interplanetary
Full Flight
315 kg Smallsat
196 m2
InflateSail (2017)
EU/Univ. of Surrey
Earth Orbit
Deployment Only
3U CubeSat
10 m2
LightSail-1 (2015)
The Planetary Society
Earth Orbit
Deployment Only
3U CubeSat
32 m2
CanX-7 (2016)
Canada
Earth Orbit
Deployment Only
3U CubeSat
<10 m2

## Slide 3: Planned Solar Sail Missions (as of April 11, 2018)
CU Aerospace (2018)
Univ. Illinois / NASA
Earth Orbit
Full Flight
3U CubeSat
20 m2
LightSail-2 (2018)
The Planetary Society
Earth Orbit
Full Flight
3U CubeSat
32 m2
Near Earth Asteroid Scout (2019) NASA
Interplanetary
Full Flight
6U CubeSat
86 m2

## Slide 4: Near Earth Asteroid Scout
The Near Earth Asteroid Scout Will
Image/characterize a NEA during a slow flyby
Demonstrate a low cost asteroid reconnaissance capability
Key Spacecraft & Mission Parameters
6U cubesat (20cm X 10cm X 30 cm)
~86 m2 solar sail propulsion system
Manifested for launch on the Space Launch System (EM-1/2019)
1 AU maximum distance from Earth
Leverages: combined experiences of MSFC and JPL with support from GSFC, JSC, & LaRC
Target Reconnaissance with medium field imaging
Shape, spin, and local environment
Close Proximity Imaging
Local scale morphology, terrain properties, landing site survey

## Slide 5: NEA Scout Goals & Objectives
Design, develop, integrate and operate a spacecraft for the purpose of demonstrating a low cost reconnaissance capability
Enable asteroids as potential destinations for human exploration
Characterize a candidate NEA with an imager to address key SKG’s
    “Robotic exploration is the principal method we use to explore the solar system, and is an essential precursor to human exploration of space.”
SMD Strategic Goals/Objectives
(Strategic Goal 1, Objective 1.5)
    “Precursor robotics, robotic missions that investigate candidate destinations and provide vital information to prepare for human explorers, will lay the groundwork for humans to achieve new milestones in deep space.”
HEOMD/AES Strategic Goals/Objectives
(Strategic Goal 1, Objective 1.1)

## Slide 6: Baseline Target Asteroid: 1991 VG
Diameter ~ 5 -12 meters
Rotation period between a few minutes and less than 1 hour
Unlikely to have a companion
Unlikely to retain an exosphere or dust cloud
  Solar radiation pressure sweeps dust on timescales of hours or day
Near-Earth Asteroid 1991VG (marked with green lines) on 2017 May 30. This is a composite of several images obtained with the ESO VLT. The images have been combined in 7 stacks tracking the position of the asteroid, resulting in the object appearing as 7 dots as it moves in front of the background stars. The stars appear trailed due to the motion of the asteroid during each series. Credit Hainaut/Micheli/Koschny

## Slide 7: Near Earth Asteroid Scout Mission Overview
JPL
Target Detection and Approach:
50K km, Light source observation
SKGs: Ephemeris determination and composition assessment
Close Proximity Science
High-resolution imaging,
10 /px over >30% surface
SKGs: Local morphology Regolith properties
NEA Reconnaissance
<100 km distance at encounter
50 cm/px resolution over 80% surface
SKGs: volume, global shape, spin properties, local environment
Reference
stars
Target
Notes: Update background pic with new one. Update camera pic. Took science pieces from design iteration review charts for science.

## Slide 8
Flight System Overview
Rad Tolerant Avionics
(JPL)
Star Tracker
(BCT)
Iris 2.0 Transponder
(JPL)
TRAC Boom Assembly
(MSFC)
Solar Sail - Stowed
(MSFC)
RCS
(VACCO)
NEA Imager
(JPL)
RWA
(BCT)
LGA
(JPL)
18650 Lithium Batteries
(SDL/Panasonic)
Solar Panels & MGA
(BCT & MMA)
Sun Sensors
(BCT)
Translating Table
(MSFC)
A fully functional planetary spacecraft in a shoebox
Payload | Context Camera
Mechanical& Structure | “6U” CubeSat form factor <14 kg total launch mass Modular flight system concept
Propulsion | ~86 m2 aluminized CP-1 solar sail (based on NanoSail-D2)
Avionics | Radiation tolerant architecture
Electrical Power System | Trifold deployable solar arrays with GaAs cells (~51.2 W EOL at 1 AU solar distance) 6.2 Ah Battery 10 -12.3 V unregulated, 5 V/3.5 V regulated
Telecom | JPL Iris 2.0 X-Band Transponder; 4 W RF output power supports doppler, ranging, and D-DOR 2 pairs of INSPIRE-heritage LGAs (RX/TX) 8x8 element microstrip array MGA (TX); ~1 kbps to 34m DSN at 0.8 AU
Attitude Control System | 15 mNm-s (x3) & 100 mNm-s RWAs Active mass translation system VACCO R-236fa (refrigerant gas) ‘warm gas’ RCS system Nano StarTracker, Coarse Sun Sensors & MEMS IMU for attitude determination

## Slide 9: NEA Scout Approximate Scale
Deployed Solar Sail
6U Stowed Flight System
Human
School Bus
Deployed Solar Sail
Folded, spooled and packaged in here

## Slide 10: Active Mass Translation (AMT) Overview
Problems and Challenges
  NEA Scout’s center of mass (CM) and center of pressure (CP) are not collinear with the estimated thrust vector. This creates a disturbance torque. Furthermore, the CP is fore of the CM, creating a naturally unstable vehicle and necessitating an active control mechanism.
  Little mass and volume available. This challenge is compounded by the vehicle’s total mass (14 kg) and volume (6 Liters) requirement. The AMT was originally given 250 grams and a volume of 226 x 105 x 17 mm (400 cc). This volume and mass will include: an X-Y translation stage, thermal controls, limit switches, and a wire harness. The wire harness must pass through the AMT and survive exposure to deep space environments.
CP
CM
Thrust
Disturbance Torque
KEY

## Slide 11: AMT Overview
Trimmed State
Nominal State
AMT
CP
CM
Thrust
Disturbance Torque
KEY

## Slide 12: On Schedule to Deliver Spacecraft

## Slide 13: Assembly, Integration, and Test (AI&T) Overview
Solar Sail Assembly
MSFC
Upper Assembly
Lower Assembly
MSFC
Flight System Integrated
Functional and Environmental Testing
MSFC
Integrate Dispenser & Flight System & Acceptance Test
SHIP
SHIP
Install into MSA
SHIP/HANDOVER
KSC
KSC
Dispenser Vendor
SHIP
DSN Compatibility Test / ETE Testing
JPL

## Slide 14
Concept of Operations Overview

## Slide 15: Questions?

## Slide 16
Backup Information

## Slide 17: The Need for CM/CP Adjustment
The AMT will move one portion of the NEA Scout relative to the other. This translation of mass will alter the inertial properties of the vehicle and align the CP and CM

## Slide 18: AMT Overview
2X Stainless Lead Screws
4X Steel Rail and Carriages
Aluminum Chassis
Tape Heater
2X Limit Switch
* Stepper Motors are housed inside of the aluminum block and are not readily visible
4X Bearings
2X Stepper Motors*
Y
X
CAPABILITIES
Translation: 160 X 68 mm (X & Y respectively)
Speed: 0.3 and 0.1 mm/s (X & Y respectively)
Precision: 0.01 mm
Volume: 220 x 99 x 14 mm (300 cc)
Mass: < 350 grams (including control board)
Harness Feedthrough Volume
Current Design State