## Slide 1: ASPECT
Cubesat Instrumentation Concept for Asteroid Exploration: The ASPECT Platform
Antti Näsilä
VTT Technical Research Centre of Finland Ltd
Notes: 2. Otsikkosivu/aloitussivu

## Slide 2: Fabry-Perot Interferometer
Two parallel mirrors separated by a cavity
Acts as an optical resonator
Can be used as a tunable passband filter
m=1,2,3,…
m
m+1

## Slide 3: Fabry-Perot Interferometer

## Slide 4: FPI platforms and examples of realized filters
0,2
0,3
µm
0,4
0,6
0,8
1
2
3
4
5
6
7
8
10
11
12
13
14
Visible
UV
NIR
SWIR
LWIR
MWIR
CMOS & CCD Image Sensors
InGaAs
InSb
MCT
PbSe
Material science
Biology
Medical, Anticounterfeit,
Space, Remote sensing, PoC
Pharma,
Food,
Agriculture
Gases,
Plastics
Minerals
Minerals
Forestry
PIEZO
MEMS
Metallic mirrors
Dielectric mirrors
Existing MEMS FPI’s
λ
MEMS process
platforms:
ALD MFPI
PolySi-SiN/SiO2 MFPI
Si-air MFPI
Metal MFPI

## Slide 5: Different mirror solutions
Al2O3 (5 nm)
Ag (VIS 45 nm, NIR 20 nm)
SiO2 (50 nm)
Fused silica substrate
Poly-Si (λ/4)
SiO2 (λ/4)
Poly-Si (λ/4)
SiO2 (λ/4)
Poly-Si (λ/4)
Fused silica substrate
SWIR mirror structure
Bragg mirror, optimized for a certain wavelength
VIS/NIR mirror structure
Simple metallic mirror
Not to scale

## Slide 6: First ASPECT concept
Developed originally for ESA’s Asteroid Impact Mission during 2015 – 2017
Originally for a 3U cubesat
1U envelope for the instrument
2 spectral imagers measuring from 500 nm to 1600 nm
1 spectrometer measuring from 1600 nm to 2500 nm
Optics model for the VIS channel
Optics model for the SWIR spectrometer

## Slide 7: Example: First images from Aalto-1 Spectral Imager
RGB image
False color image: red pixels show 711 nm, green pixels 536 nm, blue pixels 509 nm.
Spectral images

## Slide 8: Example: First images from Aalto-1 Spectral Imager
RGB image
July 5, 2017
Spectral image (509 nm, 536 nm, 711 nm)
August 3, 2017
Calibration spectrum
September 5, 2017

## Slide 9: Next images from Aalto-1 Spectral Imager
November 21, 2017

## Slide 10: Example: NIR Spectral Imager for nanosatellites
NIR spectral imager weighing less than 500 g
Measuring from 900 nm to 1400 nm (1000 nm – 1600 nm also possible)
To be launched in Q2-Q3/2018 on the Reaktor Hello World Satellite

## Slide 11: 3 um concept
Si-SiO2 Bragg mirrors on ZnSe substrate
Single instrument measuring from 2.5 um to 4.0 um
Single point detectors enable low cost devices
Very compact instrument: ~0.25 U
Spectral resolution ~20 – 30 nm
Optical apertures up to 25 mm
The same concept can also be used with imaging detectors if available for use
High SNR!