## Slide 1
Aman Chandra
PhD student,
Space and Terrestrial Robotic Exploration Laboratory
Department of Aerospace and Mechanical Engineering
University of Arizona, Tucson
Structurally reconfigurable modular inflatable reflectors
Notes: 1

## Slide 2: Outline
Introduction
Motivation
Challenges
Objectives
Approach
Results and Discussions
Further Work
Conclusion
References

## Slide 3: Introduction – High gain antennas (HGA)
JPL’s Ka Band reflector (Chahat et al., 2018)
Include reflectors and reflect-arrays.
Directional radiation minimizes losses.
Enable high data-rate communication.

## Slide 4: Introduction - Reflectors
Larger surface area to volume ratio among HGA’s.
Better packing efficiency among deployable HGA’s.
Antenna Technology | Surface Area (m2) | Mass (kg) | Stowed Volume (m3) | Packing efficiency
Deployable parabolic reflectors | 1.0 | 1.5-2 | 0.04 | 5:1
Foldable reflect-arrays | 1.0 | 0.6 – 0.8 | 0.05 | 3:1
Comparison of HGA technologies for 1 m2 reflective surface area (Chandra, 2015)

## Slide 5: Introduction - reconfiguration
Reflector curvatures can be reconfigured.
Reconfiguration enhances reflector performance.
Can be used to correct shape errors.
Can assist with antenna fine pointing.

## Slide 6: Motivation
Enhance deep space CubeSat communications by:
High gain reflector design.
Co-operative reflector systems between CubeSats.
Frequency band | Minimum required gain (dBi)
X - band | 28
Ka - band | 42
Interplanetary mission reflector gain requirements.

## Slide 7: Related Work
Reconfiguration has been attempted using:
Piezo based linear actuators. (Datahvili, 2017)
Shape memory alloys. (Kalra et al., 2018)
Control points on surface
Point force application

## Slide 8: Challenges
Mechanical actuators are bulky.
Large number of actuators are required.
Can be mechanically complex.
Metallic actuator parts cause signal interference.
(Datashvili et al., 2010)

## Slide 9: Objectives
To develop a pneumatic actuation mechanism.
To design a reflector based on this mechanism.
Numerically analyze structural behavior.
Develop a reflector design using the mechanism.

## Slide 10
Approach

## Slide 11: Chemical sublimate gas generation
Sublimates undergo solid to gas transformation.
Pressure of gas able to inflate a membrane in space.
Applied heat of sublimation
Solid to gas transformation

## Slide 12: Sublimate gas pressure control
Pressure controlled by ambient pressure and temperature shown. (Babuscia et al., 2014)
At constant temperature, pressure reaches equilibrium

## Slide 13: Sublimate gas pressure measurement
Benzoic acid gas pressures at room temperature vacuum (Chandra, 2015)
Sublimate benzoic acid yields a final stable pressure of 0.38 Pa at room temperature.

## Slide 14: Sublimate gas membrane inflation

## Slide 15: Pneumatic actuator
Sublimate incorporated into a Mylar membrane unit to form actuator.
P1, T1
P2, T2
Mylar membrane changing pressure state with temperature

## Slide 16: Actuation stroke length
Numerical analysis carried out using LS-Dyna.
Stiffness and deflection behavior simulated.
P1
P2
Results extracted at central circumference
Stroke length

## Slide 17: Numerical Results
Force and stroke length during inflation

## Slide 18: Composite inflatable reflector
Multiple units to form reflector structure (Chandra et al., 2018)
Reflective membrane
inflatable actuator layer
Backing layer

## Slide 19: Composite inflatable reflector
Inflatable units can be used to modulate f/d ratios.
Patterned inflation can be used to obtain desired geometry
d
f
focus

## Slide 20: Further Work
Radiation pattern for 1 m reflector
Work underway to understand how focal length/ distance ratios change with actuation.
Radiation pattern analysis would be done for each case.

## Slide 21: Conclusion
A pneumatic actuation mechanism has been developed.
Force and stroke length data show actuation feasibility.
A methodology towards application to parabolic reflectors has been proposed.

## Slide 22: Thank you

## Slide 23: References
Chahat, Nacer, et al. "The Deep-Space Network Telecommunication CubeSat Antenna: Using the deployable Ka-band mesh reflector antenna." IEEE Antennas and Propagation Magazine 59.2 (2017): 31-38.
Chandra, Aman. Inflatable Parabolic Reflectors for Small Satellite Communication. Diss. Arizona State University, 2015.
Datashvili, Leri, et al. Enabling Technologies and Architectures at LSS GmbH for European Large Deployable and Reconfigurable Reflector Antennas. Deutsche Gesellschaft für Luft-und Raumfahrt-Lilienthal-Oberth eV, 2017.
Boyarchuk, Mikhail Viktorovich, et al. "Investigation Testing of Structural Members of Large-sized Reconfigurable Spacecraft Antenna Reflectors." International Journal of Applied Engineering Research 12.8 (2017): 1529-1535.

## Slide 24: References
Kalra, Sahil, et al. "Smart reconfigurable parabolic space antenna for variable electromagnetic patterns." IOP Conference Series: Materials Science and Engineering. Vol. 311. No. 1. IOP Publishing, 2018.
Babuscia, Alessandra, et al. "Inflatable antenna for CubeSat: A new spherical design for increased X-band gain." Aerospace Conference, 2017 IEEE. IEEE, 2017.
Aman, Chandra, et al. “Modular inflatable space structures." Aerospace Conference, 2018 IEEE. IEEE, 2018.
Datashvili, Leri, et al. Enabling Technologies and Architectures at LSS GmbH for European Large Deployable and Reconfigurable Reflector Antennas. Deutsche Gesellschaft für Luft-und Raumfahrt-Lilienthal-Oberth eV, 2017