## Slide 1
Greg Wilburn1, Leonard Vance1
1 Space and Terrestrial Robotic Exploration (Space TREx) Lab
Aerospace and Mechanical Engineering, University of Arizona
4/30/2019
Interplanetary Small Satellite Conference
San Luis Obispo, CA
Towards Development and Testing of an Engineering Model for an Asteroid Hopping Robot
Notes: 1

## Slide 2: Introduction
Why asteroid exploration is important
Surface mobility and AMIGO Overview
Engineering Model Testing
Sublimate Propulsion
Nozzle geometry design
MEMS Fabrication Methods

## Slide 3
Motivation: Asteroid Exploration

## Slide 4: Asteroid Exploration
Planetary Science Decadal Survey highlights key questions asteroids can answer
In-situ analysis required for in-depth analysis on internal structure, surface regolith, thermal effects, etc.
Figure: Bennu Arrival from OSIRIS-Rex
(Credit: NASA, Goddard, University of Arizona)

## Slide 5: Asteroid Surface Exploration
Geohistory
Security/Deflection
ISRU
Complements flyby and orbital observation science.
Short, focused, high-risk, high-return…

## Slide 6: Asteroid Surface Hopping
Collect science data at multiple locations
Mobility through:
  Roving
  Internal actuation
  Mechanical systems
  Thrusting
Figure: Surface of Ryugu from MINERVA-II 1B (Credit: JAXA, University of Tokyo et al.)

## Slide 7: AMIGO ConOps

## Slide 8: AMIGO Mission Concept
Stereo imaging
Geologic imaging
Thermal fatigue
Seismic sensing
Electric field measurements
Complements orbital science and flyby missions
Figure: AMIGO Overview

## Slide 9: AMIGO Internals
Housing for:
  Computer/ power system
  Inflatable deployment
  Science instruments
  Propulsion components
Figure: AMIGO Internals

## Slide 10
Engineering Model

## Slide 11: Components
Parallel effort to develop low cost 1U cubesat for general use
Avionics: ¼ U
  Computer: Teensy Board
  Batteries: Li-Ion 18650 (~17 WHr)
Propulsion: ¼ U
Inflatable structure: ¼ U
Mock science instruments: ¼ U
Figure: AMIGO Internals

## Slide 12: Testing
Microgravity simulation: helium filled pseudo-inflatable
Simulant regolith to understand surface interaction
Test path planning algorithm from top mounted camera
Use micro-thrusters for hopping

## Slide 13
Sublimate Micro-Propulsion

## Slide 14: Sublimate Propulsion
Extension of cold gas systems
Usable with low-cost, readily-available chemicals
Store propellant as solid – higher storage density
Control chamber pressure by heating elements
Lower pressure than conventional cold gas
Figure: Sublimate Propulsion System Block Diagram

## Slide 15: Thruster Chip
Bottom mounted MEMS thruster chip for hopping
x-y control authority
Discretized micro-nozzles allow three saturation modes by individual actuation
Figure: Thruster Chip

## Slide 16: Sublimate Propellant Candidates

## Slide 17
Nozzle Geometry Design

## Slide 18: Algorithm Flow
Determine required thrust coefficient from required thrust:
Determine viscous loss thrust coefficient through derived throat and wall Reynold’s number
Determine discharge coefficient

## Slide 19: Algorithm Flow
Determine required isentropic thrust coefficient and thrust:
Find nozzle geometry to produce such thrust from corrected mass flow rate and exhaust velocity
Iterate through combinations of throat diameter and expansion ratio

## Slide 21
MEMS Fabrication

## Slide 22: Etching Techniques
Dry etching: deep reactive ion etching
Wet etching:
  Anisotropic: Si reaction with KOH
  Isotropic: Si reaction with HF and HNO3
Figure: Anisotropic vs Isotropic Etch

## Slide 23: DRIE
Step 1: polymer deposition
Step 2: ion bombardment to expose bottom face
Step 3: isotropic etch
Decrease etch time each step to make conical geometry
Very expensive
Figure: DRIE Etching Process

## Slide 24: Anisotropic Etching
Exploit crystal structure to etch along certain lattices
Easily creates quasi-conical nozzles
Semi-vertex angle fixed by crystal plane etched
Figure: Anisotropic Etch of Silicon <100> Face
Figure: CFD of 35° Nozzle

## Slide 25: Isotropic Etching
Etch along each crystal face at equal rates
Better for larger, simple geometries
Not limited to quasi-3D shapes
Downside: requires nitride deposition, not readily available at UA facilities

## Slide 26: Micro-Milling
Micron-level precision
Able to produce rounded nozzle throats to mitigate separation
Most feasible machining option for the simple conical nozzles

## Slide 27: Conclusion
Showed reasoning behind an asteroid surface hopping robot
Benefits of sublimate-stored, cold gas thrusting system shown
Method for designing micro-nozzles has been developed
Fabrication methods explored based on traditional MEMS manufacturing

## Slide 28: Thank You
Acknowledgement: Dr. Eniko Enikov