## Slide 1
­­Near Earth Asteroid Scout
(NEA Scout) Science Concept of Operations Utilizing Onboard Data Analysis
Jack Lightholder
David R. Thompson
Julie Castillo-Rogez
Christophe Basset
Jet Propulsion Laboratory,
California Institute of Technology
4800 Oak Grove Dr.
Pasadena, CA 91109
626-710-3246
Jack.a.lightholder@jpl.nasa.gov
This research was carried out by the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.

## Slide 2
The Agile Science Paradigm
Data Acquisition
Data Analysis
Spacecraft Points/ Slews
Re-Plan
Analysis results in new imaging goal(s)
Plan Execution
  Analyze data acquired onboard spacecraft and respond based on analysis
Potential volatiles on Ceres

## Slide 3
Near Earth Asteroid Scout
  GOALS
  Characterize one candidate NEA with an imager to address key Strategic Knowledge Gaps
  Demonstrates low cost capability for HEOMD for NEA detection and reconnaissance
6
MSFC/JPL/LaRC/JSC/GSFC/NASA
  Measurements: NEA volume, spin and orbital properties, address key physical and regolith mechanical SKGs.

## Slide 4
NEAScout Concept of Operations

## Slide 5: Imaging Challenges
Reference stars
Target
Target Detection and Approach
Ephemeris determination
Medium Field Imaging
Shape, spin, and local environment
Close Proximity Imaging
Local scale morphology, terrain properties
Target Position Uncertainty
Limited downlinks of 30 minutes at 1 Kbps
7
Spacecraft Pointing and Camera Limitations
Short Flyby Time
(<30 minutes)
Uncertain Environment
Short Time at Closest Approach (<10 minutes)
Data Value Analysis and Sorting

## Slide 6: Mission Operations Flexibility
Flat field / Radiometric calibration
Dark Current Subtraction
Calibration
Downlink
“Quick-Look” Data Products
Prioritize Data for Downlink
Follow-Up Actions
Cosmic Ray Removal
Target Detection
Reference Star Detection
Onboard Feature Detection

## Slide 7
Instrument Calibration
Notes: https://independentaustralia.net/environment/environment-display/the-mystery-of-earth-companion-1991-vg,7702
Image via: http://www.cosmosup.com/

## Slide 8: NEA Scout Camera
Sensor Capabilities | 
Type | 20M pixel CMOS image sensor
Useful array size | 3840 x 3840 pixels
Pixel size | 6.4µm2
Full well | 15,000e-
Dark noise | 8e- RMS
Windowing | Y-direction only
Shutter | Global
Color | Monochrome (with microlenses)
Quantization | 12-bit per pixel
Electrical interface | 
Physical | LVDS
Protocol | Spacewire RMAP
Power | < 3 Watts
Memory | 64Mbits
FPGA | Microsemi Rad-tolerant ProASIC3
Camera Specifications | 
Mass | 390g
Volume | 63mm x 63mm x 71mm
Operating temperature | -25C to +50C
Survival temperature | -35C to +70C
Optics | 27° FOV, f/2.8, 50.2mm iFOV=0.09mrad/ pix
NEA Scout flight camera, based on Orbital Carbon Observatory 3 (OCO-3) mission context camera.

## Slide 9: Onboard Image Calibration
Onboard L1 calibration including:
  Flat field normalization
  Dark current subtraction
  Bad pixel mask application
Lab calibration products dynamically applied based on camera temperature at acquisition.
Linear interpolation applied between calibration products bounding the raw image temperature.
Ability to apply flat fields and dark current maps acquired in flight.
Laboratory calibration trends, across camera allowable flight temperatures
Calibration laboratory setup

## Slide 10
Target Detection
Notes: https://independentaustralia.net/environment/environment-display/the-mystery-of-earth-companion-1991-vg,7702
Image via: http://www.cosmosup.com/

## Slide 11
Rosetta OSIRIS Narrow Angle Camera Detection of 2867 Steins
Raw Data is Messy

## Slide 12
Rosetta OSIRIS Narrow Angle Camera Detection of 2867 Steins
Raw Data is Messy

## Slide 13: Cleaning Up the Noise
Row Shift
Column Shift
Reference stars
Target
Onboard co-registration of images improves SNR and reduces downlink requirements
Sub-windowing around reference stars makes the problem computationally reasonable for flight hardware.
[Thompson et al. 2015]

## Slide 14
13
Stepwise processing keeps the necessary memory small.
Computation is additionally constrained by onboard memory limitations.
< 100 MB RAM
Pick Data to Co-register
Process in Batches of 3
Place Temporal Median on Output Stack
Output Image
Temporal Median Values
Images Being Processed
Raw Image Stack
Before
After
[Thompson et al. 2015]

## Slide 15
6
Cleaning Up the Noise
Increase signal to noise without long exposure imaging.
Decreases spacecraft pointing requirements.
Removal of transient artifacts, such as cosmic rays.

## Slide 16: Processed Data
Rosetta OSIRIS Narrow Angle Camera Detection of 2867 Steins

## Slide 17
17
Identify Targets with Onboard Image Subtraction
-
=
Target Uncertainty Ellipse
Determine the shift between two images, subtract with (x,y) offset.
This type of information has many mission applications.
Current trajectory verification and refinement
Automated target tracking
Target of opportunity detection
Target survey and classification

## Slide 18: Does Your Target Look “As Expected”?
New Horizons Long Range Reconnaissance Imager Detection of Pluto/Charon

## Slide 19
Target Approach and Flyby
Notes: https://independentaustralia.net/environment/environment-display/the-mystery-of-earth-companion-1991-vg,7702
Image via: http://www.cosmosup.com/

## Slide 20: Optical Navigation Products
Reconstructed optical navigation ground product resulting from window snapshots of uncertainty ellipses for target and reference star regions.

## Slide 21: Flyby Data Curation & Prioritization
Data Prioritization Strategies:
Box crop around brightest pixel
Box crop around specified coordinates
Downsample
ICER Compression (Lossy & Lossless)
Extremely limited bandwidth (1 kpbs) for future data downlink
Limited flyby time (<1 hour)
Limited image acquisition rate (15/min)
No auto-exposure of camera
  Utilize exposure bracketing
Onboard image statistics to assess quality with limited data volume
  Contrast calculation
  Pixel histogram
  Header information

## Slide 22: Conclusions
Software techniques can supplement spacecraft hardware limitations to achieve comparable science objectives.
  reduced pointing precision
  limited bandwidth volume
Distilling science data return enables increased focus of attention by human operations, reducing turnaround time for critical decision making.
Onboard data analysis enables new mission profiles which are not possible with traditional methods for analyzing science return.
Onboarding image processing enables target location quantification and imaging using small amounts of bandwidth.
  Enables new smallsat mission scenarios, where communications passes are short and infrequent.