## Slide 1
Ingenuity Mars Helicopter Technology Demonstration
Courtney Duncan, Jet Propulsion Laboratory – California Institute of Technology
May 11, 2020 Interplanetary SmallSat Conference Streaming
Joint effort of Jet Propulsion Laboratory, Ames Research Center, Langley Research Center, Glenn Research Center, and AeroVironment Inc.

## Slide 2: Ingenuity Mars Helicopter Technology Demonstration
The Mars Helicopter Technology Demonstration is now in final preparation for launch to Mars with JPL's Mars 2020 Rover in July 2020. The helicopter plans to execute the first heavier-than-air flight on another planet in April-May 2021. This presentation will overview the helicopter mission and requirements; the design and special circumstances of flight in the thin, cold air of Mars; and some of the commercial off the shelf technologies used.
  With an emphasis on the telecom connection to the Perseverance Rover
JPL URS292031 clearance number CL#20-1956

## Slide 3
From https://mepag.jpl.nasa.gov/
Why Do Planetary Helicopters?

## Slide 4
Capable of flight in thin Mars atmosphere (~1% of Earth, equiv. 30 km)
“Co-axial” Helicopter
Blades 1.2-meter tip-to-tip
Mass ~1.7 Kg
Solar powered – up to 90-second flight per sol
Flight distances up to 300 m
Heights up to 10 m
Autonomous flight & landing
Up to 5 flights
Telecommunication to Base Station on Rover
Self-sufficient thermal control (nights < -100C)
Mars Helicopter Technology Demonstration on Mars 2020

## Slide 5: AeroVironment – Major Industrial Partner
Founded by Paul MacReady
  Designer of the human-powered Gossamer Condor that won the Kremer Prize
  And the Gossamer Albatross that crossed the English Channel
    Piloted by Bryan Allen, now at JPL
Simi Valley, CA
  Unmanned electric aerial vehicles, drones
  Experience with unusual designs and environments
  Military systems, precision agriculture, etc.
Mars Helicopter rotors, motors, servos, mast & wiring, landing gear

## Slide 6
Solar powered
Relay data back to Earth through rover
Closed-loop thermal control for cold Martian nights
After Deployment from Rover,
Ingenuity Operates in Stand-Alone Fashion, with Radio Link to Base Station on Perseverance
Radio Link to Helicopter Base Station on Rover

## Slide 7
Flight 3
Fly large lateral flight path that returns to starting point
Perform scout function to image terrain far ahead of “parking lot”
Certify new “parking lot” (on Earth)
Flight 2
Fly higher vertical ascent & descent and modest lateral motion
To be completed within 118 sols of Rover landing
To be completed within 30 sols of deployment from Rover in a 10m x 10m “parking lot” meeting Mars Helicopter technology demonstration requirements
3m
Fly ~50m out and back
5-10m
5m
Fly to new “parking lot” ~50m away
Fly out ~500m away
Flight 4-5
Contingency for Flights 1-3
If contingency flights are not needed, then consider the following options:
Fly to new “parking lot”
Fly away to maximum distance that the vehicle can fly (~500m). Note: destination landing site will not have been surveyed.
Flight 1
Ascend, hover, land
Take picture of Rover
Rover takes picture of Helicopter in flight
Minimum Mission Success
Five Technology Demonstration Flights at Mars (TBR)

## Slide 8: Potential Images From Rover
NavCams at 100m:< 3.5 cm/pixel
At highest resolution:
  Blade length = 36/5120 pixels
  Body cube = 3.6/5120 pixels
NavCam Imaging Plan Proposal:
  2x2 & 2x2 tile exposed and read out every ~ 6 seconds
  7 cm/pixel
Mastcam-Z
(Full Res) w/ some noise)
Blades are ~ 145 pixels at full zoom
Body Cube ~ 19 pixels at full zoom

## Slide 9: Deployment….
A: Jettison Debris Shield ¼” Cable Cutter Pyros fired severing restraint cables that allows the Debris Shield to drop from the Rover. After drop Rover executes forward drive to prepare for rest of deployment activities
B: Heli Launch Lock Release Frangibolt energized releasing lower Heli Launch Lock Restraint. Egress Arm / Heli Assy held in place by Egress Arm Restraint
C: Egress Arm Restraint Release and Egress Arm Deploy Cable Cutter Pyro fired releasing MHDS Egress Arm. Egress Arm Release initiates rotation of Egress Arm & Heli with actuator in dynamic braking mode. Near the end of the deploy motion the actuator completes the arm deploy motion by driving to the hardstop and latching.
D: Leg Restraint Release Cable Cutter Pyro fired releasing Helicopter Leading Legs allowing them to spring into their fully deployed state. Helicopter is fully configured for drop after this event.
E: Primary Heli Restraint Release & Heli Drop Frangibolt energized releasing Helicopter from Rover & Egress Assy. Helicopter drops to Martian Surface below Rover. After nominal drop is confirmed via telemetry and imagery review Rover executes forward drive to allow Heli Solar Arrays to resume charging

## Slide 10: Ingenuity Telecom Specifications
10 gram mass
  Includes antennas and cables
  13.3 grams achieved (helicopter side)
Rover side (HBE) uses the same electronics boards
Telecom up to 1000 m., two-way
  NFZ is 100 m. radius
  no radio-navigation
Over-the-air rates 20 kbps, 250 kbps
DC power: TX < 3 W, RX < 0.2 W
Temperature -40 to +85 C, -50 C non-op
Protocol modified from ZigBee (IEEE 802.15.4)
UART connection to SnapDragon “NAV” computer
COTS Part Selection Criteria
  Very Low Mass suggests COTS ISM
  Low frequency for lowest omni to omni path loss, 900 MHz is lowest ISM band
  “High Power” – most ISM parts run a few 10s of mW, want closer to a watt
  Diversity – possibility of > 1 antenna
Cost: $60 per unit
Mass prepped: ~3.5g
Power Out: 29 dBm (0.8 W)
Band: 906-924 MHz (10 ch.)
Antennas: 1 or 2
SiFlex COTS Radio

## Slide 11: Helicopter FlatSet Electronics Core Module (ECM)
11
Battery Interface Board (BIB)
Helicopter Power Board (HPB)
FPGA
Actel A3PE3000L
FPGA Flight Control Board (FFB)
Nav Carrier Board (NCB)
Telecom Board
(TCB)
Flight Control Processor
TMS570LC4357 (x2)
Qualcomm Snapdragon 801
Processor
SiFlex Modem
Servo FETs
MHS Flatset 001
“cube” style in helicopter
“wallet” style in base station

## Slide 12: HBS Antenna performance on Mars2020 rover
Helicopter Base Station Antenna (HBA) radiation pattern
HBA1
θ
Antenna design
Antenna
Interpretation of results:
Shadowing effects
Multipath (reflections)
Suffers from a very small ground plane
Larger ground plane and/or location would improve the result
Antenna on M2020 Rover
Coordinate system

## Slide 13: Map Coverage Around M2020 Rover on the Surface
Map coverage assuming min, mean, max polarization loss with blade rotating.
The math is done for all azimuth angles around the helicopter.
These results were obtained using Bullington with ht=0.48m and hr=1.23m.
Min polarization loss
Mean polarization loss
Max polarization loss
Received power of >-94dBm  250kbps
Received power of [-102, -94] dBm  40kbps
Rover
x
z
θh
Azimuth angle θh = [0°-359°]
Link geometry
No link
0.25km
1.0 km
5%
Note: For best results, park the Rover in a “for comm” orientation.

## Slide 14: Map Coverage Around M2020 Rover Flying
Map coverage assuming min, mean, max polarization loss with blade rotating.
The math is done for all azimuth angles around the helicopter.
These results were obtained using Bullington with ht=10m, hr=1.23m, and Req = [0.25 - 1] km.
0.25km
1.0 km
Received power of >-94dBm  250kbps
Received power of [-102, -94] dBm  40kbps
No link
Rover
x
z
θh
Azimuth angle θh = [0°-359°]
Link geometry
Min polarization loss
Mean polarization loss
Max polarization loss
5%

## Slide 15: Operating Modes
Name | OTA* Rate | Throughput | Modulation | Bandwidth | Direction | Default H/B | Bit Size | Packet Size | Note
Silent | NA | 0 | NA | NA | NA | NA |  |  | No TX
Default | 20 kbps | 9 kbps | BPSK | 600 KHz** | Both | 50/50 | 50 sec | 50 msec | Boot Up
Data | 250 kbps | 80 kbps | OQPSK | 2 MHz *** | Both | 90/10 | 4 sec | 4 msec | With OTA acks
TCOW **** | 250 kbps | 204 kbps | OQPSK | 2 MHz | Heli->HBS | 100/0 | 4 sec | 4 msec | Without OTA acks
Name | OTA* Rate | Throughput | Modulation | Bandwidth | Direction | Default H/B | Bit Size | Packet Size | Note
Silent | NA | 0 | NA | NA | NA | NA |  |  | No TX
Default | 20 kbps | 9 kbps | BPSK | 600 KHz** | Both | 50/50 |  | 50 msec | Boot Up
Data | 250 kbps | 80 kbps | OQPSK | 2 MHz *** | Both | 90/10 |  | 4 msec | With OTA acks
TCOW **** | 250 kbps | 204 kbps | OQPSK | 2 MHz | Heli->HBS | 100/0 |  | 4 msec | Without OTA acks
“Silent” under HBS ‘beacon’ control (two node “Mesh” under modified 802.15.4)
* OTA: Over the Air
** Due to 15 chip spreading code
*** Due to Mcps signaling scheme
**** TCOW (Time Critical One Way); VOMIT (Vulnerable, One-way, MHS Information Transfer)

## Slide 16: Field Test (JPL Arroyo)
Helicopter Mockup with Antenna
Rover Mockup
View from Rover Mockup antenna to Helicopter Mockup

## Slide 17: Questions?