## Slide 1
Comparing Radio Occultation Results from MarCO with Mars Reconnaissance Orbiter and MAVEN: Achievable Radio Science with a CubeSat
Dustin Buccino(1), Yu-Ming Yang(1), Paul Withers(2), Kamal Oudrhiri(1), Norman Lay(1), Paolo Tortora(3), and Daniel Kahan(1)
(1) Jet Propulsion Laboratory, California Institute of Technology, Pasadena, CA, USA
(2) Boston University, Boston, MA, USA
(3) University of Bologna, Italy
2020 Interplanetary Small Satellite Conference
May 11-12, 2020
© 2020. California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Outline
Introduction – Radio Occultations
Introduction – MarCO Mission
MarCO’s Radio Instrumentation
MarCO Radio Occultation Performance Analysis
Future Radio Science Missions using CubeSats
Summary

## Slide 3: Radio Occultation Geometry

## Slide 4: Occultations & The First Interplanetary Science
Signal Frequency or Phase (ϕ)
Refractivity (n)
Temperature/Pressure (T/P) Profile

## Slide 5: Radio Science at Mars: Classic Results
Mars Reconnaissance Orbiter
MAVEN
Ionospheric occultations up to 900 km altitude
Ionosphere detectability up to ~288 km
Withers et al, First Ionospheric Results from the MAVEN Radio Occultation Science Experiment, JGR Space Physics, 2018
Hinson et al, Initial results from radio occultation measurements with
the Mars Reconnaissance Orbiter, Icarus, 2014.
Over 5000 radio occultations from 2008-2019
Atmosphere detectability up to ~90 km

## Slide 6: Introduction – MarCO Mission
Mission Objectives:
  Survive the deep space environment
  Communicate and navigate with the Deep Space Network
  Advance miniaturized telecommunications components
  Support InSight during EDL

## Slide 7: MarCO Radio Communication
Iris V2 Transponder
  1.2 kg, ~0.5 U
Antennas
  A low-gain (LGA) patch antenna (for near-Earth communications)
  A medium gain (MGA) patch array antenna (for communications during safe mode)
  A high gain (HGA) reflect-array antenna for normal operations and relaying data during InSight’s EDL
  A UHF loop antenna to receive InSight’s signal during EDL

## Slide 8: MarCO Foldable Reflectarray
Challenge: bent pipe communication at 1.04AU from Earth – i.e. receive and transmit at the same data rate (8kbps)
Main requirements:
  Stowage volume: 12.5mm × 210mm × 345mm
  Gain of at least 28dBic
Required aperture: 335mm × 587mm

## Slide 9: Radio Occultation Experiment
X-band
MarCO-A
MarCO-A
X-band
Time (UTC-ERT) | Event
14:15:00 | Begin Open-Loop Recordings
19:17:48 | DSS-63 Acqusition
19:53:09 | InSight Landing
20:51:56 | Turn Away from Earth-Point
20:52:00 | DSS-63 Loss of Signal
21:33:19 | Geometric Occultation Ingress
23:43:07 | Turn to Earth-Point
23:39:09 | Geometric Occultation Egress
23:46:48 | DSS-26 Acquisition, 1-Way
00:48:10 | DSS-26 Loss of Signal
01:00:00 | End Open-Loop Recordings
RO ingress (2-way)
RO egress
(1-way)
21:33 ERT
20:52 ERT Turn Away from Earth-Point
23:39 ERT
23:43 ERT Turn to Earth-Point

## Slide 10: Data Analysis of the MarCO Occultation

## Slide 11: MarCO Occultation Geometry
Radio Ray Path
Impact Parameter
Neutral Atmosphere Detectable to 90 km (MGS & MRO – Hinson et al 1999)
Ionosphere Detectable to 288 km (MAVEN – Withers et al 2018)

## Slide 12: Modeling of the MarCO Radio Occultation
Simulated MarCO RO Residual Frequency
Simulated MarCO RO Refractive Index
ionosphere
Atmosphere
ionosphere
Atmosphere
These atmospheric and ionospheric profiles are retrieved from the refractive (), which is defined as:
where is the unitless refractivity index, is the altitude in km, is ionospheric electron density, P is the pressure of the atmosphere, and T is the air temperature in Kelvin.

## Slide 13: Frequency Performance
0.004 Hz
0.005 Hz
0.42 Hz

## Slide 14: Occultation Assessment
Mars Ionosphere was not detectable during the MarCO radio occultation
Mars Ionosphere could have been detected in 2-way mode but not in 1-way mode
Neutral atmosphere could have been detected if the spacecraft was pointed to Earth at geometric occultation egress <35 km

## Slide 15: Frequency Stability & Comparison with MRO

## Slide 16: Impact on Future SmallSat Radio Science
Frequency Stability – MarCO’s 1-way signal is not sufficient for precision radio science measurements
    Typically, an Ultra Stable Oscillator (USO) is required for precision radio science measurements
    USO’s are heavy (1-2 kg) and consume power (1-10 W)
    For missions without a USO, 2-way occultations are possible and have been proven on multiple missions (e.g. MRO, Cassini)
Geometry – MarCO’s signal was not acquired until well above the atmosphere and in the ionosphere
    Ingress occultations are more favorable, particularly in 2-way mode
    At other planets, atmosphere is denser and limb tracking maneuvers may be required for deep atmospheric occultations

## Slide 17: Summary
MarCO-A Radio Occultation did not detect the Mars atmosphere or ionosphere during the flyby
An assessment of the MarCO flyby and RO data indicates that the MarCO 2-way data has a stable frequency residual and performance is in the same order of MRO 2-way data.
Modeling results suggest that the 2-way MarCO radio signal could have been able to have a positive detection of the atmosphere and ionosphere comparable to MRO
Frequency residual measurements derived from MarCO X-band radio links confirm that the 1-way X-band data could have detected the neutral atmosphere but not the ionosphere

## Slide 18
© 2020. California Institute of Technology. Government sponsorship acknowledged.