## Slide 1
Himangshu Kalita and Jekan Thangavelautham
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory
Aerospace and Mechanical Engineering Department
University of Arizona
End to End Strategies for Exploring Lunar/Martian Caves
SpaceTREx
ASTEROID

## Slide 2: Outline
Introduction
Motivation
SphereX Bot
Mapping and Navigation
Sensor Placement Strategies
Communication Strategies
Power Transfer Strategies
Conclusion

## Slide 3: Introduction
Science goals identified by Outer Planets Assessment Group (OPAG) with Planetary Decadal Study [1],[2].
Extreme Environments: Ascertain the range of conditions that can support life.
Extreme Environments: Identify planetary processes that are responsible for generating and sustaining habitable worlds.
[1] National Academies of Sciences, Engineering and Medicine (2011)
[2] Scientific Goals and Pathways for Exploration of the Outer Solar System (2006)

## Slide 4: Extreme Environments on the Moon and Mars
[1] High Cliffs Surrounding Echus Chasma on Mars (nasa.gov)
[2] Tycho Crater on Moon (NASA/Goddard/Arizona State University)
[3] Lava Tubes on Pavonis Mons on Mars (ESA)
[4] Mare Tranquilitatis pit on Moon (NASA/GSFC/Arizona State University)
Extreme Environments of Moon and Mars: Cliffs, craters, lava tubes, pits, caves.
These environments are rich targets of origin studies.
Caves, pits and lava tubes offer natural shelter from radiation and insulated from varying high and low external temperatures.

## Slide 5: Problem with exploring Extreme Environments?
[1] Yutu-2 on Moon (space.com)
[2] Curiosity Rover on Mars ( nasa.gov)
[3] Opportunity Rover on Mars (nasa.gov)
[4] InSight Lander on Mars (spacenews.com)
Current landers and rovers are unable to access these areas of high interest
  Limitations in precision landing
  Inability to traverse rugged environments
  Operations culture where risks are minimized at all costs

## Slide 6: Motivation - I
Inset: Artist’s rendering of NASA’s twin Mars Cube One (MarCO) spacecraft flying over Mars with Earth in the distance
Mass of all satellites under 200 kg launched from 1957 to 2016 [B. Lal et al (2017)]
Commercially-Off-The-Shelf (COTS) components

## Slide 7: Proposed Solution: SphereX
Small low-cost, modular spherical robot (SphereX)
  Mobility system for exploration
  Space-grade electronics
  Power system for power generation
  UHF/S-band antennas for communication
  Thermal and Shielding system for survival
  Outer shell for structural robustness
  Payload capacity for science instruments
Credit: Rachel Moses

## Slide 8: Exploration of Pits, Lava Tubes and Craters
Concept of Operations for exploring planetary pits/lava tubes
Concept of Operations for exploring planetary craters

## Slide 9: Mobility System
Mode of Mobility: Hopping
Hopping achieved through:
  Miniaturized propulsion system
  3-axis reaction wheel system
2 modes of Hopping Mobility
  Hard-landing mode
  Soft-landing mode
Time Diagram
Control System Architecture

## Slide 10: Lunar Pits
Recently discovered lunar mare “pits” are key science and exploration targets.
Ready made shelter for future lunar explorers, benign T (-25o C)
Pristine preservation
  Flow features
  Sublimate minerals
  Regolith? Water?
Mare Ingenni
Mare Tranquilitatis
Marius Hills
Test Model: modelled in Blender

## Slide 11: Pit Entrance Survey
Hop 1
Hop 2
Hop 3
Hop 4
Combined Map

## Slide 12: Pit Entrance
Map Generated
Position Estimate
Orientation Estimate

## Slide 13: Line-of-sight Analysis
Line-of-sight from pit surface to pit floor

## Slide 14: Line-of-sight Analysis
m
m
BW
BW
Laser
BW
BW
Laser

## Slide 15: Sensor Placement
Optimal Sensor Placement using RRT*

## Slide 16: Sensor Placement
Optimal Sensor Placement using RRT* in an unknown cave through 5 successive ExplorePlace sensor cycles

## Slide 17: Communication
Two types of sensors modeled
  Reflectors (Inactive)
  Amplifiers (Active)
Variation of data rate in bps over distance for 10 hops. The simulation is performed with RF communication () with () bandwidth and optical communication () with () bandwidth assuming a) Reflectors, and b) Amplifiers.
Variation of BER over for different number of hops. The simulation is performed assuming two sensor configurations a) Reflectors, and b) Amplifiers

## Slide 18: Power Transfer
Wireless power transfer through Lasers
  Electricity to Laser Conversion
  Laser Transmission
  Laser to Electricity Conversion (P-V cells)
Variation of electricity to laser efficiency over supplied power
Variation of laser transmission efficiency over distance
Variation of laser to electricity conversion efficiency of a solar cell over voltage
Variation of laser to electricity conversion efficiency of a solar panel over incident power

## Slide 19: Power Transfer
Two types of sensors modeled
  Reflectors
  Converters
LineSpec | Property
Color – ‘red’ | 
Color – ‘blue’ | 
Color – ‘black’ | 
LineStyle – ‘Solid’ | 
LineStyle – ‘Dashed’ | 
LineStyle – ‘Dash-dot’ | 
Marker – ‘Square’ | Converters
Marker – ‘Asterisk’ | Reflectors
LineSpec | Property
Color – ‘red’ | 
Color – ‘blue’ | 
Color – ‘black’ | 
LineStyle – ‘Solid’ | 
LineStyle – ‘Dashed’ | 
LineStyle – ‘Dash-dot’ | 
Marker – ‘Square’ | Converters
Marker – ‘Asterisk’ | Reflectors
Variation of transmitted power over distance for
Variation of transmitted power over distance for
Laser wavelength nm

## Slide 20: Power Transfer
Two types of sensors modeled
  Reflectors
  Converters
LineSpec | Property
Color – ‘red’ | 
Color – ‘blue’ | 
Color – ‘black’ | 
LineStyle – ‘Solid’ | 
LineStyle – ‘Dashed’ | 
LineStyle – ‘Dash-dot’ | 
Marker – ‘Square’ | Converters
Marker – ‘Asterisk’ | Reflectors
LineSpec | Property
Color – ‘red’ | 
Color – ‘blue’ | 
Color – ‘black’ | 
LineStyle – ‘Solid’ | 
LineStyle – ‘Dashed’ | 
LineStyle – ‘Dash-dot’ | 
Marker – ‘Square’ | Converters
Marker – ‘Asterisk’ | Reflectors
Laser wavelength nm
Variation of transmitted power over distance for
Variation of transmitted power over distance for

## Slide 21: Conclusion
Presented Strategies for exploring Lunar/Martian caves that includes
  Mobility
  Mapping and Navigation
  Communication
  Power Transfer
Use of multiple sensors to maintain a direct line-of-sight connection link for both wireless communication and power transfer
Use of Lasers for both communication and power transfer has an advantage

## Slide 22
Thank You

## Slide 23
Questions ?