## Slide 1
NASA Big Idea 2020: Lunar Autonomous Scalable Emitter and Receiver (LASER) System –FemtoSat Design
SpaceTREx
Álvaro Díaz-Flores Caminero, Jose María Fernández Moreno, Jekan Thangavelautham & The LASER Team
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory
Aerospace and Mechanical Engineering Department
University of Arizona

## Slide 2: Introduction
We have been studying the surface of the Moon since the mid-1960s – “surface bone dry”.
2009 NASA’s M3 onboard the Chandrayaan-1 detected water and results were confirmed in 2018
New evidence for evolution of water on the Moon
  Transport from mid-latitude to poles over eons.
Water on the Moon is a “make or break” moment in terms of space economics.
Renewed hope lunar resources will kick-start the space economy.

## Slide 3: Motivation
Burgeoning tendency to miniaturization
  Reduced cost and weight
Secondary payloads
  Advance science at reasonable cost
LASER aims to charge a Smart device positioned in the PSR using a laser beam
  How to use something small and cheap for this?  FemtoSats
Looking for new opportunities

## Slide 4: Objective
Design a 2F FemtoSat
  RF localization
  Charge battery
  Data transmission
  Keeping it low-cost

## Slide 5: Related work
Femto concept  SunCube
Solar panel miniaturization  DHV technologies
Charge devices with laser  ASU/Univ. of Arizona (2014), Univ. of Washington (2018)
Arduino platform

## Slide 6: Mission Requirements
Survive the extreme temperatures: [-153, 107] ºC
Charge a battery with a laser
RF localization
UHF data transmision
Perform tasks for at least 12 hours
Total mass per FemtoSat under 100g
Cost under $350
Low cost approach to obtaining first look inside PSR region.
Notes: RF localization between 2 and 20 meters

## Slide 7: Challenges
Technology limitations
Coupling
Extreme conditions
It is never easy
Notes: Tech limit explain that there are no current solar cells that provide the voltaje required

## Slide 8: Concept of Operation
Launch
Landing
Deployment
Data recollection
Disposal
t=0
t=3h
t=3.5h
t=12 days
Launch + 5.5 days

## Slide 9: Design Part I: launching survival
Conservation of energy model
Results:
m/s
Earth testing:
Minimizing impact forces…

## Slide 10: FemtoSat Architecture
Dimensions: 2F (60mm x 30mm x 30mm)
Elements:
Case (green) [60,30,30]
Gorilla glass [54.8, 24.8, t: 0.4]
Solar panels [51, 21, t: 1.6]
Aluminum box [54.8, 23.8, 23.8, t: 0.5]
Insulation (MLI) [53.8, 23.8, 23.8, t: 2,3]
Hardware [20, 20, 30]
All dimensions are in mm

## Slide 11: FemtoSat Architecture
Group | Element | Mass (g) | Volume (mm)
Hardware | Processor board (TinyZero) | 1.4 | 20x20x2.9
 | Processor board (TinyDuino) | 1.10 | 20x20x2.9
 | IMU | 1 | 20x20x5.11
 | Radio + (antenna) | 1.15+0.26 | 20x20x5.11 (+177)
 | Battery (150 mA, 3.7V) | 3.77 | 20x20x5
 | Proto Board | 0.85 | 20x20x5.11
Solar array | Charger controller | 0.54 | 14x9x3.7
 | Short panels (Test) 2x | ~5.6 | 21x21x2
Structure | Long panels (Test) 4x | ~27 | 51x21x2
 | TPU case | 9 | 60x30x30
Insulation | Box (aluminum) | 9 | 54.8x24.8x24.8 (t=0.5)
 | MLI |  | 53.8x23.8x2 23.8x23.8x2
Total | Aerogel |  | 
 |  | 53.97 | 60x30x30 (2F)
Notes: Then let’s move piece by piece

## Slide 12: Circuit Design
Panel 1
Panel 4
Panel 3
Panel 2
Proto board
Charger controller
Battery
IMU
Processor
Radio 433MHz
Notes: Let’s go part by part

## Slide 13: Solar panels design
Requirements:
A | 4.41
 | 10.71
 | 1367
 | 1322 (summer)
 | 1414 (winter)
 | 4444.44
T | 107 (sun lluminated)
 | -153 (shadow)
TSTD | 28
 | -5.6
 | -13
 | 9·10-3
A | 4.41
 | 10.71
 | 1367
 | 1322 (summer)
 | 1414 (winter)
 | 4444.44
T | 107 (sun lluminated)
 | -153 (shadow)
TSTD | 28
 | -5.6
 | -13
 | 9·10-3
Battery |  | 30 mA
 |  | 150 mA
 |  | 4.2 V
 |  | 5 V
Charger controller |  | 15 mA
 |  | 500 mA
 |  | 4.2 V
 |  | 6 V
Battery |  | 30 mA
 |  | 150 mA
 |  | 4.2 V
 |  | 5 V
Charger controller |  | 15 mA
 |  | 500 mA
 |  | 4.2 V
 |  | 6 V
Boundaries:
Equations:

## Slide 14: Solar panels design
One cell (n1=1, n2=1)
Four cells (n1=2, n2=2)
 | 28 mA
 | 4.64 V
 | 28 mA
 | 4.64 V
Area | Phi | dV/dT | T | Imp | Vmp
4,41 | 1322 | -5.6 | 107 | 30,11 | 4,2
4,41 | 4444 | -5.6 | 107 | 101.23 | 4.2
4,41 | 4444 | -5.6 | -153 | 67,68 | 5.65
4.41 | 1414 | -5.6 | 107 | 32.21 | 4.2
10,71 | 1322 | -5.6 | 107 | 34.44 | 4,2
10,71 | 4444 | -5.6 | 107 | 115.79 | 4.2
10,71 | 4444 | -5.6 | -153 | 34.31 | 5.65
10,71 | 1414 | -5.6 | 107 | 36.84 | 4.2
Area | Phi | dV/dT | T | Imp | Vmp
4,41 | 1322 | -5.6 | 107 | 64.09 | 3.1
4,41 | 4444 | -5.6 | 107 | 215.46 | 3.1
4,41 | 4444 | -5.6 | -153 | 148.36 | 6.01
4.41 | 1414 | -5.6 | 107 | 68.55 | 3.1
10,71 | 1322 | -5.6 | 107 | 72.75 | 3.1
10,71 | 4444 | -5.6 | 107 | 244.59 | 3.1
10,71 | 4444 | -5.6 | -153 | 81.63 | 6.01
10,71 | 1414 | -5.6 | 107 | 77.82 | 3.1
 | 28 mA
 | 1.99 V
 | 28 mA
 | 1.99 V
Notes: Here explain that the best solution would be n1=1 and n2=2
Insert the results for the conclusión at -98ºC

## Slide 15: Solar panels: market analysis (DHV technologies)
DHV technologies a viable option for Deep Space Exploration
Data from DHV technologies

## Slide 16: Thermal Analysis
Results:
Simplyfied model for thermal anlysis

## Slide 17: Radio frequency localization
Clock transmission and triangulation: too much error. Need new method for localization
Decawave: DWM1000 – UWB Localization  However, antenna too big
  Foldable?
Option for new development

## Slide 18: Arduino platform
RX on
Temperature
Laser
TX on
Send data
TX and RX off
Time/ Low battery
TX send
RX on
Data:
Address
Working panel
Input Volatage
IMU
Battery percentage

## Slide 19: Discussion
Future work:
  Close future: build a model for laser testing
  Iterate on the thermal design to minimize power consumption
  Upgrade the FemtoSat equipment to perform more complex mission.
  Locate the FemtoSat

## Slide 20: Conclusions
Improvement in technology gets us closer to FemtoSat design
Highly coupled systems but feasible design
Attempt to extend solar panel miniaturization
Limited working temperatures range

## Slide 21
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory