## Slide 1
Derivation of Surface
Previous Approach
Planar Airbearing allowing 3 degree of freedom motion
Updated Approach
Radially sculpted air-bearing table to mimic a low gravity asteroid environment
Conclusion
Capture of erupting particles is a plausible alternative to touchdown on the asteroid surface
Creation of a radially symmetric air bearing can reproduce aspects of the dynamic environment for system test
This air bearing table can also be used as a hands on teaching tool for Keplerian dynamics.
Leonard Vance
SpaceTREx Laboratory, University of Arizona
Asteroid Gravity Test System Using a Planar Air Bearing
References
D.S. Lauretta et al. Episodes of particle ejection from the surface of the active asteroid (101955) Bennu. Science, 2019
Table Cross Section
(Vertical Scale Exaggerated)
Diameter is chosen consistent with reasonable max handling size (rmax = 1.6m)
Period of max radius orbit limited with ability to level platform (tp = 120 seconds)
Inner radius limited by ability of air bearings to plausibly maintain lift on a curved surface (rmin = 0.1m)
Manufacturing
Motivation
The size and makeup of near earth asteroids make spacecraft sample and return missions hazardous. Since at least one of these asteroids (101955) Bennu regularly ejects particles, nanospacecraft could be deployed to capture these objects in flight, eliminating the need for touching down on the asteroid itself.
The proposed airbearing table is radially curved to mimic the low gravity of a centrally located asteroid, permitting evaluation of such a mission’s navigation, guidance and docking.
Inwards acceleration at max radius
Gravitational model
Value of k for chosen orbital period tp
Slope required for that orbital period
Integration of slope to get outline
CNC Vertical Turning Lathe Accuracy usually about 0.02mm
Specifications
Concept of Operations
1) Observe eruption and choose particle
2) Nano-spacecraft guides to particle
3) Rendezvous and capture
4) Return to Mothership
D.S. Lauretta et al. Episodes of particle ejection from the surface of the active asteroid (101955) Bennu. Science, 2019
Particle Trajectories from 19 Jan 2019 eruption event
Table requirements well within existing tooling machine capability
1.6 m diameter
Orbital period
120 sec (outer edge
5 sec (inner edge)
Airbearing table mimics low gravity system
mass = 20 kg Approx.