## Slide 1
Alvaro Diaz-Flores1, Claire Pedersen2, Yinan Xu1, Lindsey Williams2, Cho Lik Chan3 and Jekan Thangavelautham1,2
1Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory
2Asteroid Science, Technology and Exploration Research Organized by Inclusive eDucation Systems (ASTEROIDS) Laboratory
3Aerospace and Mechanical Engineering Department, University of Arizona
First Phase of the Lunar Ark Concept – Towards Saving Life on Earth from a Future Catastrophe

## Slide 2: Outline
Introduction
Motivation
Objectives
Lunar Lava Tube Exploration
Lunar Ark Concept
Feasibility Summary
Conclusions

## Slide 3: Introduction – Living Organism Endangered
Diverse ecosystems in danger on every continent
Large fraction of every kind of plant and animal in danger
Due to human activity and other factors, we don’t fully understand
IUCN Endangered Animals

## Slide 4: Motivation
Loss of apex predators cascades down to entire food chain.
Devastating loss to animal and plant diversity

## Slide 5: Motivation – Collapse of World’s Food Supply
Combination of factors killing of critical organisms such as honeybees holding up the world’s (human) food supply
Pesticides, artificial chemicals, predators, disease, change in climate

## Slide 6: Constellation Validation
Performance of the constellation simulated for 1 day.
Camera View
Scene
Chebalinsk, 2013
Constellation for Monitoring Space Threats
[J. Thanga*, V. Reddy, R. Furfaro]

## Slide 7: Motivation - Mass Extinction Dangers on Earth
Earth is in an extremely fragile state. Humans have already faced one close call, 75,000 years ago.
Super Volcanic Eruption
Global Nuclear War
Asteroid Impact
Global Epidemic
Climate Change Accelerated
Global Solar Storm
Global Drought

## Slide 8: Motivation – Toba Super Volcano
Toba Super-volcanic eruption nearly 74,000 years ago.
Prolonged winter for decades or more and 1,000 year cooling period
Aligns with estimated drop in human diversity

## Slide 9: Need for a Modern Ark
More cost-effective than trying to protect all the endangered species any other way.
More cost-effective than creating an entire artificial ecosystem to keep them alive.
Save them till technologies advances to re-introduce these species.
A modern global insurance policy!
Biblical Noah’s Ark
Biblical Noah’s Ark
Svalbard Seed Vault
Svalbard Seed Vault

## Slide 10: Need for a Modern Ark
Why ? Humanity has responsibility to protect the diversity of life.
Svalbard Doomsday Seedbank one-step in the right direction.
Svalbard Seedbank can be in danger of Earthly cataclysms, especially rising ocean from climate change.

## Slide 11: Objectives
Develop a secure modern Ark that can house all the endangered species of the Earth and avoid any Earthly cataclysm.
  Explore potential for lunar lava tubes and caves.
  Perform preliminary concept development and determine energy/power feasibility.
  Determine how we can start small and get started now!

## Slide 12: Lunar Pits and Lava Tubes
Recently discovered lunar mare “pits” are key science and exploration targets.
Likely 3-4 billion years old
Nearly 200 found [Wagner & Robinson, 2013]
Ready made shelter, benign T (-25o C)
Shelter from:
  Surface Temperature Swings
  Solar and cosmic radiation
  Micrometeorites
Pristine preservation ?
  Flow features
  Sublimate minerals
  Regolith? Water?
Mare Ingenni
Mare Tranquilitatis
Marius Hills

## Slide 13: Why a Lunar Ark ?
Only four days away from Earth.
Moon subsurface sheltered and frozen in time for 3 billion years
Moon likely doesn’t have enough water resources to become thriving center
Humans not eager to live and work subsurface

## Slide 14: Lunar Bases Underground
A few concepts have explored underground lunar bases
More likely a temporary shelter.
Humans unlikely to prefer them as they are not ground moles!

## Slide 15: First Phase – Exploration of Lunar Pits
We need to confirm all the hypothesis discussed earlier
Do so with the enabling low-cost technology from small satellites
Utilizing teams of robots, where even if one or a few are damaged or destroyed, mission continues.
Green exploration doctrine
The lava tubes are great natural monuments that needs to be well preserved, so no contact/tether grinding with side walls or mouth.

## Slide 16: SphereX Robots for Lunar Pit Exploration
Small low-cost, modular spherical robot (SphereX)
  Mobility system for exploration
  Space-grade electronics
  Power system for power generation
  UHF/S-band antennas for communication
  Thermal and Shielding system for survival
  Outer shell for structural robustness
  Payload capacity for science instruments
Avoid damage of pit walls or entrances.
Credit: Rachel Moses

## Slide 17
ARNE Mission Concept
SphereX Platform
[Jekan Thanga*, Mark Robinson, Wagner, 2015]
Explore caves, canyons and craters using swarms of flying/hopping robots.

## Slide 18
ARNE II Mission Concept
[Jekan Thanga*, H Kalita, Mark Robinson, 2018-]

## Slide 19: Exploration of Pits, Lava Tubes and Craters
Concept of Operations for exploring planetary pits/lava tubes
Concept of Operations for exploring planetary craters

## Slide 20: Lunar Pits
Recently discovered lunar mare “pits” are key science and exploration targets.
Ready made shelter for future lunar explorers, benign T (-25o C)
Pristine preservation
  Flow features
  Sublimate minerals
  Regolith? Water?
Mare Ingenni
Mare Tranquilitatis
Marius Hills
Test Model: modelled in Blender

## Slide 21: Pit Entrance Survey
Hop 1
Hop 2
Hop 3
Hop 4
Combined Map

## Slide 22: Pit Entrance
Map Generated
Position Estimate
Orientation Estimate

## Slide 23: Line-of-sight Analysis
Line-of-sight from pit surface to pit floor

## Slide 24: Line-of-sight Analysis
m
m
BW
BW
Laser
BW
BW
Laser

## Slide 25: Sensor Placement
Optimal Sensor Placement using RRT*

## Slide 26: Sensor Placement
Optimal Sensor Placement using RRT* in an unknown cave through 5 successive ExplorePlace sensor cycles

## Slide 27: Multi-Robot Mapping
Robot 1
Robot 2
Robot 3
Master Map

## Slide 28: Protecting Earth’s Endangered Species
Total Nearly: 6.7 million species need protection
  5.1 million Fungi
  0.3 million Plants
  1.3 million Animals
Seed, sperms, eggs, DNA could be stored for hundreds of years at cryo-conditions.

## Slide 29: Where to Get Started
Replicate Svalbard Seed Vault on the moon.
Second mission would be to carry 12U CubeSat canisters containing seeds and store them in a lava tube.
Estimates show 15 launches of SpaceX Falcon Heavy.
Svalbard Seed Vault

## Slide 30: Seeds to be Stored
Based on the Svalbard experience seeds would be stored in foil bags and sealed (500 per species).
Depending on amount of background radiation from granite, will need additional protection.
Store 1 million seeds.

## Slide 31: Seed Ark vs Full Ark
International Space Station took 40 launches. Lunar Seed Ark can be started now without breaking the bank!

## Slide 32: A Modern Lunar Ark
Modular robotic base inside lava tube powered using renewable energy.

## Slide 33: Lunar Ark Modules
Modules would be pre-fabricated and transported from Earth
Envision using SpaceX Falcon Heavy or SLS to do the heavy lifting.
Current numbers show
need for 250 Falcon Heavy
launches!
Design optimization – next step

## Slide 34: Lunar Ark
Shafts for base expansion and preserve transport
Preserves held cryo-modules

## Slide 35: Cryo-Module Cross Section
Cryo-module hold preserves in cassettes stored at -180 oC to 196 oC
Floating 7-DOF robot manipulator retrieves preserve

## Slide 36: Structures & Thermal Insulation
Material | Thermal expansion coefficient | Thickness (mm)
Ortho-fabric (outer) | 1.2 × 10-4 | 4
Aluminized mylar | 1.7 × 10-5 | 6
Goretex Pressure Garment | -1.0 × 10-5 | 3
Bladder (coolant) | 2.4 × 10-4 | 4
Nylon Ripstop | 8.0 × 10-5 | 3
Ortho-fabric (inner) | 1.2 × 10-4 | 3
Aluminum | 2.3 × 10-5 | 20
Multiple layers, consisting of inflatable bladder, pressure garments, nylon ripstop, with AL 6065 backing

## Slide 37: Lunar Ark and Logistics Base

## Slide 38: Power Needs – Lunar Full Ark
Total Subsurface Cryo-modules: 5 Needed
For modules at -180 oC:
  2.3 kW
For modules at -196 oC
  3.8 kW
Cryo-modules total: 23 kW
More work needs to be done to figure out if 5 cryo-modules enough or more needed.

## Slide 39: Power for Lunar Ark
Power to be generated using PV cells located on surface operating over lunar day.
Ark needs 11,000 kWh for lunar day.
Total needs: 28,500 kWh (including margins)
Solar Panels: 191 m2, 3TJ, 30% efficiency

## Slide 40: Lunar Seed Ark
Refrigeration power needs is zero.
Still will need small amount of power for lighting. (500 W) and controlled access.
Laser power beaming from surface could be sufficient.
Simple elevator shaft placed at center of pit with “T” support structure anchoring surface.
Lunar seeds placed in stacked 12U cannisters, no need for building complex structure to house them.

## Slide 41: Conclusions
Proposed a Seed Lunar Ark as first step before trying to protect all major animals, plants, fungi.
Would store 1 million seed packets
Need 15 launches (SpaceX Falcon Heavy)
Material needs to be preserved at -18 C
Technology exist to do this now (within 5 years)

## Slide 42: Authors
Alvaro Diaz-Flores
Claire Pedersen
Yinan Xu
Lindsey Williams
Prof. Cholik Chan
Prof. Jekan Thanga

## Slide 43: Thank You!

## Slide 44: Questions ?