## Slide 1: Design and Construction of a Hot-Fire Rocket Test Stand at The University of Arizona Amid Restrictive Pandemic Protocols
Devon Schmitt, Dr. Gregory Ogden
The University of Arizona
Department of Chemical and Environmental Engineering

## Slide 2: Agenda
Introduction and Background
Hardware
Data Acquisition System
Thermoelectric Cooling Study
Safety Protocols

## Slide 3: Introduction and Background
Test Stands are a secure means of firing engines and collecting data
  Chamber temperature, pressure
Examples
Purdue
UAH

## Slide 4: Initial Stand Design

## Slide 5: Changes Made
Increased modularity
Streamlined Assembly
Adjusted Plate dimensions

## Slide 6: Stress Tests
Displacement, ½”
Displacement, 1”
Von Mises Stress, ½”
Von Mises Stress, 1”

## Slide 7: Final Mechanical Assembly

## Slide 8: Data Acquisition System
Three Major Components
  2x Futek Load Cells
  Pressure Sensor
    100 bar (not pictured)
SENSIT Software
  User interface
500 lbs
50 lbs

## Slide 9: Thermoelectric Cooling Study
Phones used for videotaping engine tests overheated during summer academy
Needed a solution to keep them cool
Chosen Method: Thermoelectric Coolers

## Slide 10: What is a Thermoelectric Cooler?
https://toroccoscoolingandheating.com/thermoelectric-wine-coolers-work/

## Slide 11: TEC Study Parameters
Parameter | Value
Tamb | 100 oF
To | 25 oC
Tmo | 95 oF
iPhone 8 dimensions | W: 67.3mm, H: 128.44mm
Max Output of a Phone | 3 W
Working Current TEC | 4 – 4.6 W
Max Output TEC | 60 W
Solar Radiation | 1,361 W/m2
hair, nc | 25 W/(m2K)

## Slide 12: Results of Study
Total Energy Transfer
to System: 15.644 W
dT (chart) : 10o
Peltier Efficiency: 40%
Power Required: 39.11 W
The TEC system will work

## Slide 13: Safety Protocols
Standoff Distance is the minimum distance required for all operators to safely fire a rocket engine
Various Sources
  Legacy military documents
  Explosive safety manuals
  Demolition Data
Used data from High Power Rocket Safety Code

## Slide 14: Standoff Distance (cont.)

## Slide 15: Standoff Distance

## Slide 16: Standoff Distance Adjustment
Long distance means remote ignition trouble
Instead of simply standing further, implement protective barriers
  Reduces standoff distance considerably
  Better for remote ignition, operation cost

## Slide 17: Safety Procedures
Remote Ignition from Protective Covering
Most Likely Failures
  Failure to Ignite
    Caused by faulty wiring, bad rocket
  Dislodged Rocket
    Caused by poor/malfunctioning mounting
  Detonation
    Caused by a faulty rocket

## Slide 18: Procedure in the Event of Failure
Failure to Ignite
  Turn off ignition system, wait 60 – 120 seconds, approach the rocket and remove the ground wire first, troubleshoot
Dislodged Rocket/Detonation
  Remain behind protective barrier for 3 – 4 minutes, turn off ignition, proceed with caution and retrieve fragments

## Slide 19: References
National Association of Rocketry High Power Rocket Safety Code URL: nar.org/safety-information/high-power-rocket-safety-code/
II-VI The Peltier Effect. URL: ii-vi.com/how_do_thermoelectric_coolers_tec_work
Futek LCF300/400 Images. URL: futek.com