## Slide 1: CATSAT: A 6U Inflatable antenna technology demonstrator mission

## Slide 2: Mission Description
6U CubeSat technology demonstrator mission
  To be launched on NASA’s ElaNa 43 mission.
  Launch NET August 2022 on board Fire-Fly Black Alpha.
  Sun synchronous orbit at 550 km.
  Nominal mission lifetime: 6 months.
Payload
  X-band inflatable antenna system - 1.5U
  HF whip antenna deployment system - 0.1U
  Instrumentation module - 1U
    HD Cameras, FPGA processor, SDR
  Metrology camera system – 0.5 U

## Slide 3: Science/Technology Traceability Matrix
Science/Technology Questions | Objective | Measurement Requirement | Mission Requirement
How can low power, high data rate communications be achieved with a Small Satellite? | Demonstrate a deployable, high gain antenna | Relay high definition images from orbit in near real time | Orbital platform High Def Camera imaging system Inflatable, 0.5m reflector X band data link ~550 km, sun synchronous orbit >1 month
How does the structure of the ionosphere vary from day to night? | Measure ionospheric structure along the terminator | Monitor multiple HF WSPR beacons above the ionosphere | Orbit along terminator >550 km altitude >1 month

## Slide 4: 6U CubeSat System Overview
Feed support structure
Vectran ties
Line feed unit
Antenna metrology module
AD&CS
Whip antenna deployer
HD camera
ASTRO SDR
Microwave upconverter
X-band patch antenna
Whip antenna
UHF antenna

## Slide 5: Concept of operation
CatSat X-Band Ground Stations:
Biosphere 2: Tucson AZ
Rincon Research: Centennial CO
Whip Antenna Rx mode

## Slide 6: Spherical Inflatable Antenna
Engineering prototype
Arecibo observatory
Line feed
1.5 U System
0.5 m spherical reflector

## Slide 7
Line feed – field measurements

## Slide 8
HF Whip Antenna
Probe diurnal variation in the Ionosphere.
A 0.6 m whip antenna deployed from a 0.1U packaging system.
Listens to Weak Signal Propagation Reporter (WSPR) from Amateur radio stations.
Probes from above Ionosphere.
Aim to generated 3D Ionosphere ray tracing along terminator.
Antenna deployment system

## Slide 9
6U CATSAT Flight Hardware Integration
Antenna metrology module
Whip antenna deployer
HD camera
ASTRO SDR
Microwave upconverter

## Slide 10
6U CATSAT Flight Hardware TVAC testing
Integrated 6U system
Assembly in TVAC chamber

## Slide 11
6U CATSAT Flight Hardware TVAC testing

## Slide 12
Orbit lifetime assessment model
CubeSat Platform | Mass (kg) | Ballistic Coefficient | Lifetime in years | 550 km | 600 km | 650 km
 |  |  | 500 km | 550 km | 600 km | 650 km
6U | 9 | 20.83 | 2.00 | 3.75 | 11.94 | 24.48
12U | 12 | 27.78 | 2.45 | 4.56 | 14.52 | 28.98
16U | 16 | 37.04 | 3.07 | 6.53 | 17.24 | 
12U | 20 | 46.30 | 3.64 | 11.43 | 25.10 | 
16U | 24 | 55.56 | 4.10 | 13.49 | 27.87 | 
16U | 25.8 | 59.73 | 4.31 | 14.12 | 29.31 | 
Atmospheric Model - NRLMSISE2000
Drag coefficient ~ 2.2
Orbit inclination: 30 degrees
Estimated LEO lifetime in years
NASA ORDEM 3.1
Lifetime sensitivity analysis conducted with respect to:
Low Earth Orbit altitude and inclination (circular).
Launch year.
Gas composition (Helium, Nitrogen, Carbon dioxide, Argon studied).
Membrane material.
Membrane thickness.
Chart: Cumulative orbital debris flux 550 km circular orbit, 30 deg inclination

## Slide 13: Inflation control system TVAC test setup – Northrop Grumman
Flat reflective membrane
Flat clear membrane

## Slide 14
TVAC – Shape measurement and leak-rate analysis
The inflation control system was able to maintain required ΔP in response to controlled punctures on the membrane surface.
Measured leak rate of the inflatable under nominal TVAC conditions: 12 Pa/hr (0.0017 PSI/hr)
Estimate lifetime based on leak rate: ~ 5 months (over pressure state), ~8 months (nominal pressure state). True lifetime between 5-8 months as we switch between these states.
Inflated shapes repeatable with a 10 μm precision

## Slide 15
Integrated CATSAT system
Conclusion
CATSAT aims to establish the efficacy of inflatable systems in LEO.
Flight data to be used to validate lifetime assessment models and RF performance.
Paves the way for further enhancements including membrane Rigidization and feed steering.

## Slide 16
Thank you!
Contact: achandra@email.arizona.edu