## Slide 1
Derek Gilbert, Nathan Grossman, Garrett Romero, Dr. Greg Ogden
Department of Chemical & Environmental Engineering
University of Arizona
Resistojets for CubeSat Propulsion

## Slide 2: Presentation Outline
Motivation
  Where we fit in
Objective
Challenges
Methods
Current Status
Discussion
Takeaway

## Slide 3: Big Picture
Develop Green Propulsion System for 1-3U CubeSat
  Early CubeSats did not have propulsion systems
  Increased CubeSat activity increased demand for extended mission lifetimes and navigation
  Resistojets are simple engines that only require a heat source and control valves
  Interplanetary CubeSats with Resistojets could use water from asteroid regolith to extend their mission operations

## Slide 4: Objectives
Create a Thruster that is:
Clean
Cheap
Simple in design
Solution:
Resistojets are common and simple in design
Water is clean and cheap

## Slide 5: Current CubeSat Resistojets
CUA Resistojets simplify design by using refrigerants
AQT-D Resistojet successfully operated from ISS deployment in 2019

## Slide 6: Challenges
Steam is not an ideal gas (CEA code is not valid)
Converging-diverging manufacturing difficulties (currently using a simple hole nozzle)
Finding small parts was difficult
Lead times of these parts extended the assembly timeline

## Slide 7: CEA Code Analysis
Major Finding: CEA relies on expelled gasses being an ideal gas
Limiting Factor: Steam is not an ideal gas for temperatures below 748 Degrees Celsius (and pressures above 109 atm)
  500.0 C / 374.0 C = 1.337 (Fails)
  1.97atm /217.7 atm = 0.009 (Does not Fail)

## Slide 8: Analyzed research articles to obtain typical Resistojet values
A comparison of the UK-DMC Cubesat and the Optical Communications and Sensor Demonstration (OCSD) Cubesat
Gave us a starting point to determine our required Resistojet parameters​

## Slide 9: Experimental Sizing
Heater Section:
Mass Flow Rate: 2.0 mL/min
Temperature: 200 to 300 C
Pressure: 2 to 4 bar
Feed Water Pump:
Up to 6LPM
Periodic Operation
  Fill unit, self pressurizes upon heating, then expel in pulse

## Slide 10: Process Flow Diagram

## Slide 11: Purchased Design Components
Heater Assembly
  ¼” 60V, 140W heater
  3/8” SS sheath
PID heater & thermocouple
Solid State Relay
Feed Water Pump

## Slide 12: Remaining Parts
Power Supply (15 V)
Expansion Relief Piston (Airpot 2KS95-3.0CP-ET)
Solenoid Valve (Burkert 6013 136019)

## Slide 13: Future Work
Experimental verification of MATLAB data
Converging-Diverging nozzle design and fabrication
Vacuum Chamber testing
Ice Plug buildup experimentation

## Slide 14: Questions