## Slide 1
Jiawei Qiu, Sebastian B. Miranda, Virupakshan Vilvanathan, Yinan Xu, Athip T. Raj,
Erik Asphaug, Jekan Thangavelautham
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory
Aerospace and Mechanical Engineering Department
University of Arizona
Robust Lunar Base Architectures using
Smart Pico-Building Blocks

## Slide 2: Motivation
Artemis Program - Establish a permanent habitat on the Moon
Underground Structures
(LPI, NASA)
Inflatable Structures
(G. Kitmacher, NASA)
Rigid Structures
(LPI, NASA)

## Slide 3: Challenges
Harsh environment + expensive launch budget
Lunar Surface Radiation
(LPI, NASA)
Meteorite Bombardment
(LPI, NASA)
Saturn V Launch
(NASA)

## Slide 4: Approach
In-situ resource utilization (ISRU) with “smart” sandbags
Superadobes Built with Sandbags
(N. Khalili)
Embedded Electronics in
Smart Sandbags

## Slide 5: Approach
Electrical Components | Usage | Application
Proximity Sensors | Detect presence of neighboring sandbags | Enable streamlined construction process involving multiple simple rovers
LED / LED Matrices | Indicate warnings, display info | Signage for machine/human vision
Thermocouples | Measure temperature | Monitor structure in/exterior temperature
Force Sensors | Detect presence of sandbags above | Facilitate construction process; monitor structural integrity;
Accelerometer | Determine orientation of sandbag; detect movement | Monitor structure integrity; monitor micrometeorite bombardment
Low range antenna | Communicate info to nearby system | Establish info channel across infrastructure; beacon presence for rover guidance
Localization module | Broadcast geolocation of self | Facilitate construction process; label/tag structure on habitat map

## Slide 6: Approach
Energy harvesting technologies to prolong sandbag lifetime
Charging Technology | Pros | Cons
Induction coupling | Simple implementation High efficiency | Precise alignment required Short charging distance (mm to cm)
Magnetic resonance coupling | Charges multiple devices simultaneously High charging efficiency Non-line-of-sight charging | Limited charging distance (cm to m) Complex implementation
RF radiation charging | Long charging distance (m to km) No alignment required | Line-of-sight transmission Unsafe for human if high power Low efficiency
Thermoelectric | No extra infrastructure required Passive harvesting method | Low power output Somewhat complex implementation

## Slide 7: Results
Demo: Sandbags implemented with force sensors

## Slide 8: Results
Superadobe construction using pick-and-place rovers
Yinan Xu, SpaceTREx
University of Arizona
Joseliz Perez, SpaceTREx
University of Puerto Rico

## Slide 9: Results
Proximity sensors improves construction process efficiency
Linear Layering
Random Placement
Proximity Sensors
Simulation of constructing a 10x10 sandbag wall
(green = sandbag, red = holes)

## Slide 10: Results
ANSYS simulation for sandbag structural and thermal analysis
Superadobe with
ANSYS static structural solver
Superadobe physical thermal modeling
 | External wall
 | Internal wall
 | Internal ground
 | Rover surface
 | External ground
 | External wall
 | Internal wall
 | Internal ground
 | Rover surface
 | External ground

## Slide 11: Results
From the initial structural studies, the material density and yield strength has the most affect on the equivalent stress.

## Slide 12: Results
 | External wall
 | Internal wall
 | Internal ground
 | Rover surface
 | External ground
 | External wall
 | Internal wall
 | Internal ground
 | Rover surface
 | External ground
Superadobe physical thermal modeling
Superadobe thermal circuit

## Slide 13: Distributed Processing Network
With microprocessors and antenna in sandbags, they could be utilized as a distributed processing network to offload routine and mundane tasks (e.g. monitor important parameters, structure maintenance)
Centralized processing resource is vulnerable in the unforgiving lunar surface

## Slide 14: Conclusion
Smart sandbags to provide semi-permanent shelter
  Cheaper alternative for expanding lunar habitat
Smart sandbags offload tasks from mobile systems and astronauts
  A more robust processing system
  Versatility of sandbags with different config. of electronics

## Slide 15: Future Work
Test structural integrity of sandbag structures
  Accurately scale down to simulate lunar gravity on Earth
Prototype sandbags embedded with electronics
  Material requirements
  Mass/Volume/Cost estimates
Investigate fibers from lunar regolith
  Further step in ISRU

## Slide 16
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory

## Slide 17
Asteroid Science, Technology and Exploration Research Organized
by Inclusive eDucation (ASTEROID) Center