## Slide 1: Hardy Tree-Mounted Loop Antenna for the Tree of Life Mission
ISSC 2022, California Polytechnic State University, May 3rd, 2022
Charles Penny*, Alessandra Babuscia*, Steven Anderson, Julia Christensen**, Steve Matousek*, Roger Klemm*,
* Jet Propulsion Laboratory, California Institute of Technology; **Oberlin College
Notes: INSERT© 2022 California Institute of Technology. Government sponsorship acknowledged.
INSERT NASA Meatball logo
INSERT Conference Date and Details

## Slide 2: Outline
Motivation
Project Background
Objectives
Prior Research
Methods
Some Results
Changes
More Methods
More Results
Discussion/Moving Forward

## Slide 3: Motivation (1/2)
The Tree of Life Mission:
Interstellar missions may last
200+ years
How do we design craft to last for such durations?
How do we design missions to last for such durations?
Proxima Centauri – Image taken by the Hubble Space Telescope

## Slide 4: Motivation (2/2)
Combine space and Earth science missions of similar duration
  Diversify sources of interest
  Crowdsource ground station upkeep
Trees can have long lifespans
  Trees became focus of Earth science
Upgradeable tree-based antenna and ground station
200-year CubeSat designed for longevity
Tree health/environment data
CubeSat ‘health’/environment data
Credit: Space Song Foundation
Notes: INSERT Motivation (2/2)

## Slide 5: Project Background – Tree Antenna
CON – Trees are somewhat unpredictable regarding location, shape, etc.
CON – Trees exhibit non-constant electrical and physical properties
PRO – Antenna has close proximity to data collection station and high mounting location
PRO – Tree-Antenna system has somewhat improved beamwidth for an uncomplicated antenna
Daniel Tam and John Rockway - US Patent No. 8,094,083
Steven Anderson – Tree of Life Antenna concepts (2020)
Notes: Maybe mention that other approaches seek to use the tree as an antenna, only coupling branches with current sensors

## Slide 6: Objectives
Design antenna that is hardy to an on-tree environment
To do this we must
1. Understand typical tree conditions
– namely electrical properties
2. Characterize antenna performance in typical conditions
Notes: CHANGE Minimize - > Understanding
CHANGE Characterize antenna performances in typical tree conditions

## Slide 7: Prior Research (1/2)
Diurnal and Spatial Variation of Xylem Dielectric Constant in Norway Spruce (Picea abies [L.] Karst.) as Related to Microclimate, Xylem Sap Flow, and Xylem Chemistry
Kyle C. McDonald, Reiner Zimmermann, and John S. Kimball
Automated Instrumentation for Continuous Monitoring of the Dielectric Properties of Woody Vegetation: System Design, Implementation, and Selected In Situ Measurements
Kyle C. McDonald, Reiner Zimmermann, JoBea Way, William Chun

## Slide 8: Prior Research (2/2)
Diurnal and Spatial Variation of Xylem Dielectric Constant in Norway Spruce (Picea abies [L.] Karst.) as Related to Microclimate, Xylem Sap Flow, and Xylem Chemistry
Kyle C. McDonald, Reiner Zimmermann, and John S. Kimball

## Slide 9: Methods - Simulation
Ansys HFSS models aiming to represent different layers of tree tissue and foliage

## Slide 10: Some Results – Antenna Sensitivity to Tree Properties
Changing dielectric results in shifting resonant frequency
Deformation due to gradual tree growth ruins antenna
Antenna is very sensitive to tree’s changes!

## Slide 11: Minimizing Impact
Decrease volume of tree enclosed by loop antenna
Decrease deformation caused by tree growth
Simulate design in HFSS for varied conditions
Notes: CHANGE - effects

## Slide 12: Impact Minimization
Simulation sweeps of tree dielectric values for varying tree area show more consistent antenna performance for smaller tree areas
Chart: Standard Deviation of S11 Values vs Fraction of Antenna Filled with Wood
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0.069611 | 0.03163 | 0.054529 | 0.68712 | 1.3606 | 2.1111 | 4.2391 | 5.7829 | 5.5328 | 4.7236

## Slide 13: Design Changes
  Reduces tree branch size enclosed
  Spring absorbs deformation instead of antenna
  Wider range of fitting branches due to spring mount

## Slide 14: How do we know our simulations are any good?
Testing!

## Slide 15: More Methods – Testing in Typical Conditions
How will the Antenna react to real life dielectric shifts?
Is our simulation model accurate?
Antenna on tree, VNA, raspberry pi, battery, and solar panel in bucket

## Slide 16: Typical Conditions Results/Analysis
Chart: 

## Slide 18: Antenna Performance vs Environmental Factors
Data generally showed high correlation to ambient temperature and solar radiation
Chart: Temperature Line Fit Plot
Chart: Radiation Line Fit Plot

## Slide 19: Antenna Performance vs Environmental Factors
Antenna performance seems to be powerful indication of tree’s environment

## Slide 21: Discussion
Antenna design changes successfully minimize effect of tree activity on antenna performance
-antenna is also generally less sensitive than in simulation
Antenna performance still reflects tree activity
Chart: 
Notes: CHANGE Conclusion Next steps

## Slide 22: Moving Forward
A Tree-Antenna as a Tree-Transducer?
Further development of the system
  Multi-branch array
  Multi-tree array
  Testing against ‘open-source’ 433MHz satellites

## Slide 23: Acknowledgements
Thanks to Alessandra Babuscia for her mentorship!
Thanks to all the former interns who worked on this and whose work laid the foundation for everything I have done!
Inge Baho - Thomas Choi - Steven Anderson
Thanks to Dr. Kyle McDonald for insight into the dynamic properties of trees!
Thanks to The Tree Song Foundation for involving me!
Thanks to Dr. Jekan Thanga and SpaceTREx Labs for supporting this research!

## Slide 24: Thank you!
for your time

## Slide 25: References
https://www.spacesong.org/
Q. Xiao and E. G. McPherson, “Tree health mapping with multispectral remote sensing data at UC Davis, California,” Urban Ecosystems, vol. 8, no. 3-4, pp. 349–361, 2005. https://link.springer.com/article/10.1007/s11252-005-4867-7
M. Acker, K. Ikrath, and W. A. Schneider, “HELICAL COIL COUPLED TO A LIVE TREE TO PROVIDE A RADATING ANTENNA,” 29-Feb-1972. https://patentimages.storage.googleapis.com/31/f8/8b/e11a188592e001/US3646562.pdf
D. W. S. Tam and J. W. Rockway, “MULTI-BAND TREE ANTENNA,” 10-Jan-2012. https://patentimages.storage.googleapis.com/19/cf/0f/424d5e0be1614f/US8094083.pdf
I. Baho, rep. “Tree of Life: Designing and Simulating the Antenna Tree,” 2019.
T. Choi, rep. “Tree Antenna Report,” 2020.
S. Anderson, rep. “Tree of Life: A Multi-Generational Telecommunication Concept”, 2021.
K. C. McDonald, R. Zimmermann, J. Way, and W. Chun, “Automated instrumentation for continuous monitoring of the dielectric properties of woody vegetation: System design, implementation, and selected in Situ Measurements,” IEEE Transactions on Geoscience and Remote Sensing, vol. 37, no. 4, pp. 1880–1894, 1999.
K. C. McDonald, R. Zimmermann, and J. S. Kimball, “Diurnal and spatial variation of xylem dielectric constant in Norway spruce (picea abies [l.] karst.) as related to microclimate, xylem sap flow, and xylem chemistry,” IEEE Transactions on Geoscience and Remote Sensing, vol. 40, no. 9, pp. 2063–2082, 2002.