## Slide 1
A DSN Retrospective:
CubeSat Support for Lunar Flashlight
Kristofer Buckmaster, Krisjani Angkasa
May 1, 2023

## Slide 2: Agenda
Introduction and Background
Summary of DSN Services for Lunar Flashlight
What Did We Do Well?
What Can We Do Better?
Conclusions and Path Forward
Notes: The framework of this presentation draws inspiration from agile methodologies – specifically, the ceremony of a scrum retrospective, which is typically conducted at the end of a work interval, also known as a sprint.
For those unfamiliar with agile development, we conduct retrospectives immediately after a sprint so that we can quickly adapt how we work, to become more effective and efficient in future intervals by reinforcing our good habits and eliminating our bad ones.

## Slide 3: Introduction and Background
The BLUF
Background on the Deep Space Network
Overview of the Lunar Flashlight Mission
About the Authors

## Slide 4: Introduction and Background
The BLUF
Bottom Line Up Front
  The DSN provides standard services for Lunar Flashlight, and initial acquisition was a success!
  Kudos to the team for the years of work and collaboration that went into preparing for tracking support, the flexibility to accommodate multiple launch slips, and for how calmly the Ops teams handled the issues encountered during the initial acquisition support.
  Lunar Flashlight continues to leverage DSN services for mission operations.

## Slide 5: Introduction and Background
The Deep Space Network
The Deep Space Network - or DSN - is NASA’s international array of giant radio antennas that supports interplanetary spacecraft missions, plus a few that orbit Earth. The DSN also provides radar and radio astronomy observations that improve our understanding of the solar system and the larger universe.
The DSN consists of three facilities spaced roughly equidistant from each other – approximately 120 degrees apart in longitude – around the world. These sites are at Goldstone, near Barstow, California; near Madrid, Spain; and near Canberra, Australia. The strategic placement of these sites permits constant communication with spacecraft as our planet rotates – before a distant spacecraft sinks below the horizon at one DSN site, another site can pick up the signal and carry on communicating.
The DSN is operated by NASA's Jet Propulsion Laboratory (JPL), which also operates many of the agency's interplanetary robotic space missions.

## Slide 6: Introduction and Background
Overview of the Lunar Flashlight Mission
Roughly the size of a briefcase, Lunar Flashlight is a very small satellite developed and managed by NASA's Jet Propulsion Laboratory using near-infrared lasers and an onboard spectrometer to map ice in permanently-shadowed regions near the Moon's south pole. The observations made by the low-cost mission will provide unambiguous information about the presence of water ice deposits inside craters that would be a valuable in-situ resource for future Artemis missions to the lunar surface.
As a technology demonstration mission, Lunar Flashlight showcases several technological firsts, including being the first mission to look for water ice using a laser reflectometer and the first planetary CubeSat mission to use "green" propulsion - a propellant that is less toxic and safer than hydrazine (a common propellant used by spacecraft).
The mission was selected by NASA's Advanced Exploration Systems in 2014 and is currently funded by the Small Spacecraft Technology program within NASA's Space Technology Mission Directorate.
After missing the integration window to launch with the Artemis-1 mission, Lunar Flashlight was eventually remanifested to launch as a rideshare with the Hakuto-R Mission on a SpaceX Falcon 9 rocket. Lunar Flashlight launched on 11-December-2022.

## Slide 7: Introduction and Background
Overview of the Lunar Flashlight Flight System
6U CubeSat Form Factor
Power
  Trifold deployable solar arrays
Propulsion
  4 Thrusters
Attitude Control System (ACS)
  Reaction Wheels, Star Tracker, Coarse Sun Sensors
Telecom
  Iris ver. 2.1 X-band Transponder
    Supporting Doppler, Sequential Ranging, and DDOR
  Low Gain Antennas
  Low Noise Amplifiers & Solid State Power Amplifiers

## Slide 8: Introduction and Background
About the Authors – DSN Mission Interface Management
A Mission Interface Manager (MIM) acts as a DSN Service Provider representative to interface with mission customers - from early planning through design, development, testing, flight operations, and closeout.
Responsible for the provision of DSN Operations support.
Kris “A” has 30 years of experience in the space industry. Currently a Program Manager in JPL’s Interplanetary Network Directorate
Kris “B” has nearly 20 years of DSN experience, in various roles.
Notes: 30 years in space industry - Payload Systems Engineer at Hughes - Tenure at JPL includes: DSN Receiver CogE, Iris Radio CTM, DSN MIM for flagship mission such as M2020 and CubeSat ride share mission such as Lunar Trailblazer. Currently serves as a Program Manager at JPL IND

## Slide 9: DSN Services for Lunar Flashlight
Overview
DSN Standard Services:
  Command, Telemetry, and Tracking services for Lunar Flashlight.
  Network support that allows connectivity between DSN assets & the Mission Operations Center (MOC) located at Georgia Tech.
  JPL Engineering Support for Mission Critical Events.
  RF Compatibility Test Support, to validate the RF interface between Lunar Flashlight and DSN, and signal processing for the Command, Telemetry, and Tracking functions.

## Slide 10: DSN Services for Lunar Flashlight
Telemetry Frame Service
Telemetry Frame Service
  DSN acquires and processes turbo-encoded transfer frames compliant with CCSDS Telemetry AOS Space Data Link Protocol (732.0-B-2).
  DSN delivers transfer frames using CCSDS Space Link Extension – Return All Frames Service Specification (911.1-B-3).
  DSN has supported downlink rates up to 128 kbps from Lunar Flashlight.

## Slide 11: DSN Services for Lunar Flashlight
Command Radiation Service
Command Radiation Service
  Command data, in the form of Command Link Transmission Units, are received from the MOC via CCSDS SLE Forward CLTU service (912.1-B-4).
  Stream Mode ensures timely radiation of the command data.
  Command Data Rates and Modulation are controlled with throw events, invoked through the NASA AMMOS Software running an SLE client application used in the MOC.

## Slide 12: DSN Services for Lunar Flashlight
Tracking Services
Tracking Services
  Tracking Services provide radio metric observables from which the position and velocity of the Lunar Flashlight can be derived.
  Tracking Data Types include: Doppler, range, and DDOR.
  File and Stream Delivery Mode via DSN Interface TRK-2-34 specification.
  Utilizing both ”classic” DDOR and PN DDOR techniques.
Notes: Delta-DOR using a wide-band pseudo noise (PN) sequence instead of sinusoidal tones. Each of these DOR tones, or PN sequence, is recorded at two stations simultaneously. Nearly contemporaneously, a quasar is observed with the same pair of stations (this may be done in the pattern quasar-spacecraft-quasar, spacecraft-quasar-spacecraft, quasar-spacecraft_1-spacecraft_2-quasar, etc.). The signals are analyzed afterwards to calculate the delta-DOR observable.

## Slide 13: What We Did Well (1 of 3)
Service Provision with a New MOC
Implemented service interfaces with Georgia Tech & conducted a comprehensive validation campaign prior to launch.
Initially, the Lunar Flashlight MOC was planned at JPL. The Georgia Tech MOC required new ground communication infrastructure and NASA Cybersecurity Review.
Notes: IPsec is a network layer security protocol that protects IP packets with cryptographic integrity and confidentiality processing and replay detection.

## Slide 14: What We Did Well (2 of 3)
Service Provision with a New MOC
Key Accomplishments
  Successful service interface testing with 17 different deep space stations between 3-Jan and 11-Oct-2022.
  Validated mission control software tools using simulated data flows.
  Conducted Operational Readiness Testing to exercise fault responses and reporting.
  Drafted and approved a NASA Agency Interconnection Security Agreement within 45 days.
Notes: ISA signatures were contingent on NASA assessment of the GT cybersecurity policies and procedure. The ATO (authorization to operate) was approved on November 8; just over a month before we ultimately launched.

## Slide 15: What We Did Well! (3 of 3)
Initial Acquisition
DSS-35 acquired the downlink signal and established a two-way communications link that enabled the project to command the spacecraft out of the initial safe-mode sequence, and receive telemetry about the spacecraft health and status.
The Ops team at Georgia Tech did an outstanding job communicating the operating modes and expected observables from their Iris radio, along with potential off-nominal conditions.

## Slide 16: What Didn’t Go Well? (1 of 2)
Launch Trajectories and DSN Asset Scheduling
Problem: Launch trajectory details (ephemerides) came relatively late in the DSN Schedule Negotiation process.
  DSN Assets are not scheduled without viewperiods generated from a spacecraft ephemeris.
  After missing the integration with Artemis, preliminary forecasts targeted launch NET Spring 2023.
What Can We Improve?
  There were multiple organizations between the data producer (SpaceX) and the recipient (DSN). If DSN will be the primary ground support network, missions and launch service providers should be mindful of the DSN scheduling process and time horizons for schedule negotiation. Ask your friendly MIM for additional details.

## Slide 17: What Didn’t Go Well? (2 of 2)
Problem: A misconfiguration in a DSN support table caused the station to conduct a valid-but-incorrect uplink frequency sweep, resulting in an unexpected bias in the downlink frequency.
Corrective Action: Once the misconfiguration was identified, the parameter value was changed, and subsequent tracks were nominal.
What Can We Improve?
  Rigorous peer review is a hallmark of JPL and DSN processes. However, engineering support for CubeSats and Small Sats has been historically constrained by smaller budgets that limit the size of teams and expertise that can participate. DSN is actively gathering lessons-learned to augment our approach to reviewing CubeSat preparedness and support readiness.
80kHz Bias During Initial Contact

## Slide 18: Conclusion & Path Forward
DSN continues to provide support for on-going Lunar Flashlight operations, as the mission is now targeting lunar flybys (as opposed to lunar orbit) due to glitches in the thrusters.
Mission Operations now schedule routine and unattended tracks with the DSN.
MIMs will continue to leverage world-class JPL/DSN expertise to provision communications services and prepare for future missions, facilitating process improvements with lessons learned from our experiences with CubeSats like Lunar Flashlight.