## Slide 1: Downsizing Mission Design for CubeSats
Presenter: Dan Grebow
May 1, 2023

## Slide 2: Interplanetary CubeSats
Relatively cheap
Risk more tolerable
Investment & risk worth the return
Artemis I CubeSats
MarCO
NEAScout
Lunar Flashlight

## Slide 3: Some Mission Design Challenges
Mission design does not scale down with spacecraft size
CubeSats must adapt on a whim to prime mission launch targets
CubeSats generally have more limited propulsion capabilities
CubeSats have greater chance of post-launch anomalies
Due in part to these challenges, we believe it is important to find ways to scale down mission design for CubeSats

## Slide 4: Descope Mission Objectives
Mission design preparations should focus on satisfying a descoped objective
Going beyond the descoped objective should be considered more as adapting “on the fly”
Notes: Example descoped objectives: (1) NEAScout should simply try to unfurl the sail and see if a maneuver can be designed (2) Lunar Flashlight should simply try to do one pass over the south pole of the moon

## Slide 5: Find the Right Team
The mission design team should be small and experienced
The team should have a reliable suite of generic mission design software tools

## Slide 6: Tolerate More Risk
Do not design everything to 99th percentile
And don’t be precise about it
  Don’t waste time try to obtain an exact percentage of success
  Use fewer Monte Carlo samples than is normally acceptable
Design-to
% Success
100%
1%
Deploy & establish contact
Maneuver w/ sail
Navigate toward asteroid
Image asteroid
Flyby asteroid
Achieve minimal science
Achieve full science
Unfurl sail
Example Solar
Sail Mission to Asteroid

## Slide 7: Avoid Over-Preparing
Avoid extensive, unnecessary analyses
  Examples: High-fidelity Monte Carlo studies, esoteric trade studies
Minimize contingency studies and cut away number of back-up trajectory options
For a given day in the launch period, preparation should be proportional to the probability launch

## Slide 8: Fly Imperfect Designs
Use low-fidelity trajectory models whenever possible
  Example: Two-body propagations with impulsive maneuvers
Accept sub-optimal trajectories
  Having the perfect, globally optimal trajectory is time consuming and often unnecessary
  For high-thrust use rules of thumb for maneuvers
  For low-thrust use well-known control laws whenever possible

## Slide 9: Be Capable of Adapting “On the Fly”
Be mentally prepared for designing an entirely new mission
  Don’t fall too much in love with a particular design
Rely on astrodynamics intuition
Notes: Relying on intuition requires an experienced team

## Slide 10: Know When to Let Go
When the spacecraft is ailing, don’t spend copious amounts of time trying to recover the mission
Let go sooner than you would for a larger-scale mission

## Slide 11: Conclusion
Nearly all these recommendations boil down to accepting more risk in mission design
Reducing mission design cost becomes a selling point for SmallSat and CubeSat missions
  Mission enabling; even greater return on investment
Stakeholders not willing to accept more risk must expect to pay more for mission design
  In the event of anomalies or failure, chance of significant wasted cost