## Slide 1
The Tree of Life Project
Tree-Mounted Antenna
and Accessible Ground Station
Charles Penny,
Interplanetary Small Satellite Conference 2023
May 1 – 2, 2023

## Slide 2: Project Background – The Tree of Life
A Multigenerational Mission
Sustaining a mission in LEO for an extended period (ultimately multigenerational)
Sustaining ground-based support during that extended period
Performing citizen science simultaneously
  Dendrology
  Climate
Credit: Space Song Foundation

## Slide 3: Project Background – Tree Antennas
Historically, current probe and toroidal antennas were tested on trees
Performance tradeoffs from tree-mounting
  Tree branches constrain size
  Attenuation/scattering from foliage
  Trees have varying dielectric properties (they are alive!)
Previous JPL internships (Inge Baho, Thomas Choi, Steven Anderson) simulated loop antennas and refined design for on-tree deployment
Patent No 3,646,562 1972
Patent 8,094,083 B1 2012
early simulation setups

## Slide 4: Project Background – Prior Work
Further design adaptions were made to decrease the sensitivity of the antenna’s parameters to the widely varying dielectric values of a tree
Simulation and testing of antennas on trees was done that confirmed the success of the design adaptions

## Slide 5: Recent Goals
Determine methods to improve performance
  Arrays
  Design Adjustments
  Ease of Reproducibility
Perform proof of concept on these improvements

## Slide 6: Performance Improvements via Arrays
Gradually diminishing returns on adding antennas
Antenna relative placement plays a big role
Chart: Sky Coverage for Arrays
| 1 | 2 | 3 | 4 | 5
Coverage(High) | 18 | 32 | 64 | 80 | 92
Coverage (Low) | 12 | 20 | 32 | 44.4444 | 63.8889
1-antenna sky coverage
5-antenna sky coverage
Results

## Slide 7: Design Alterations
- No large 3d printed parts
- 90% reduction in print time
- Fully enclosed antenna port
This does not change the rf performance of the antenna, but does make it more accessible

## Slide 8: Improvements Proof-of-Concepting
Satellite Stand-In Testing Method
Sample test locations around the tree
In lieu of relying on satellite passes to consistently test performance, a “transmitter-on-a-stick” is initially used to observe the ground station performance
Transmitter with omnidirectional stub antenna affixed to PVC pipe

## Slide 9: Improvements Proof-of-Concepting
System Deployment
System can use 1-3 antennas
Affixed to tree via paracord with recycled 2-liter bottles providing spacing and isolation between antennas and branches

## Slide 10: Improvements Proof-of-Concepting
In Comparison to an Omnidirectional Reference Antenna
Reference antenna results
Tree-antenna results
Sphere size proportional to signal strength
Green spheres represent RSSI > -60dBm
Yellow spheres represent RSSI < -60dBm
Red circles represent failure to receive signal from test location
Tree antenna-based ground station performed marginally better than reference antenna
Reference antenna seemed to be blocked by branches which the tree antennas mounted to

## Slide 11: LEO Proof-of-Concepting
Satellite Reception Testing Method
Utilize existing network of open source CubeSats and SmallSats
Compare ground station performance to that of other open-source ground stations
Verify LEO downlink capabilities

## Slide 12: LEO Proof-of-Concepting
Satellite Reception Testing Results
Satellite downlink was achieved with mixed success
~30% of satellite passes were not observed
  i.e. LOS theoretically existed between tree and satellites with no downlink
~50% of observed passes had CRC error (points in red)
All downlinks had RSSI less than -100dBm – not reliable

## Slide 13: Conclusion
Tree based antenna and ground station can work
  A ground station that is not centered on a tree will work better
  Can outperform antennas not designed for use on a tree – tree adaptations somewhat successful
System needs reliability improvement
  30% of satellite passes missed
  50% downlink rate of observed passes
  35% overall success rate
  Currently not suited for mission critical infrastructure

## Slide 14: Future Work
Work on this project will continue under the Space Song Foundation and their mission: https://www.spacesong.org/
LEO downlink capabilities demonstrated here are being incorporated into their existing tree-sensor system which will use a Raspberry Pi and commercially available SDR and LNA dongles
This will hopefully lead to citizen science and hands-on learning opportunities!
Space Song Foundation visualization of tree sensor data

## Slide 15: Acknowledgments
Major thanks to my fantastic mentor Alessandra Babuscia!
Thank you to past Tree of Life Interns Inge Baho, Thomas Choi, and Steven Anderson for building a foundation for my internship!
Thank you to Steve Matousek, Julia Christensen, Roger Klemm, Joel Ferree, and the entire Space Song Foundation for letting me participate in their epic mission!
Thank you to Dr. Kyle McDonald for providing insight into trees!
Thank you to the contributors to TinyGS, their open-source software was extremely helpful in setting up tests!

## Slide 16
Thank You for Listening!

## Slide 17: References
J. Christensen, “MISSION ,” THE TREE OF LIFE. [Online]. Available: https://www.thetreeoflife.space/mission/.
S. D. Anderson, “Infrastructure Design Concepts for Space Permanence,” Thesis, 2021
M. Acker, K. Ikrath, and W. A. Schneider, “HELICAL COIL COUPLED TO A LIVE TREE TO PROVIDE A RADATING ANTENNA,” 29-Feb-1972. https://patentimages.storage.googleapis.com/31/f8/8b/e11a188592e001/US3646562.pdf
D. W. S. Tam and J. W. Rockway, “MULTI-BAND TREE ANTENNA,” 10-Jan-2012. https://patentimages.storage.googleapis.com/19/cf/0f/424d5e0be1614f/US8094083.pdf
I. Baho, rep. “Tree of Life: Designing and Simulating the Antenna Tree,” 2019.
T. Choi, rep. “Tree Antenna Report,” 2020
Brown, G. S., and W. J. Curry (1982), A theory and model for wave propagation through foliage, Radio Sci., 17(5), 1027–1036, doi:10.1029/RS017i005p01027.