## Slide 1
Commercial Lunar Payload Services (CLPS) Lander S-Band User Terminal
Faramaz Davarian, Mazen Shihabi, Matt Chase, Emmanuel Decrossas, and John Baker (JPL)
Stuart Golden and Kevin Lynaugh (Vulcan Wireless)
May 1, 2023
Interplanetary Small Satellite Conference 2023

## Slide 2: One Small Step for Radio, one giant leap for Earth-Moon communications
When Neil Armstrong uttered one of the most famous sentences in human history, he did so via a microphone in his helmet and a 3-kilogram VHF-band radio in his backpack.
The radio linked to a rig in the lunar lander, which launched microwave signals on a 325,000-kilometer journey to Earth.
A memorable feature of the Apollo communication system was the S-band erectable antenna, which was connected to the lunar module’s radio system.
Stowed as a cylinder 25 by 100 cm, it was unfurled on the moon into a 3-meter-diameter dish covered with a fine, flexible, gold-plated mesh.
The erectable antenna had a transmit gain of 34 decibels.
The higher gain was needed to accommodate color-TV signals, along with the voice and data channels.
Credit: IEEE Spectrum

## Slide 3: Now Earth-to-Moon communications are poised for a new era
Earth’s moon is the target of more missions than at any time
NASA, for example, has plans to visit the moon using both robots and humans, and is also considering—with international collaborators—an orbiting outpost in the next decade, known as the Lunar Gateway
Lunar Gateway is only one of over 90 lunar missions being considered for the years between now and 2030.
And this is only the beginning: It is anticipated that interest in the moon will accelerate, eventually culminating in a permanent human presence on the surface, where lunar occupants will need to stay in touch with Earth.
While direct radio communication with Earth was used during the Apollo missions, it doesn’t work in every possible situation; for example, the moon’s far side, as well as large portions of its poles, have no direct line of sight to Earth.
The proposed Lunar Crater Radio Telescope would convert a crater on the moon’s far side into a 1-kilometer dish-shaped antenna.
The proposed FARSIDE telescope would use unspooled antennas across an area of the moon’s surface 10 km in diameter to create a large interferometric array.

## Slide 4: Relay Communications from the Moon If a lunar orbiter were available, the Apollo mission could have used a much smaller antenna
Enable communications from the far side
Enable communications from polar regions without direct line-of-site to Earth
Improve communications from the near side
Provide for Moon-to-Moon communications
Image Credit: SSTL

## Slide 5: Overview of Relay Proximity Protocol and the Need for Extension to the Lunar Enterprise

## Slide 6: Proximity Communications at the Moon: CCSDS Proximity-1 Standard
The present CCSDS standard applies to the UHF band at Mars
At the Moon, UHF usage has limitations in order to protect radio astronomy from harmful interference
SFCG has designated the S-band: Return (2200 – 2290 MHz) , and Forward (2025-2110 MHz) for lunar proximity communications
  SFCG also has Ka-band designation for the proximity links.
The Martian frequency spectrum environment is different from the Moon
  There will be many more users on the Moon
  Higher proximity data rates are likely to be used at the Moon
  Lunar closeness to Earth requires avoidance of interference with terrestrial radios (surface and orbit)
  Spilling over the adjacent band would not cause a problem at Mars because there are no adjacent band users
Because of the above differences, an extension of the Proximity-1 standard, with new frequency bands, should be developed for the Moon by CCSDS (in progress)

## Slide 7: Extending Prox-1 to S-Band Frequencies with the Following Modulation, Coding, and Frame Format
*In addition to the proposed coding options in the above table, other LDPC code rates and block lengths may be considered if deemed appropriate by CCSDS
*
One frame format for TC, TM, & proximity

## Slide 8: Lunar User Terminal Architecture

## Slide 9: What Next: A low-Cost Communications User Terminal (UT) for Lunar Applications
NSR-SDR S-Band Radio
S-Band Antenna
UT development is funded by NASA as a low cost system to be used by future lunar payloads for their communication needs and it consists of:
  S-Band Software Defined Radio (SDR) with 4-W built-in amplifier
  One S-Band Antenna
  8x1 Data Switch that supports Ethernet or serial interfaces to provide communication connectivity for multiple on-board commercial and scientific payloads
  Dummy data source (as an input to one of the Switch ports) for commissioning the Switch.
The UT will be compatible with the Lunar Pathfinder relay as well as other future relays adopting S-band proximity communication standards
The first launch of the UT will be on CS-3, where two units will fly, one for LPF commissioning, and another for LuSEE communications through the Lunar Pathfinder (LPF) orbiter.
8x1
The UT with its 8-pole switch can connect multiple payloads to the radio using either IP or RS-422 port
.
.
.

## Slide 10
The first UT flight is scheduled for 2025 to the far side of the Moon
One UT for commissioning LPF
  In orbit commissioning
  Lunar surface commissioning
  This UT is powered by the lander and will be powered off along with the lander at the end of the first lunar day per LuSEE science operation requirements.
Another UT, part of the LuSEE payload, to provide proximity communications for LuSEE for a year starting from the first lunar night after landing.
CS-3 Mission
LPF
11-hour frozen orbit
Lunar Surface
CS-3 Mission
Credit: SSTL

## Slide 11
Commands requesting simulated science data from the UT dummy source, onboard the CLPS lander (CS-3), will be transmitted to Goonhilly station
Goonhilly and other ground stations (TBD) will radiate the commands to LPF to be transmitted to the UT
UT will package data and send them back to JPL through LPF/Goonhilly
JPL will provide end-to-end commissioning for LPF

## Slide 12: UT Setup Options and the CLPS Lander
Single-User
Multi-User
LPF Commissioning

## Slide 13: More on the UT Features and Specifications

## Slide 14
Radio Specifications for the NSR-SDR-S/S-JPL-UT
Parameter | Specification | Comments
Frequency Forward (Rx) Reverse (Tx) | S-Band 2025-2110 MHz 2200-2290 MHz | 
Frequency Channels Forward (Rx) Reverse (Tx) | TBD TBD | Specific frequency channels to be specified by SSTL. Radio will be configured appropriately
Data Rate (bps) Forward & Reverse | 1, 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048, 4096 kbps | Coded bit rate. Note information rate is less. Scale coded bit rate by coding rate to get information rate. E.g. multiply by 2/3.
Modulation Forward & Reverse | PCM Bi-Phase-L, 60°or GMSK | GMSK used for higher rates only
Coding | LDPC Rate 2/3 or uncoded | 
RF Power | 1 Watts RF 4 Watt RF | Power can be lowered from maximum in 0.25dB steps. (open loop leveling)
Max Receiver Input Power | +3 dBm | No damage
Typical Receiver Power | -60 dBm to -135 dBm | 
Protocol | CCSDS USLP Framing | Type 4 Frames: Superset of TC and TM and AOS Space Protocols
Duplex Communications | Full Duplex | Standard
Frequency Tolerance | +/- 1ppm | Over Temperature and 20 years Aging

## Slide 15
Parameter | Specification | Comments
Temperature Operational Storage | -25 to 60C -40 to 85C | Measured at Baseplate of Radio, tested with thermal couple on base plate
Polarization | RHCP or LHCP | Defined by antenna system
Flight Computer Interface | RS-422 UART-serial Or Ethernet | Standard options other options available.
DC Power -DC Power -DC Current | 12 Volt Option 8Vdc-16Vdc 1550 mA | 28V Option 12 Vdc- 36 Vdc 700 mA
DC Power Rx Rx Tx Full Duplex | < 2Watt Average 3.7 Watts Nominal/ 14.8Watts DC at 4W RF 18.5Watts DC at 4W RF | Duty Cycle Rx Only Rx Only Tx Only (+/-5% over Frequency)
Compatible Service Providers | SSTL CLMSS | Contact Vulcan Wireless for additional connectivity options.
Radio Specifications for the NSR-SDR-S/S-JPL-UT contd.

## Slide 16: Conclusion
The User Terminal development is funded by NASA to provide future lunar payloads access to inexpensive, small size and mass lunar comm system that can be purchased at low cost and on a short schedule basis
It will be fully compatible with the Lunar Pathfinder relay and the CCSDS S-band Lunar Proximity-1 Standard
Two copies of the UT will fly on CS-3:
  One to support LPF commissioning and
  Another to provide a communications system for the LuSEE payload.