## Slide 1
Simultaneous Tracking and Navigation Solution for 8 CubeSats using the DSN’s Open Loop Receiver
Daniel Kahan, Dustin Buccino, Elias Barbinis, Clement Lee, Meegyeong Paik, Oscar Yang, Walid Majid, Gerhard Kruizinga, Shan Malhotra, Douglas Abraham
2023 Interplanetary Small Satellite Conference, May 1-2, 2023
© 2023 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Artemis I Mission Overview
https://www.nasa.gov/exploration/systems/sls/launching-science-and-technology-on-nasa-s-artemis-i-mission.html

## Slide 3: Communications Challenges
Of the 10 cubesats on Artemis, 8 communicate through NASA’s Deep Space Network (DSN)
DSS-14 (70m)
DSS-25
DSS-24
DSS-26
DSS-63 (70m)
DSS-54
DSS-53
DSS-55
DSS-56
DSS-43 (70m)
DSS-35
DSS-34
DSS-36
DSS-65
DSN antennas support Artemis, plus cubesats, plus already-flying deep space missions
Multiple Spacecraft Per Aperture (MSPA) can receive data from 4 missions within the same beam
  But only downlink, limited to single uplink

## Slide 4: DSN Scheduling Considerations
Uplink Demand vs. Supply Analysis for 4-MSPA During Earth-Moon Transit
(First 40-Hours, Not Accounting for Beam Exits, Accounting for DSS-17 and JAXA Antennas)
Downlink Demand vs. Supply Analysis for 4-MSPA During Earth-Moon Transit
(First 40-Hours, Not Accounting for Beam Exits, Accounting for DSS-17 and JAXA Antennas)
Downlink demand at times is more than double supply.
Uplink demand almost always exceeds supply, sometimes by a factor of 4 or more.
2-way Doppler & ranging requests overwhelm what 4-MSPA alone can supply. Need to facilitate navigation with a less uplink-intensive navigation technique.
How can we navigate without 2-way Doppler and ranging?
Downlink Demand Analysis
Uplink Demand Analysis

## Slide 5: Interferometric Narrowband Spacecraft (INS)
Two DSN stations (A and B) track simultaneously Cubesat One-Way Doppler. Two One-Way Doppler measurements are differenced by the navigation team (NAV) to form INS measurement

## Slide 6: Two-Way Doppler vs INS Tracking Data Comparison
Two Way Doppler | INS
Requires one DSN station | Requires two DSN Stations
Requires uplink and downlink | Requires only downlink
Measurement can be made any time in the pass | Measurement can only be formed when the cubesat is in view for two DSN complexes
Tracking data require no post pass processing | Requires post pass processing by combining One-Way Doppler from two DSN stations into INS measurements
Data content independent from cubesat distance to Earth | Data content diminishes as the cubesat distance to Earth increases
Can use closed-loop or open-loop, limited by MSPA number | Possibility of using Open Loop Receivers (OLR) allowing (16 channels per OLR, 8 OLR per complex) the possibility to track all cubesats as long as they are in the same antenna beam.
MSPA-4* can use one channel for Two-Way Doppler | MSPA-4* can use four receivers for One-Way Doppler

## Slide 7: Open Loop Receivers
RF to IF Downconversion
Digitization
Open Loop Receiver 1
OLR Channel 1
OLR Channel 2
OLR Channel 3
OLR Channel 4
… up to 16
Open Loop Receiver 2
… up to 8
Signals from Cubesat ‘cloud’

## Slide 8: Artemis 1 Open Loop and INS Support
Use Open Loop Receivers (OLR) to simultaneously derive One-Way Doppler tracking data for 8 CubeSats launched with the Artemis EM-1 mission
  Insufficient amount of transmitters and tracking receivers at DSN to track all CubeSats at once; optimize total tracking time for all CubeSats
  No current capability for multiple uplinks per antenna
  The OLRs can track up to 16 channels each, allowing observation of 8 cubesats simultaneously at each DSN complex, even with multiple channels per spacecraft
Tracking a cubesat from two DSN complexes allows for the formation of high data quality Interferometric Navigation Solution data and only requires one-way tracking
  Also, Must have knowledge and pointing considerations to keep cubesats “cloud” within the beamwidth of the antenna
OLRs record full spectra that can be processed into One-Way Doppler tracking data
Proof of concept established with Mars 2020 launch

## Slide 9: INS View Periods
*INS #1
INS #2
INS #3
INS #4
Antenna rise/set at 6 degrees (but used actual azimuth horizon mask)
Actual coverage reduced somewhat by actual DSN tracking times
Part of the coverage “best efforts” during station pre-cal and tear-down periods
Even a short period is helpful to the Nav solution

## Slide 10: Overview of DSN Data Flow
Service Preparation Subsystem
CubeSats
DSN Complex B
DSN Complex A
OSCAR-X
1-Way Doppler
1-Way Doppler
Track-2-34
Files
Track-2-34
Files
Pointing, Schedule, Frequency Predicts
Pointing, Schedule, Frequency Predicts
Green Text
= INS-OLR Specific
= Campaign Nav Specific
= Standard DSN Ops
= CubeSat Specific
Key
Launch Provider Trajectory
SPK
JPL
Radio Science
Campaign Nav
CubeSat Projects - Nav
JSC Nav
TDM Files
Orbital Parameter Message
“Cloud” SPK
OLR Data
OLR Data
OLR Settings
OLR Settings
SPK (for initial pos/vel), “Cloud” SPK
Desired TDM & Track-2-34 Files
Schedule, Frequency Predicts

## Slide 11
SNR & Residuals
OLR Data
Check end time
Wait
Filtered SNR & Residuals
Sky Frequencies
TDM
Web Dashboard
JPL Campaign Navigation Team
OLR Data Processing
OSCARX

## Slide 12: Typical Observables

## Slide 13: Simultaneous Detection of 3 of 8 Cubesates
EQUL
BIOS
CUSP
ARGO
HMAP
MLIC
NEAS
OMOT

## Slide 14: Frequency Offsets
The oscillator frequency on board several of the spacecraft was off by 10+ kHz from prediction. Wider bands on the OLR were needed to allow detection of the signal, followed by a frequency offset (FRO) by the operator to center the signal in the recording bandwidth being processed
  ARGO 23 KHz
  BIOS -104 KHz
  CUSP 13.25 KHz
  EQUL -3 KHz (optimized to capture 1-Way at -6.3 Khz and 2-Way)
  HMAP 93 KHz
  MLIC 144 KHz
  NEAS N/A
  OMOT 0 KHz
This uncertainty coupled with the frequency separation and strong side-tones while close to Earth allowed for the mistaking of a BIOS sideband for NEAS, which was never actually detected

## Slide 15: Mission-by-Mission Summary: Part 1
ArgoMoon (ARGO) - Good source of INS data throughout the support, with periods of coherent data falling outside the main recording band, periods of 1-way data, and periods with no signal.
BioSentinel (BIOS) - Good source of INS data early on, with several short sessions of 1-way data. By the last two tracks, the signal is usually coherent.
Graphics: NASA/Arizona State University
Graphics: NASA/Arizona State University

## Slide 16: Mission-by-Mission Summary: Part 2
CubeSat for Solar Particles (CUSP) - Initial detection over DSS-25 only for 1 hour 16 minutes, with no subsequent detections. Residual frequencies, SNR, and sky frequency were sent to the NOPE and the CuSP spacecraft team, as well as a 1-MHz movie. Telemetry frames from 1-MHz backup recording confirmed that the signal was, in fact, CuSP. Further post-processing analyses found other signal detections in the data—these were found to be RFI from BIOS.
EQUULEUS (EQUL) - Nominal tracking throughout. 1-Way Frequency Offset -3000 applied to -6300 residual, thus allowing both to be recorded in the primary band.
Graphics: NASA/Arizona State University
Graphics: NASA/Arizona State University

## Slide 17: Mission-by-Mission Summary: Part 3
LunaH-Map (HMAP)- Nominal tracking throughout, with periods of coherent data, 1-way data, and no signal. The RS dashboard was used to quickly confirm a drop in signal strength every 9 minutes, consistent with the expected rotation rate
Lunar IceCube (MLIC) – Acquisition over DSS-25 at DSS-25’s official BOT (320/12:50). No explanation for lack of detection at DSS-53. Loss of signal at 13:50:21. No further acquisitions. RS provided post-processed data and supported continued tracks for 3 weeks after the launch event.
Graphics: NASA/Arizona State University
Graphics: NASA/Arizona State University

## Slide 18: Mission-by-Mission Summary: Part 4
NEA Scout (NEAS) - No detection. Over the 4th and 5th tracks, Radio Science detected a tone initially thought to be NEAS. This initial detection was eventually determined to be a side-band of BIOS. JPL Radio Science supported a spacecraft emergency with WebEx through DOY 326 and continued to script and check OLR for NEAS through early 2023.
OMOTENASHI (OMOT) - Initial detection for 80 minutes then nothing further. RS provided data and plots to project to help assess spacecraft condition and what may have happened
Graphics: NASA/Arizona State University
Graphics: NASA/Arizona State University

## Slide 19: Conclusion
Although not all CubeSats were detected or continued to transmit, data capture with the OLR for use with the INS method proved valuable as a means for establishing the ephemerides for multiple CubeSats deployed at once
  Radio Science team delivered to JPL Campaign Nav the One-Way Doppler measurements every 30 minutes during overlap periods
  JPL Campaign Navigation produced new ephemerides for the cubesats
Staffed by 3 people at a time, automation did the bulk of the data flow/processing work, allowing for the movement of 16 elements (8 spacecraft x 2 stations) during each INS period
The suite of automation tools developed for this event will be valuable for supporting similar campaigns in the future
  Doppler observable processing into standard navigation formats
  Data flow from OLRs to web tools for quick visualization, data validation checks

## Slide 20
This work was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration (80NM0018D0004).
© 2023 California Institute of Technology. Government sponsorship acknowledged.