## Slide 1
Copyright 2023 California Institute of Technology.
U.S. Government sponsorship acknowledged.
Multiple Uplinks Per Antenna (MUPA): Potential Communication and Navigation Benefits for Smallsats
Douglas S. Abraham, Shakeh E. Brys, Matthew D. Chase, Shantanu Malhotra, Leila Meshkat, David D. Morabito, James A. O’Dea, Emily R. Pascua, Marc Sanchez-Net, Dong K. Shin, and Zaid Towfic
Jet Propulsion Laboratory, California Institute of Technology
Interplanetary Small Satellite Conference
Pasadena, CA
May 1, 2023
Deep Space Network

## Slide 2: Artemis-1 Cubesat Support Predicament Deep Space Network (DSN) Antenna Availability
Not enough antennas at each in-view DSN Complex.
Prime Antenna
“Hot” Backup Antenna
Antenna devoted to Artemis-1 cubesats.
Artemis and cubesats used significant ground resources leaving all other same-sky DSN customers with very limited resources.
Artemis-1
Cubesats
in-beam for ~12-36 hours after deployment from ICPS.

## Slide 3: 4-MSPA Applied to Artemis-1
Multiple Spacecraft Per Antenna (MSPA) Technique
Insufficient 2-way Doppler & ranging time for the Artemis-1 cubesats – hence, the adoption of INS-OLR.*
* INS-OLR = Interferometric Narrowband Spacecraft (INS) tracking, essentially differenced 1-way Doppler, with the 1-way downlink signals captured via Open Loop Recorders (OLRs).

## Slide 4: Vision for the Future
Multiple Uplinks Per Antenna (MUPA) Technique Used in Tandem With MSPA
Virtually simultaneous uplink while all of the participating spacecraft simultaneously downlink. Simultaneous 2-way Doppler and ranging, as well.
* FCLTU = Forward Communications Link Transmission Unit
*

## Slide 5: Smallsat Situations Amenable to MUPA-MSPA
Everything at Mars or Venus is typically within the half-power beam-width of a 34m antenna at S- and X-band. Ka-band has some orbital altitude dependence when the planets are closer to Earth.
Concentrations of lunar surface assets such as those planned for near the Moon’s south pole would be in-beam.
If designed to be in-beam, constellations of spacecraft or flotillas of unaffiliated spacecraft.
Future secondary payload deployments – Artemis and otherwise.

## Slide 6: MUPA Prototyping Progress (1/2) The FCLTU Multiplexer (FMUX)
Version 1.1 has been successfully tested at DTF-21 using a virtual machine on JPL’s Flight Operations network.
Working with the SunRISE and EscaPADE projects on ground and flight demonstrations.
Identifying necessary DSN system updates.
FIFO = First In First Out
SLE = Space Link Extension
FCLTU = Forward Communications Link Transmission Unit
MOC = Mission Operations Center
DSS = Deep Space Station
UPA = Uplink Processing Assembly

## Slide 7: MUPA Prototyping Progress (2/2) Spacecraft System Interface Implementation Pathfinding
Capability to switch between assigned uplink frequency and the MUPA session uplink frequency.
  NASA spectrum management, in conjunction with international bodies (e.g. SFCG, ITU), may need to designate acceptable MUPA session frequencies in advance.
Ability to differentiate transfer frames on the basis of spacecraft ID.
  Iris radio has this capability. Most spacecraft have this capability to prevent errant commanding.
Radio capable of supporting non-standard turnaround ratios to coherently turnaround shared uplink signal frequency on individually assigned downlink frequency.
  Capability now built into Iris radio. Need to expand beyond Iris.
Radio (or C&DH in conjunction with radio) capable of compensating for perceived Doppler dynamics in single frequency uplink.
  Multiple Iris radio prototypes successfully DTF-21 tested. Capability now built into Iris radio. Need to expand beyond Iris.
Sweep Generator + Type 3 PLL
FFT + Improved Carrier Tracking Loop
Relative Doppler Dynamics

## Slide 8: Conclusions & Recommended Next Steps
Deep space antennas will likely remain in high demand during future human lunar missions, making antenna beam-sharing a necessity – particularly during secondary payload deployments.
MUPA, operating in tandem with MSPA, has the potential to enable multiple, in-beam spacecraft to “simultaneously” uplink through a single antenna while they simultaneously downlink.
  Simultaneous 2-way Doppler and ranging, too.
MUPA efforts to date have culminated in: (1) a prototype, DTF-21-tested FCLTU multiplexer, (2) identification of necessary DSN system modifications, and (3) incorporation of onboard Doppler compensation and certain other necessary features into the Iris radio.
Recommended next steps include:
  Ground and flight demonstrations of the FCLTU multiplexer and onboard Doppler compensation techniques.
  Expanding needed flight-side MUPA capabilities beyond the Iris radio.
  Implementation of MUPA within the DSN.
  Working with appropriate agencies and international bodies to establish: (1) acceptable MUPA session frequencies and (2) MUPA CCSDS and spacecraft radio-related standards.