## Slide 1
Interplanetary Small Satellite Conference May 1, 2023
Stephen M. Lichten
JPL Interplanetary Network Directorate, Chief Engineer
Douglas S. Abraham
JPL Interplanetary Network Directorate, Customer Interface Management Office System Engineer
Henry Minervini
Metis/Peraton, DSN Senior Network Operations Analyst
Charles Miyamoto
JPL Mission Systems and Operations Division, DSN Mission Interface Manager
NASA Deep Space Network (DSN) Experiences with Artemis-I Cubesat Mission Support
Europa Clipper
Span ~ 22 meters
BioSentinel (6U)
Span ~ 0.3 meters
DSN Antenna
Span = 34 meters
© California Institute of Technology 2023. All Rights Reserved.

## Slide 2: Artemis-I CubeSats
Credit: autoevolution
Artemis-I, an uncrewed lunar mission, launched Nov 16, 2022 and returned Dec 11, 2022 -- the first major flight of NASA’s Artemis program, marking the Agency’s return to lunar exploration originally begun in the Apollo program decades earlier
Artemis-I carried 10 cubesats, each a few tens of centimeters in size
  8 were supported by the DSN
With the launch of Artemis-I, the number of spacecraft tracked and supported by the DSN immediately increased by ~ 20%

## Slide 3: Ten Artemis-I Cubesats [GREEN = Launch/Early Orbit Phase DSN SUPPORTED (8)]
OSA Orion Stage Adaptor
  NEA Scout
  Lunar IceCube
  CisLunar Explorers: did not launch on Artemis
  Team Miles DSN support was requested later
  Argo Moon
  Bio Sentinel
  CuSP
  LunaH-Map
  Lunar Flashlight: did not launch on Artemis
  EQUULES
  LunIR DSN support was requested later
  OMOTENASHI
Credit: NASA/Cory Huston

## Slide 4: Artemis I CubeSat Release Process
https://www.nasa.gov/exploration/systems/sls/launching-science-and-technology-on-nasa-s-artemis-i-mission.html
Five cubesat release “Bus Stops” are possible
Artemis-I deployed 5 cubesats at Bus Stop 1 and another 5 were stagger-released (over 3 hours) at Bus Stop 2
These deployments presented the DSN with one flagship mission (Artemis-I) plus 8 (later 10) smallsats, all requiring critical event DSN communications and navigation services
Dahir, A. et al. (2021): JoSS, Vol. 10, No. 2, pp. 1049–1060

## Slide 5: DSN Utilized Innovative Techniques for CubeSat Supports
Interferometric Narrowband Spacecraft (INS) tracking, Open Loop Recording (OLR), and Multiple Spacecraft Per Aperture (MSPA) were utilized for DSN CubeSat supports, making most efficient use of limited DSN apertures
  Notable events: out of band CubeSat signals (RFI); CUSP frames extracted from OLR showed anomalous software resets and power/temp readings with loss of signal; BIOS CubeSat initially tumbling was rescued by DSN commanding
With OLRs, one DSN antenna could receive signals from up to 8 spacecraft simultaneously (versus 4 using regular DSN receivers and MSPA*). A new DSN Multiple Uplink Multiple Spacecraft (MUMS) capability was utilized for uplinks to multiple spacecraft in discrete segments.
DSN OLR data were the ONLY signals ever received from some of the cubesats
* MSPA = Multiple Spacecraft per Aperture

## Slide 6: Artemis-I CubeSats Status At A Glance
Mission name | Destination | Status | Lead Organization | Radio
LunaH-Map | Lunar South pole hydrogen mapper | Propulsion system (Busek ion thruster) unable to activate; missed LOI; losing link margin; using DSN arrays to close link | Arizona State University (ASU) | IRIS
Lunar IceCube | Lunar Neutron spectrometer to look for water ice at lunar south pole | Carrier briefly detected (~ 1 hr) with large frequency offset, then lost | Morehead State University (with Busek, GSFC) | IRIS
Cubesat for Solar Particles | Heliocentric Pathfinder for Space Weather Network, prove CubeSats as High Value Science platform | Carrier briefly detected, then lost Spacecraft health in question DSN used special SPK files + OLR to search. | Southwest Research Institute (SwRI) | IRIS
BioSentinel | Heliocentric | Early problems, tumbling; recovered via ground DSN commanding | NASA AMES | IRIS
Near Earth Asteroid Scout | Asteroid Carries 924 sf solar sail to reach an asteroid | 70m searching; no signals yet; EOM declared March 30, 2023 | NASA MSFC JPL Science PI: Julie Castillo-Rogez Mission PI: Les Johnson (MSFC) | IRIS
Argo Moon | Geocentric; heliocentric | Signals detected; imaged Earth and Moon; safing; received additional DSN passes; no signal since DOY 332 and spacecraft is out of propellant; EOM declared March 17, 2023 | ASI (Italian Space Agency) | IRIS
EQUULEUS [EQUilibriUm Lunar-Earth point 6U Spacecraft] | Earth-Moon L2 Lower energy maneuvers; imagers | Nominal DSN has transferred support to JAXA | JAXA | Adapted PROCYON transponder (ISAS)
OMOTENASHI [Outstanding Moon exploration Technologies by Nano Semi-Hard Impactor] | Lunar Lander | Tumbling; early signal, no signal now | JAXA | Adapted PROCYON transponder (ISAS)
LunIR | Lunar flyby Demonstrate IR sensor and cryocooler in cubesat | Solar panel(s) partially deployed, blocking antenna; flyby failed; DSN help requested | Lockheed-Martin (NASA) | Tyvak LDRR Radio
Team Miles (NASA Centennial Challenge winner) | Heliocentric orbit | In trouble, tumbling, off-trajectory; a few partial frames; DSN passes (OLR) did not detect signal | Miles Space | USRP B200mini S-band radio
Green – operating nominally
Yellow – operating with anomaly
Red - failed

## Slide 7: DSN: Artemis-I Cubesats Experiences
The DSN is optimized for high-reliability deep space mission operations planned weeks in advance
  DSN Follow the Sun Operations (FtSO) maximizes use of remote, automated operations
  A typical launch has one spacecraft covered by two DSN antennas. This time: nine spacecraft and eight DSN antennas.
  Normal DSN scheduling collaborative process has all missions engaged and working to address issues
    Artemis-I cubesats were launched together but due to DSN antenna loading and constraints, had to be acquired as an ensemble. They were not designed for this nor did cubesats coordinate for common concerns such as sequential DSN passes or deployment spacings.
  Frequent special requests from cubesats in distress disrupted what is ordinarily a smooth operational process. Future adaptation will be needed for the DSN to better accommodate such a “dynamic” environment.
Each of many Artemis launch shifts required labor intensive cubesat rescheduling
Impact of Artemis-I on DSN antenna demand over 26 days: +903 hours (~ 1.8 antennas)
Impact of cubesats on DSN demand over 26 days: +871 hours (~ 1.7 antennas)
Context: the DSN has a total of 14 antennas, with 4 at two DSN complexes and 6 at a third
DSN antenna time rescheduled from other missions over 26 days: 1585 hours.
DSN antenna time from deferring DSN maintenance previously scheduled over 26 days: 509 hours
  None of this DSN rescheduling was automated, so it was very labor intensive. This will change in the future.

## Slide 8: DSN and Artemis CubeSats: What We Now Know
DSN successfully deployed both new and traditional “search and rescue” methods on Artemis cubesats
  Ultra-sensitive DSN receivers, big apertures, INS, MSPA, open-loop searches (needles in a haystack)
Cubesat failures: tumbling; flight system; propulsion; mechanisms; no downlink
Workload on DSN ops teams very high. Process changes are being studied.
Artemis-I secondary payload cubesats lacked central coordination for cross-cutting issues. Due to DSN loading and resource constraints, they had to be acquired as an ensemble, but they were not designed for this.
Jim Free, NASA Associate Administrator for ESDMD, has stated that future Artemis flights will carry cubesats.
EARTH ORBITER CUBESAT RELIABILITY OVER TIME
Based on 855 Earth orbiter cubesat launches
Villela T., Costa C., Brandao A., Bueno F., Leonardi R. Towards the thousandth CubeSat: A statistical overview, Int J Aerosp Eng (2019)
While deep space Artemis CubeSats had only ~ 30% success, if we factor in MARCO, Lunar Flashlight, CAPSTONE, and Mars Helicopter, which have been successful, deep space CubeSats may have a promising future.
MARCO
Lunar Flashlight
CAPSTONE
Mars Helicopter Ingenuity