## Slide 1: Opportunistic Multiple Spacecraft Per Antenna (OMSPA) Deployment In the Deep Space Network (DSN)
Presenter: Jason Liao
Co-authors: Clayton Okino and Shan Malhotra
Jet Propulsion Laboratory
California Institute of Technology
Interplanetary Small Satellite Conference
May 1, 2023

## Slide 2: Introduction
Brief background on the OMSPA
OMSPA Design
OMSPA Testing
Performance of OMSPA
Observations & Lessons Learned
Future Enhancements
Notes: Iris

## Slide 3: Objective
OMSPA performs open-loop recording of other spacecraft in the antenna beam of a primary spacecraft track and uses a software receiver to demodulate and decode the recorded telemetry signals in near real-time. Postprocesses the recorded IF signal and sends back to projects using existing DSN delivery (SLE) within 24 hours.
Increase the DSN antenna utilization by adding software downlink channels for the larger set of missions.
Notes: Iris

## Slide 4: Future Mission Set
The DSN currently supports ~44 spacecrafts with 16 antennas.
In the next decade, the DSN may need to support almost 2-to-3 times today’s number.
Notes: Iris

## Slide 5: OMSPA History
2014: OMSPA Proof-of-Concept
2018: OMSPA prototype with MarCO CubeSAT
2018: OMSPA prototype with DSN-affiliate antenna
2019: OMSPA prototype with spacecraft at Mars
2021: OMSPA V1.0 end-to-end demonstration with spacecraft at Mars
2022: OMSPA V1.1 testing with 8 Artemis 1 CubeSATs

## Slide 6: OMSPA Functional Design

## Slide 7: OMSPA Hardware
OMSPA utilized DSN Common Platform for the analog RF to digital IF signal conversion.
OMSPA software receiver VMs are hosted on DSN Private Cloud Appliance.
Typical VM configuration is 16 CPUs and 320 GB memory.

## Slide 8: OMSPA Design
OMSPA operations is automated without human intervention.
OMSPA utilizes existing DSN infrastructure to minimized development cost.
OMSPA Telemetry is limited to 200 Kbps and 2 hours duration.
OMSPA support up to 16 simultaneous channel recordings.
Users submit service requests in OMSPA Portal.
Telemetry can be delivered within 24 hours.

## Slide 9: OMSPA Testing Approach
Test signal are generate using the DSN Test Signal Generator or recording of the spacecraft’s own radio.
Automated testing perform 55 candidate tests for all software receiver built at testing and production site.
6 end-to-end tests are performed for each built.
Daily automated testing performed for reliability verification.
Shadow tracks are performed with the MEX mission and verified with existing DSN processing.

## Slide 10: OMSPA Testing Result
8920 block size
Successful in testing maximum software receiver implementation loss < 0.5 dB.
Successful in testing maximum decoder implementation loss < 0.5 dB.
E.g. Performance plot for Turbo with 8920 block size
Bit Error Rate | OMSPA RS(255,223) (Eb/No [dB]) | CCSDS RS(255,223) (Eb/No [dB]) | Implementation Loss (Eb/No [dB])
1e-3 | 5.67 | 5.55 | 0.12
1e-4 | 6.02 | 5.9 | 0.12
1e-5 | 6.25 | 6.15 | 0.10
Tested performance for all turbo code block sizes (1784, 3568, 7136, 8920) and rates (1/2, 1/3, 1/4, 1/6) as well as all RS (223/255) interleaver sizes (1,2, 3, 4, 5, 8) .

## Slide 11: DSN Deployment Locations Around the World
GEO
30,000 Km
LEO
(600 Km)
Goldstone View
Canberra View
Madrid View
Earth
Canberra, Australia (CDSCC)
Goldstone, California (GDSCC)
Madrid, Spain (MDSCC)
JPL Control Center

## Slide 12: OMSPA Performance
16 successful simultaneous OMSPA channel recordings.
Typical post-processing latency is 1X-3X.
  2 hours recording typically take 2-6 hours to process.
Max Bitrate is limited to 200 Kbps based on the current requirement.
Up to 1 Mbps bitrate were tested with improving VM configuration.
Successfully daily processing for more than a year in the test environment.

## Slide 13: OMSPA Artemis 1 Processing
OMSPA recorded Artemis CubeSAT over the 36 hours primary mission.
Optimal recording bandwidth & frequency are generated based on the predicts.
Backup open loop recording of up to 1 Mhz are scheduled.
Most of the “optimal” recording failed during primary mission.
Predicted frequency, offset, and bitrate are far off. Sometimes even spacecraft ID (sent by the spacecraft) is wrong.
Artemis-1 Cubesats | Madrid | Canberra | Goldstone
Argomoon | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
Bio-Sentinel | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
CuSP | No obvious signal | No obvious signal | Obtained Transfer Frames
EQUULEUS | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
Lunar IceCube | No obvious signal | No obvious signal | Only identified carrier
Lunar Hmap | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
NEAScout | No obvious signal | No obvious signal | No obvious signal
OMOTENASHI | Signal detected but requires software upgrade | No obvious signal | Signal detected but requires software upgrade

## Slide 14: Observations & Lessons Learned
Need to provide a different service type when predicts are un-predicable as the Artemis 1 launch.
  Larger bandwidth or have multiple recordings for coverage
OMSPA service can serve as automated flight recorder, even when DSN receiver cannot decode.
In some instance, OMSPA re-processing of the Artemis 1 recording are the only recoverable telemetry for CUSP, otherwise would be lost.

## Slide 15: Timeline & Enhancement
CDR | TRR | Artemis 1 Testing | DDR | Deployment
Summer 2021 | Summer 2022 | Nov 2022 | Summer 2023 | Fall 2023
Possible Future Enhancement (not funded)
Doppler data extraction
Beacon detection
Software arraying
Cloud Computing & delivery
Automation and processing upgrade.

## Slide 16: OMSPA
Questions