## Slide 1: Opportunistic Multiple Spacecraft Per Antenna (OMSPA) Deployment In the Deep Space Network (DSN)
Presenter: Jason Liao
Co-authors: Clayton Okino and Shan Malhotra
Jet Propulsion Laboratory
California Institute of Technology
Interplanetary Small Satellite Conference
May 1, 2023

## Slide 2: Introduction
Brief background on the OMSPA
OMSPA Design
OMSPA Testing
Performance of OMSPA
Observations & Lessons Learned
Future Enhancements
Notes: Iris

## Slide 3: Objective
OMSPA performs open-loop recording of other spacecraft in the antenna beam of a primary spacecraft track and uses a software receiver to demodulate and decode the recorded telemetry signals in near real-time. It postprocesses the recorded IF signal and sends back to projects using existing DSN delivery (SLE) within 24 hours.
Increase the DSN antenna utilization by adding software downlink channels for the larger set of missions.
Notes: Iris

## Slide 4: Future Mission Set
The DSN currently supports ~44 spacecrafts with 16 antennas.
In the next decade, the DSN may need to support almost 2-to-3 times today’s number.
Notes: Iris

## Slide 5: OMSPA History
2014: OMSPA Proof-of-Concept
2018: OMSPA prototype with MarCO CubeSAT
2018: OMSPA prototype with DSN-affiliate antenna
2019: OMSPA prototype with spacecraft at Mars
2021: OMSPA V1.0 end-to-end demonstration with spacecraft at Mars
2022: OMSPA V1.1 testing with 8 Artemis 1 CubeSATs

## Slide 6: OMSPA Functional Design

## Slide 7: OMSPA Hardware
OMSPA utilizes digitized IF signal provided by the DSN Downlink Telemetry and Tracking Infrastructure.
OMSPA software receiver VMs are hosted on DSN Private Cloud Appliance.
Typical VM configuration is 16 CPUs and 320 GB memory.

## Slide 8: OMSPA Design
OMSPA operations are designed to be fully automated.
OMSPA utilizes existing DSN infrastructure.
OMSPA Telemetry is limited to 200 Kbps and 2 hours duration.
OMSPA support up to 16 simultaneous channel recordings.
Users submit requests in the OMSPA portal.
OMSPA scheduling software determines opportunities from a Cubesat ephemeris and the DSN schedule.
OMSPA software receiver postprocesses the recording and the portal reports the status.
Telemetry can be deliverer within 24 hours.

## Slide 9: OMSPA Portal
Portal Login
Request Opportunity & Reservation based on a spacecraft ephemeris and the DSN schedule
Successful processing & Status
Contact DSN Mission Interface Manager for SLE Delivery setup

## Slide 10: OMSPA Testing Approach
Tests are performed using either a spacecraft IF signal (live or recorded) or a DSN test signal generator.
Automated testing performs 55 candidate tests for all software receiver built at testing and production site.
6 end-to-end tests are performed for each built.
Daily automated testing are performed for reliability verification.
Shadow tracks are performed with the MEX mission and verified with existing DSN processing.

## Slide 11: OMSPA Testing Result
8920 block size
Successful in testing maximum software receiver implementation loss < 0.5 dB.
Successful in testing maximum decoder implementation loss < 0.5 dB.
E.g. Performance plot for Turbo with 8920 block size
Bit Error Rate | OMSPA RS(255,223) (Eb/No [dB]) | CCSDS RS(255,223) (Eb/No [dB]) | Implementation Loss (Eb/No [dB])
1e-3 | 5.67 | 5.55 | 0.12
1e-4 | 6.02 | 5.9 | 0.12
1e-5 | 6.25 | 6.15 | 0.10
Tested performance for all turbo code block sizes (1784, 3568, 7136, 8920) and rates (1/2, 1/3, 1/4, 1/6) as well as all RS (223/255) interleaver sizes (1,2, 3, 4, 5, 8) .

## Slide 12: DSN Deployment Locations Around the World
GEO
30,000 Km
LEO
(600 Km)
Goldstone View
Canberra View
Madrid View
Earth
Canberra, Australia (CDSCC)
Goldstone, California (GDSCC)
Madrid, Spain (MDSCC)
JPL Control Center

## Slide 13: OMSPA Performance
Typical processing is 1X-3X recording time.
  2 hours recording typically take 2-6 hours to process.
Max Bitrate is limited to 200 Kbps based on the current requirement.
Recordings of Up to 1 Mbps bitrate was tested with higher performance VM configuration.
16 successful simultaneous OMSPA channel recordings.
Successfully daily processing for more than a year in the test environment.

## Slide 14: OMSPA Artemis 1 Processing
OMSPA recorded Artemis CubeSAT over the 36 hours primary mission.
Optimal recording bandwidth & frequency were generated based on the predicts.
Larger bandwidth open loop recording scheduled for Radio Science were used afterward for postprocessing with the OMSPA software receiver.
Most of the “optimal” recording failed during primary mission.
Predicted frequency, offset, and bitrate were far off. Sometimes even spacecraft ID (sent by the spacecraft) was wrong.
Artemis-1 Cubesats | Madrid | Canberra | Goldstone
Argomoon | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
Bio-Sentinel | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
CuSP | No obvious signal | No obvious signal | Obtained Transfer Frames
EQUULEUS | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
Lunar IceCube | No obvious signal | No obvious signal | Only identified carrier
Lunar Hmap | Obtained Transfer Frames | Obtained Transfer Frames | Obtained Transfer Frames
NEAScout | No obvious signal | No obvious signal | No obvious signal
OMOTENASHI | Signal detected but requires software upgrade | No obvious signal | Signal detected but requires software upgrade

## Slide 15: Observations & Lessons Learned
Need to provide a different service type when predicts are un-predicable as the Artemis 1 launch.
  Larger bandwidth or have multiple recordings for coverage
OMSPA automated scheduling and postprocessing is a valuable troubleshooting tool.
In some instance, OMSPA re-processing of the Artemis 1 recording are the only recoverable telemetry for CUSP, otherwise would be lost.

## Slide 16: Timeline & Enhancement
CDR | TRR | Artemis 1 Testing | DDR | Deployment
Summer 2021 | Summer 2022 | Nov 2022 | Summer 2023 | Fall 2023
Possible Future Enhancement (not funded)
Doppler data extraction
Beacon detection
Software arraying
Cloud delivery
Automation and processing upgrade

## Slide 17: OMSPA
Questions
jliao@jpl.nasa.gov