## Slide 1
Deep Space Network Smallsat Data Management
Sirina Nabhan
Project Data Systems Engineer
May 1st 2023

## Slide 2: Introduction/Qualifications
Operations Network Engineer 2017-2020
Project Data Systems Engineer 2020-
  Telemetry, Tracking, and Command (TTC) Services
    Defining configurations
    Data delivery requirements
  Anomaly Investigation aka “Data Detective”
  Interfaces:
    TT&C Data System Operations Team (DSOT) - “Data Control”
        Operates SLE Telemetry Gateway and Tracking Data Processing
    TT&C Data System Integration Team (DSIT)
        TT&C Engineering Support
    TT&C Subsystem Cognizant Design Engineers (CDEs)
    Mission Interface Managers (MIMs)

## Slide 3
Agenda
Artemis I Payload Impact on DSN Data Management
Testing Campaigns
Tracking, Telemetry and Command Services
Looking Ahead: Future small sat users

## Slide 4
Artemis I Payload Impact on
DSN Data Management

## Slide 5
DSN, Backbone of Space Exploration
DSN tracks over 40 operational spacecrafts
  Even more due to phase C & D missions in testing and integration phase
  30+ NASA spacecrafts in development
2 new antennas
10x data rates of Apollo era missions
A standard initial acquisition uses 2 antennas, Artemis used practically all possible resources

## Slide 6: Supporting Multiple Initial Acquisitions
Artemis I used 8 antennas to support 9 critical activities at the same time!
Past multi-mission activities of similar scale:
  MMS
  Mars System
More to come:
  Artemis II payloads
  Sunrise Spacecrafts
  Escapade

## Slide 7
Artemis I Payloads
Argomoon (Italian Space Agency)
Biosentinnel (Ames Resarch Center)
CuSP (Goddard Space Flight Center)
Equuleus (JAXA)
LunaH-MAP (Arizona State University)
Lunar Ice Cube (Morehead State University)
Near Earth Asteroid Scout (Marshall Space Flight Center)
Omotenashi (JAXA)

## Slide 8
Testing Campaign

## Slide 9: DSN Integration Tests
Radio Frequency (RF) Compatibility Test: spacecraft receiver to facility test
Connectivity Test: Networking check—ping test or SLE bind that may require a telnet or similar
Dataflow Test: Antenna to MOC to JPL full end to end flow
Ground Data Systems Tests: testing each antenna front end to ensure all necessarily configurations are in place
Operational Readiness Tests: Rehearsals of critical activities such as launch, maneuvers, etc.
We ask ourselves if this can be reduced? The answer is no, not really.

## Slide 10: Testing Life Cycle Within TTC

## Slide 11
Tracking, Telemetry and Command (TTC) Services

## Slide 12
Services Provided

## Slide 13: Data Capture Delivery Routes
Spacecraft

## Slide 14: Reduction in Services
Software Lifecycle: large number of engineering builds and point delivers in parallel with normal deliveries
SLE Configurations:
  service instances (antenna each SLE bind)
  RAF only
  1 Mbps d/r or less
No search pattern for initial acquisition contingency
Coordinating SLE binds to correct provider and confirming TLM/TRK was delivered
  for 9 different MOCs

## Slide 15: TTC Software Lifecycle

## Slide 16: Challenges Faced
Mistake: assuming a small sat do not require as big of an effort as any other spacecraft. This may be true in other cases but not telecom and GDS
  Unique SCID means overall software update to be used by subsystems
  Training through testing —unavoidable but hard to keep the same teams
Varying spacecraft timelines
No central place for coordination —explaining the same needs 9 times
Artemis delays caused retesting
Artemis I priority concern, even more important for Artemis II

## Slide 17
Looking Ahead: Future Small Sat Mission Users

## Slide 18
Artemis leadership visits JPL to express gratitude

## Slide 19: DSN Wish List
Cubesats have similar timelines
  stricter testing campaigns
Training the same project ops people from compatibility to GDS
Monitor data as a service
DSN was accommodated any issue and this was costly on peoples times
Direct line to communicate wants/needs of the DSN to all cubesats
Getting DSN involved earlier so there’s a potential to enhance comms design
Software architect needs to be upgraded, no doubt
  but keep in mind efficiently sometimes makes things more complicated (operational cost) trade off

## Slide 20: Questions?