## Slide 1
A multi-mission solution for meeting the mission control needs of CubeSat missions
Leila Meshkat & Josh Choi
Interplanetary Small Satellite Conference
May 1, 2023
Copyright 2023 California Institute of Technology.
U.S. Government sponsorship acknowledged.

## Slide 2: Outline
Objective
Background
  Current NASA Multi-Mission Mission Operating System Capabilities
    AMMOS
    AMPCS
    AIT
MCS-Lite
AIT limitations and Sunrise experience
Current Status

## Slide 3: Objective
To create a lightweight and easily configurable suite of Mission Control System (MCS) tools that provides near earth and deep space Cubesats and Small Satellite missions with necessary capabilities for mission development and operations.
We call this tool suite MCS-lite
MCS-lite will support 1) the control/commanding, and monitoring of a Cubesat (pre & post launch) and ground station/support equipment including telemetry processing & display and 2) uplink command management & radiation control
MCS-lite will be used throughout the mission lifecycle, from early Flight Software development through Operational phases

## Slide 4: Current NASA Multi-Mission Capabilities
AMMOS Mission Data Processing and Control System (AMPCS)
Consists of tools and services that support 1) the control/commanding, and monitoring of a spacecraft (pre & post launch) and ground station/support equipment including telemetry processing & display and 2) uplink command management & radiation control
AMPCS is designed to be used during all phases of a mission lifecycle, from early Flight Software development, through testbed, ATLO, and Operational phases.
Advanced Multi-Mission Operating System (AMMOS)
A set of mission operations and data processing capabilities for robotic missions through an "Ops in a Box" approach.
AMMOS is a low-cost, highly reliable system utilized by more than 50 missions, including planetary exploration, deep space, earth science, heliophysics, and astrophysics, by NASA, ESA, industry, and academia.
Source: https://ammos.nasa.gov/
Source: AMMOS Mission Data Processing and Control System ( AMPCS) Software Requirement Document (SRD)

## Slide 5: AMMOS Context Diagram

## Slide 6: AMPCS Context Diagram

## Slide 7: Current Capabilities
AMMOS Instrument Toolkit (AIT)
AIT is a Python-based Ground Data System (GDS) and Mission Operation System (MOS) toolkit that provides Instruments with critical capabilities for mission development and operations in a light-weight and easily configured suite of tools.
  It was initially developed for Vehicle Cabin Atmosphere Monitor (VCAM) and Electronic Nose (ENose) ISS instruments circa 2008.
  It was originally called Bespoke Links to Instruments for Surface and Space (BLISS)
  It was then updated and expanded for OCO-3 (2019 launch) and ECOSTRESS (2018 launch). Baseline for ISS S.A.M instrument (a VCAM follow-on), Cold Atom Lab (CAL), M2020 MOXIE EGSE, MAIA IOS, Lunar IceCube, and LunaH Map
  It has been extended to support CCSDS SLE and CFDP specifications for Small Satellites in 2017/18
  The newest version of AIT is now called BIFROST
  Cubesat missions, such as Sunrise, have used BIFROST as a starting point for developing their MCS

## Slide 8: Why MCS-Lite?
Cubesats need a low-cost, fully functional mission control system, which is adaptable to their needs
AMPCS is a large-scale software product, and adaptations to it are expensive
AIT/ BIFROST has limited functionality
Key functionalities required by SunRISE:
The Sun Radio Interferometer Space Experiment, or SunRISE, is an array of six toaster-size CubeSats that will work together to study solar activity.

## Slide 9: AIT/BIFROST Limitations & SunRISE Experience
1) Fixed frame and packet size - guaranteed only single packet inside each frame.
  AIT does not provide the user the ability to create customized packet handlers. SunRISE encountered situations where a packet could be split between multiple frames. Full customization over downlink and uplink chains is a requirement for most Cubesats, which AIT does not provide.
2) Rudimentary GUI
  AIT requires users to copy and paste commands in the UI. This was too risky for Sunrise - they integrated with OpenMCT (data visualizer) and did some custom tooling to enhance the GUI for the purpose of error-free uplink

## Slide 10: AIT/BIFROST Limitations & SunRISE Experience
3) Single Client Use
  AIT requires that each OpenMCT (data visualizer) client to connect directly to the server, which was going to overload the AIT server. SunRISE developed middleware that accepts the queries and makes a single connection to the AIT server. So now multiple users can view the telemetry simultaneously
4) CCDS Telecommand Frames
  AIT can read and process CCSDS space packets as it was meant for processing instrument data but has no concept of transfer frames. SunRISE has added the CCSDS layers to enable the processing of CCSDS telecommand frames

## Slide 11: Current Status
Developing Requirements, Operations Concept and Architecture for MCS-Lite
  Soliciting information from Cubesat missions
  Deriving key functionality from information on github
  Reviewing literature for commercial Cubesat MCS systems
  Assessing integration with F-prime
    (F´ (or F Prime) is a software framework for the rapid development and deployment of embedded systems and spaceflight applications.

## Slide 12: Acknowledgements
SunRISE project:
  Adrian Vasquez, Carson Schubert
AIT
  Michael Joyce
Multi- mission Ground Systems and Services:
  Scott Markham