## Slide 1
Improving Small Spacecraft Mission Operations in Deep Space through the use of Disruption Tolerant Networking and Spacecraft-Initiated Operations
E. Jay Wyatt, Marc Sanchez Net, Nathaniel Richard
Jet Propulsion Laboratory/California Institute of Technology, Pasadena, CA, USA
Benjamin Malphrus, Emily Walter, Nathan Fite
Morehead State University, Morehead, KY, USA
Interplanetary Small Satellite Conference
May 1, 2023
California Institute Of Technology
Pasadena, CA

## Slide 2: Abstract
Small spacecraft missions in deep space are inherently different in many ways than traditional larger-scale deep space missions. They can be lower priority when competing for scarce communication resources, have less redundancy, simpler fault protection systems, less funding for operations, less experienced operations teams, and unproven mission enabling technologies, to name a few. Moreover, the forward looking mission landscape for small spacecraft missions is unique. Small spacecraft, for example, can be used to create constellations, fleets, and contribute to large-scale Lunar exploration in the coming decade. For these and other reasons, deep space small spacecraft missions can be considered novel within the worldwide space community. What is not novel, however, is the strong tendency to operate these missions in much the same way as flagship missions or similar larger mission classes. It generally isn’t well known, however, that there are highly mature capabilities that can be used to create operations concepts better suited for small spacecraft. These capabilities can lower mission risk, increase science return, improve operational efficiency, or lower mission operations cost. Moreover, if adopted, space agencies worldwide over time can operate more effectively and improve our collective ability to explore the Solar System. Two of these capabilities will be described. The first is Space Networking. Just as the internet has become pervasive on Earth, the space-based analog to the terrestrial internet can allow missions (even single missions) to be operated more effectively, enable networked spacecraft mission concepts, enable coordinated observations between two or more spacecraft, and improve automation for space-based relays. Space networking enables interoperability among spacecraft, which means that each spacecraft launched can become a node of the solar system internet. Over time, this can create permanent communication infrastructure in space by adding communications redundancy, improved performance, and decreased mission lifecycle cost. The other capability to be discussed is Spacecraft-initiated Operations. With this approach, pre-planned communication periods can be largely eliminated for most mission phases and a more adaptive means of communicating adopted. The spacecraft determines when to communicate and signals the ground system and mission operations team to activate when telemetry downlink or command uplink is required. These capabilities are largely available today, flight validated, and especially suited to small spacecraft missions. This briefing will describe how these technologies work, specific capabilities and services that are currently available, mission use-cases, and overall benefits for deep space small spacecraft missions.

## Slide 3: Introduction
This talk focuses on two new capabilities for deep space communication
  Disruption Tolerant Networking
  Spacecraft-initiated Operations
Both have matured in the past year
Both are especially relevant to small spacecraft missions beyond Earth Orbit
Spacecraft-Initiated Operations
Tracking On Demand
Disruption Tolerant Networking
More efficient communications

## Slide 4: NASA’s Deep Space Network
Slide Credit: Stephen Lichten (JPL)
DSS-17
Deep Space Operations Center
(DSOC) at JPL

## Slide 5: MSU 21m DSN-Compatible Ground Station
The first university-operated deep space antenna affiliated with NASA’s Deep Space Network (DSN)
After approximately 6 years in development the antenna is fully operational for supporting CubeSats in deep space
Also certified for supporting downlink for any DSN mission as needed
Status
  Provided initial acquisition support for Artemis CubeSats
  Currently supporting NASA’s Capstone Mission
  Others missions planned in the near-term
Offers DTN and Spacecraft-initiated Operations

## Slide 6: What is DTN?
The Disruption Tolerant Networking (DTN) Protocol Suite extends the terrestrial Internet capabilities into highly stressed data communication environments where conventional Internet protocols do not work.
  These environments may contain frequent disruptions, possibly long delays, and high error rates.
  In the Internet: Each received packet is forwarded immediately if possible, deleted if immediate forwarding is not possible.
  With DTN: Each received packet is forwarded immediately if possible, stored for future transmission if forwarding is not currently possible but is expected to be possible in the future.
DTN Protocols enable Disruption Tolerant Networking in deep space.
  Improves operational efficiency of most any mission
  Enables NASA to conduct science missions that otherwise would not be feasible.
Single Spacecraft and Relays
Networked Constellations
Example Mission Scenarios

## Slide 7: DTN Benefits for Small Spacecraft Missions
Benefit | Description
Improved Operations and Situational Awareness | The DTN store-and-forward mechanism along with automatic retransmission enables more reliable communications and significantly reduces ground-based spacecraft data management
Interoperability | The standardized DTN protocol suite enables interoperability of communication assets and can enable an interplanetary internet to be grown incrementally with each mission launch. DTN is part of the LunaNet Architecture which is an architectural framework and suggested set of recommended standards for interoperability in the Lunar vicinity
Reuse | Organizations can use of the same communication stack for each mission to reduce cost
Space Link Efficiency, Utilization and Robustness | DTN enables more reliable data transmissions and ability to have multiple data paths improves redundancy
Security | The DTN Bundle Security Protocol (BPSec) allows for integrity checks, authentication and encryption
Quality of Service | Priority levels can be set for different data types, ensuring that the most important data is received ahead of less important data

## Slide 8: DTN Development Status
Core protocols (BP, LTP) are complete and have been in use operationally within NASA (on International Space Station) since 2014.
NASA’s primary reference implementation is called ION (Interplanetary Overlay Network)
  In operational use in the Deep Space Network and onboard ISS for managing payload data
  Bundle Security Protocol (BPSec) has been integrated into the public release
Multiple implementations exist within NASA, including a BP module for Core Flight System software, a high-rate DTN implementation (HDTN), and DTNME with added ground system functionality.
Bundle Protocol (BP)
Licklider Transmission Protocol (LTP)
Bundle Security Protocol (BPSec)
Network Management
Key Management
Routing
Quality of Service (QoS)
DTN Deployment Services (Timing, Naming, etc.)
Mature/Standardized
Approaching Maturity
In Development
Research
DTN User Applications
Physical Layer
Key

## Slide 9: DTN Infusion Status
Lunar IceCube
Spacecraft End-to-end Testbed
(ongoing)
Morehead State Univ.
DSN-Compatible 21m Antenna
Pilot DTN Node (2018-Present)
DSN DTN Operational
Capability – Phase 1
(July 2022)
Korea Pathfinder
Lunar Orbiter (KPLO)
DTN Experiment
(Aug-Oct 2022)
NASA PACE Mission
DTN Operations
(November 2023)
International Space Station
Payload Data Management
Service (2014-Pressent)
LunaNet Architecture and International
Collaboration for Interoperability at the Moon (ongoing)

## Slide 10: Upcoming DTN Demonstration
Joint ESA-NASA-MSU DTN Interoperability Experiment will test 3 DTN software implementations in a flight-like configuration

## Slide 11: Spacecraft Initiated Operations Introduction
Background
Mission Communication periods (tracking passes) are negotiated months and weeks in advance because the Deep Space Network (DSN) is heavily utilized.
Mission operations beyond earth orbit cannot be real-time because of round-trip light time delays inherent in deep space communication
Mission tracking frequency varies by mission type and mission phase.
  Small spacecraft are generally low priority
Tracking passes are for telemetry downlink and command uplink
Spacecraft-initiated Operations reduces traditional tracking by using a simpler signal to indicate that a tracking pass is required
  This is called a beacon tone and is an operational DSN Service
  Used extensively during long cruise periods on the New Horizons mission.
  Can help Deep Space CubeSats lower mission risk in multiple mission phases, improve science return, and decrease cost
  Can enable constellations and coordinated observations
Spacecraft-Initiated Operations
Tracking On Demand
Beacon Tone
Modulated Sub-Carrier Signal

## Slide 12: Spacecraft Initiated Operations
Wouldn’t you like to know if your spacecraft is healthy everyday instead of waiting on the next scheduled tracking pass?
  If a problem has occurred requiring ground intervention it could be resolved sooner
Are there certain conditions since the last tracking pass that can influence what your ops team does on the next pass, making mission ops more efficient?
Motivations
What if you were just awarded a mission to send 50 spacecraft to 50 Near-earth asteroids? That would be the equivalent of 50 new missions all at once!
  How would you operate this mission at low cost and risk?
  How would the DSN support 50 new missions?

## Slide 13: Spacecraft Initiated Operations Process
Tone Definitions

## Slide 14: Spacecraft Initiated Operations Use-Cases
Use Cases Identified by the Lunar IceCube Project:
Beacon tone requests track when there has been a spacecraft computer reset
  Not an emergency but don’t want to wait until it is seen in the telemetry log.
Instrument lens cap status – if the lens cap is still Open after being set to Close (which was seen during LIC testing)
  Send an urgent tone if sun pointing is likely before the next pass
  Otherwise, send a non-urgent tone notifying the spacecraft team to issue the command again on the next scheduled pass
Trigger Coordinated Science Observations – Coordinated observation with LunaH Map (spectroscopy experiment). If LIC finds an elevated volume of hydrogen, use the beacon system to schedule as downlink asap so LunaH Map can be notified to do a follow-up observation.
Beacon tone notifies the ops team that the science data recorder is filling-up, which can happen at an unpredictable rate during instrument calibrations.
Notify ops team if instrument temperature has not cooled down in time to do the planned measurement,
  Use next pass to gather navigation data or replan the science activity.
  Could be important for mission success depending on how often this happens.
Beacon tone indicates when a momentum dump in the attitude control system is necessary
Beacon tone indicates that the thrust activity was shorter than planned – Could result in the spacecraft rapidly moving off-course making it urgent for the ground to intervene.

## Slide 15: Conclusions
Future missions can benefit from DTN and Spacecraft-initiated Operations
Deep Space CubeSats
Small Spacecraft Fleets
Small Spacecraft Constellations
Human/Robotic Exploration
Single Spacecraft