## Slide 1
Interplanetary Small Satellite Conference
The Hera Milani Mission
2nd May 2023
Margherita Cardi
VP Programs, Milani Program Manager

## Slide 3: Milani Consortium
Customer:
  European Space Agency
Industrial team
  Tyvak International: Prime contractor
    platform developer, spacecraft integrator, SVT with Hera, launch services, operations
  12+ sub-contractors
    from Italy, Czech Rep, Finland

## Slide 4: Italian representatives (consortium)
Strategic partnership / active program / cooperation
Academic partnership / cooperation
Supply chain
Institutional relations
POLITECNICO
DI TORINO
ALTEC
LATTES
CHIARLONE
ALLEGRETTI
OPTEC
POLITECNICO
DI MILANO
FAE TECHNOLOGY
T4i
CIRA
INAF
TECHNOMEC
ESSEGI
SOPHIA
Requirements, debris analysis, radiation activities
Development of VISTA Payload
  Support from Politecnico di Milano (polo di Lecco) and CNR
Mission analysis, GNC and Image Processing algorithms, Navigation Experiment
Ground Segment Interfaces definition
Propulsion system qualification and the vehicle PFM qualification at “Laboratorio di Qualifica Spaziale” (Tyvak heritage)
CNR
INFN
INFN

## Slide 5: Italian representatives (additional partners)
Strategic partnership / active program / cooperation
Academic partnership / cooperation
Supply chain
Institutional relations
POLITECNICO
DI TORINO
ALTEC
LATTES
CHIARLONE
ALLEGRETTI
OPTEC
POLITECNICO
DI MILANO
FAE TECHNOLOGY
T4i
CIRA
INAF
TECHNOMEC
ESSEGI
SOPHIA
Provision of retroreflectors, passive elements to be installed on Milani surface for ranging measurements with Hera
CNR
INFN
INFN
Joint development (Tyvak and T4I) of the Milani propulsion system (“Ianus”), leveraging on the Perseus development
Provision of NavCam lenses optimized for Milani mission

## Slide 6: Milani Scientific objectives
Milani (as well as the Juventas CubeSat) aims at enhancing the overall Hera scientific return
Main scientific objectives of Milani missions are:
  Map the global composition and characterize the surface of the Didymos asteroids
  Characterize dust clouds around the Didymos asteroids
  Evaluate DART impact effects on Didymos asteroids and support gravity field determination
Hyperspectral imaging
DUST detection

## Slide 7: Milani Operational constraints
From an operational point of view, Milani’s communication with ground will be performed via Inter-Satellite Link (ISL) using Hera as data relay. For this reason, data downlink and uplink must be performed within the same communication windows used by Hera. Operations will be scheduled considering:
  Hera mission operations requirements
  Milani CubeSat mission operations requirements
  Mission Data downlink (Milani-to-Hera)
  Communication window (Hera-to-Earth)
ISL

## Slide 8: Milani Mission Overview
Milani mission designed by Politecnico di Milano
Main phases related to the achievement of the scientific mission objectives and operational constraints
  Launch and Near-Earth Commissioning
  Cruise phase (ca 2,5years)
  Deployment and nominal mission (far range and close range)
Far Range Phase (FRP)
  Distance: 11 km from D2 surface.
Close Range Phase (CRP)
  Distance: less than 3 km from D2

## Slide 9: Milani Mission Objectives
Objectives: visual Inspection of the Dimorphos asteroid
  Payload “ASPECT”
  Hyperspectral Imager, developed by VTT (Finland) supported by University of Helsinki, University of BRNO, KUVA Space, Institute of Geology of the Czech Academy of Sciences
Scientific goals:
  ASP SG1 - Global composition of the Didymos asteroids mapping
  ASP SG2 - Surface of the Didymos asteroids characterization
  ASP SG3 - Space weathering and global shock effects on Didymos asteroids evaluation
  ASP SG4 - Local shock effects on Dimorphos caused by DART impact identification
ASPECT Payload Reduced EM
Parameter | Value
Total Mass | 1,5 kg
Power consumption during acquisition | 13-14W
Total amount data | 4.7 Gbit
Parameter | VIS channel | NIR1 channel | NIR2 channel | SWIR channel
Field of View [deg] | 10 x 10 | 6.7 x 5.4 | 6.7 x 5.4 | ca 5.85 circular
Spectral range [nm] | 500 - 900 | 850 - 1250 | 1200 - 1600 | 1650 - 2500
Image size [px] | 1024 x 1024 | 640 x 512 | 640 x 512 | Single-point
Pixel size | 5.5 x 5.5 um | 15 x 15 um | 15 x 15 um | 1 x 1 mm
No. spectral bands | Ca. 14 | Ca. 14 | Ca. 14 | Ca. 30
Spectral resolution [nm] | < 20 | < 40 | < 40 | < 40
Resolution @ 10 km | 1.7 m/px | 1.8 m/px | 1.8 m/px | 1022 m
Resolution @ 5 km | 0.85 m/px | 0.9 m/px | 0.9 m/px | 511 m
Notes:   Add scientific value to the Hera mission, supporting asteroid structure and composition assessment and numerical models refinement

## Slide 10: Milani Mission Objectives
Objectives: dust detection following the DART impact
  Payload “VISTA”
  Dust detector, developed by INAF (Italy) supported by Politecnico di Milano and CNR
Scientific goals:
  VIS SG1 – Dust particles smaller than 10μm detection
  VIS SG2 – Characterization of volatiles (e.g., water) and light organics
  VIS SG3 – Molecular contamination monitoring in support to Milani and ASPECT Spectrometer
VISTA EQM Payload
Technical characteristics | Value
Resonance frequency | 10 MHz
Mass | 90 g
Volume | 79 cm3
Power | < 0.85 W (passive mode) < 1.5 W (active mode)
Operational temperature range | from 243K to 308K
Total Data volume | 1.6 Mbit
Methods/technique used | 1. Dust and contaminants accumulation (passive mode) 2. TGA cycles (active mode) 3. Cooling cycles (active mode)
Notes: Detect any small dust natural ejection from Dimorphos due to micrometeorite impacts (as observed on Bennu asteroid)
Detect any dust exchange between Didymos and Dimorphos, providing information on the binary system stability / evolution

## Slide 11: Hera Milani interfaces validation
  Overall Hera Milani System configuration
  Milani integrated into the Hera main spacecraft for launch and cruise
  Multiple interfaces to be managed (common to the whole mission spacecraft)
Deep Space Deployer (DSD), provided by ISIS
Milani-to-Hera interface during launch and cruise phase
Life Support Interface Board (LSIB)
Deployer-to-Hera interface
Cubesat Interface Bracket (CIB), provided by ISIS
Milani-to-deployer interface
Milani vehicle Engineering Model

## Slide 12: Hera Milani interfaces validation
Two models developed to validate interfaces with Hera mothercraft
  Reduced EM (“rEM”)
  Structural and Thermal Interface Model (“STIM”)

## Slide 13: Hera Milani interfaces validation
Two models developed to validate interfaces with Hera mothercraft
  Reduced EM (“rEM”)
  Structural and Thermal Interface Model (“STIM”)
Reduced EM
  Reduced set of Satellite avionics for data and power interfaces validation
  Preliminary interfaces testing at Tyvak premises with Hera simulator
Status
  Main test campaign successfully executed in OHB with the Hera Avionic Test Bench
  Integrating ISL features
Milani rEM
Hera ATB – Milani rEM test campaign at OHB

## Slide 14: Hera Milani interfaces validation
Two models developed to validate interfaces with Hera mothercraft
  Reduced EM (“rEM”)
  Structural and Thermal Interface Model (“STIM”)
Structural and Thermal Interface Model (“STIM”)
  Reduced set of Satellite avionics and dummy masses for mechanical and thermal interfaces validation
  To be qualified and delivered to OHB for the execution of the Hera qualification test campaign
Status:
  Under testing

## Slide 15: Milani Engineering Model
Engineering Model
  Mechanical Fit check
  Internal interfaces validation
  EMI EMC Campaign completed
Status: completed

## Slide 16: Milani Engineering Model
Engineering Model
  Mechanical Fit check
  Internal interfaces validation
  EMI EMC Campaign completed
Status: completed
Milani EM integration into DSD
December 2022

## Slide 17: Milani ProtoFlight Model
ProtoFight Model
  Milani is a 6U CubeSat that leverages on Tyvak Trestles platform architecture, avionics technology Mark II
  Although the Trestles platform is a standard platform, some customizations were made specifically for Milani mission, including Software with the support of HULD
  System Validation Test (SVT) with Hera upon delivery
Status:
  Preparing AI&T Phase
Milani CubeSat configuration – Deployed configuration
Milani CubeSat configuration – Stowed configuration

## Slide 18: Milani satellite: focus
ASPECT Payload
  Developed by VTT, Finland
  Flight Model under final integration
VISTA Payload
  Developed by INAF, Italy
  Flight Model completed delivered to Tyvak
Propulsion System (”Ianus”, Cold gas)
  Joint development by Technology for Propulsion and Innovation (T4I, Padova) and Tyvak International
  Successful qualification in September 2023 at CIRA, Italy
  Flight Model delivered to Tyvak
Navigation Camera
  Navigation camera developed by Tyvak
  Algorithms developed by Politecnico di Milano
  IP and GNC design validated through a test activity executed at PoliMI to assess IP performances and noise characteristics
Main payload, Intersatellite Link system, Deployer and Cubesat Interface Bracket
  Defined by ESA
  Milani system designed according to ICD
Navigation Camera
Ianus Propulsion System – Flight Unit
INAF TEAM delivering VISTA PL
ASPECT PL - Mechanics

## Slide 19: Radiation test activities
Radiation harndness campaign
  Ensure the mission execution in a deep space environment
  Heavy ion test on components and high energy proton on modules
  Managed by Tyvak with support of Politecnico di Torino
High Energy Proton test campaign

## Slide 20: Ground Segment
Hera Mission Operations Center (HMOC), started in October 2022 and led by SpaceBel (Prime Contractor)
  Includes Mission Control Center for the two cubesats
  Basic interfaces for the Milani Mission Control Center (MMCC) defined as part of Milani program with the support of Altec, Italy
Milani Protoflight vehicle will support the Ground Segment validation in the frame of the System Validation Campaign with Hera mothercraft
MMCC

## Slide 21: Milani mission timeline: where are we?
PRR
PDR
CDR
TRR
QAR
NECR
Preliminary requirements review
Preliminary Design review
Critical Design review
Test Readiness Review
Qualification and Acceptance Review
Near Earth Commissioning Review
DART launch
DART IMPACT
HERA LAUNCH
HERA Mission
Nov 21
Sept 22
Oct 24
Dec 27
Mission
Milani deployment and mission
Milani delivery to ESA

## Slide 22: Dissemination
In the past months, Tyvak International was involved in a series of events, including the DART impact event at which the Milani model was exposed at the ESA stand
DART Impact Event PR
Uni Padova PR
ESA Media briefing

## Slide 23: Dissemination: DART Impact Event (26th Sept 2022)
DART Impact Event, APL

## Slide 24: Missing a mission logo and patch!!!
Mission name was decided by European Space Agency in conjunction with Italian Space Agency
“Milani”, in honour of Prof. Andrea Milani
Tyvak proposes to find a proper logo for the mission through an academic contest

## Slide 25: Flawless Execution Sustains Growth
Contacts: margherita@tyvak.eu