## Slide 1: Radar tomography of small asteroids with cubesat platform Alain Herique, Wlodek Kofman, Juventas Team and Droid Team.

## Slide 2: JuRa - Juventas Radar on Hera
Filip Záplata

## Slide 3: JUVENTAS
6U CubeSat
  HERA Lauch 2024
  Asteroid phase 2027
In orbit science
  JuRa sounding radar
  Inter Satellite Link (Radio science and TM)

## Slide 4: JUVENTAS
Sun-synchronous orbit terminator orbit
Two phases (~1 month each):
  Global Observations Phase: 3.3 km
  Proximity Observations Phase: 2.0 km
Didymoon Landing and surface ops
  low velocity
  Uncontrolled impact/bouncing
  1 day operation
  Gravimeter + start tracker

## Slide 5: JuRa radar
Monostatic radar
  @ 60 MHz
  Full polar
  Coded radar BPSK
Synthetic Aperture Radar
  Internal structure tomography
  Multipasses acquisition
  mapping Backscattering coefficient
 | JuRa
carrier | 60 MHz
signal | BPSK
BW | 20 MHz nominal 30 MHz extended
Resolution | 10 – 15 m (1D)
Polarization | Full linear
Tx power | 5 W
NEσ0 | Better than -50 dB.m2/m2

## Slide 6: JuRa HW
2 cross dipoles
4 deployable booms
1.26 m & 65 g each
Credits: Astronika sp. z.o.o
Credits: UGA
FM Acceptance and radar calibration in progress
Juventas S/C integration mid-June
Electronics 1U / 1kg

## Slide 7: JuRa to fathom Didymoon
Dimorphos & Didymos internal structures
to identify internal structure like layers, voids, sub-aggregate,
to characterize its constitutive blocks in terms of size distribution, heterogeneity at different scales (from sub metric to global)
  Binary system formation and stability conditions
  Impact crater characterization (with limited resolution)
Average permittivity and its spatial variation
to retrieve information on composition and porosity
  Full tomography if waves penetrates the whole moonlet

## Slide 8: DROID mission to of 99942 Apophis in 2029

## Slide 9
DROID: A mission concept to accompany and characterize Apophis
through its 2029 Earth closest approach by Carol A. Raymond et al.

## Slide 10: 2 CubeSat’s to probe interior of Apophis
Bistatic Mode – like CONSERT / Rosetta
  Spacecrafts in opposition
  Measurement in transmission (assuming SNR>0 after processing)
  Absolute measurement of the average permittivity
  Multipath propagation and scattering (block-size distribution)
  Whole tomography possible – deep interior
Monostatic Mode – like JuRa / Hera
  Each unit operating separately
  Measurement of the backscattering coefficient
  Whole penetration not expected (SNR!)
  First 100 – 200 meters of the subsurface
Bistatic radar S/C versus Earth
  Reception on Earth (LOFAR?)
  Very prospective

## Slide 11: Radar to Apophis
Identifying and characterizing the Apophis internal structures: to identify internal structure like layers, voids, sub-aggregate, to bring out the aggregate structure, to characterize its constitutive blocks in terms of size distribution, heterogeneity at different scales (from sub metric to global) crucial inputs to model mechanical behavior and stability conditions
Measure average permittivity and its spatial variations to retrieve information on mean porosity and composition and its spatial variation.
A large measurement coverage will provide tomography capabilities to image interior with a 10 m resolution or better

## Slide 12: Radar to Apophis & DROID CubeSats
R.A. close to a reflight of JuRa: the Juventas Radar on Hera/ESA to probe Dimorphos (launch 2024).
Required evolution for Droid bistatic :
  the Bistatic mode requires a synchronization process between plateforms using Mothercraft .
  Inter Satellite Link (ISL) would provide the reference frequency and a common timing (TBC)
  Limited evolution by regards to JuRa (interface board and SW).
  Preserved monostatic capabilities
Droid Cubesat
  6 or 8 U CubeSats
  Inter Satellite Link (ISL) would provide the reference frequency and a common timing (TBC) + radio science measurement

## Slide 13: DROID CubeSat
Orbits and operations
  Altitude lower than one kilometer
  relative position close to opposition to limit the instrument blinding by the direct path
  Full polarization and the large antenna beam to limit attitude control constraints.
  During one measurement, alternation of radar measurement and ISL measurement for orbit reconstruction and timing accuracy.
  Alternation of monostatic and bistatic sequences.
Orbits of the 2 CubeSats in the body fixed frame

## Slide 14: Radar tomography of small asteroids with CubeSat platform
Low frequency radar to fathom asteroid
  Unique opportunity to directly observe asteroid interior
  Characterization of aggregate structure
    Re-accretion processes, stability condition and binary formations
    Science and planetary defence
On small platform
  Low altitude radar measurement
    SNR and geometries
  SC motion contributing to the geometry diversity
    Apophis (30h)
  Bistatic mode 2 platforms
    Possible alternation of monostatic and bistatic sequences.

## Slide 15
JuRa Instrument Team
Alain Herique (IPAG/UGA), Dirk Plettemeier (TUD), Amine Kechouindi (Emtronix), Cedric Lorant (Emtronix), Christian Schmidt (Emtronix), David Moirin (Hensoldt), Dominik Nolbert (Astronika), Evgeny Zakutin (TUD), Filip Záplata (FZa), Henri Du Faux (Emtronix), Hugo Naydenov (IPAG/UGA), Kevin Stoffels (Emtronix), Lucas Cicero (Emtronix), Martin Laabs (TUD), Paul Torrente (IPAG/UGA), Ronny Hahnel (TUD), Stephane Papais (Hensoldt), Sylvain Rochat (IPAG/UGA), Thomas Pfohl (TUD), Yves Rogez (IPAG/UGA)
DROID Teams
C. A. Raymond, R. B. Amini, P. C. Adell, S. Bandyopadhyay, P. Bousquet, S. Bhaskaran, B. J. R. Davidsson, F. Esteve, L. Fesq, Y. Gregoire, M. Haynes, A. Herique, R. Karimi, J.T. Keane, N. Mastrodemos, P. Michel, D. Plettemeier, R. Pinède, Y. Rogez, N. Verdier
Acknowledgement
Hera is the ESA contribution to the AIDA collaboration. Juventas and JuRa are developed under ESA contract supported by national agencies.
DROID study is being carried out at the Jet Propulsion Laboratory, California Institute of Technology, under contract with NASA (80NM0018 D0004), and at CNES.
RA & JuRa preliminary studies has been supported by the CNES’s R&T program and the ESA's GST program.
JuRa is built by Emtronix (LU), UGA/IPAG (FR), TU Dresden (DE), Astronika (PL) and FZ (CZ). Juventas is built by
Gomspace (LU).
This project has received funding from the European Union’s Horizon 2020 research and innovation program under grant agreement No 870377 (project NEO-MAPP).

## Slide 16
99942 Apophis in 2029
Notes: 350 m , S type, 30 h