## Slide 1: Pelican: Radiation-tolerant Computational Storage
Interplanetary Small Satellite Conference
Caltech, April 2023

## Slide 2: SmallSats Need More Storage than Ever
Better Sensors
  More pixels
  More bands
New Sensing Methods
  Synthetic Aperture Radar
  Hyperspectral
Onboard Processing
  Larger software binaries
  Requires reference data
Just LANDSAT + Sentinel

## Slide 3: Legacy Storage is Large and Slow
Based on legacy technology
  Use of only rad-hard components limits capability
Low Performance
  1/10th capacity
  1/10th data rate
High Size Weight and Power
  100x volume
  50x weight
  10x power
Airbus NEMO-2 2041

## Slide 4: COTS Drives Can’t Handle Radiation
Designed to a cost
  No ECC on controller RAM (Error Correction Codes)
  Simple hardware
Poor Radiation Performance
  Life as short as months in LEO
  Requires redundant units
Great Performance, though
  High capacity
  Fast data rates
Samsung 960 Pro

## Slide 5: Pelican = Performance + Reliability
3D NAND Flash
  High capacity
  Small form factor
Modern Compute
  High throughput
  Performance tuning
Custom Controller
  Dual-string design
  Triple Modular Redundant hardware
Reliable Hardware
  Latch-up detection
  Improved telemetry

## Slide 6: Modern Technology for Modern Spaceflight
Xilinx Versal AI Edge
  7 nm FinFET for rad-tolerance
  FPGA, CPU, MCU, and more
3D NAND Flash
  Vpp rail bypasses charge pumps
  Increases radiation resistance
Rad-tolerant Power Supplies
  Mitigate latch-ups
  Provides fault isolation

## Slide 7: A Look Inside the Hardware

## Slide 8: A New Data Flow Model

## Slide 9: LDPC Codes Provide Flexibility
Supports hard and soft decision decoding
  Extract data from multiple voltage measures
  10x improvement in error correction
Easily switch code rates
  Follow NAND as it ages
  Adapt to user needs
Low-Density Parity-Check Codes

## Slide 10: Custom Solution = Custom Performance
Firmware Updates
  Performance Tuning
    Optimize for streaming
    … or random operations
  Capacity Scaling
    High redundancy for filesystems
    High capacity for bulk storage
  Encryption
  Special Features
Electrical Updates
  Custom data interfaces
  eg, NVMe over 40G Ethernet, SpaceWire, SRIO, LVDS
Mechanical Updates
  Move mounting holes
  Change connectors

## Slide 11: Special Features: Cache Prewarming
Maximize limited downlink windows
How it works:
  Controller pulls from NAND flash (slow)
  into RAM (fast)
NAND -> RAM
RAM -> Radio
time
data
rate

## Slide 12: Special Features: In-Drive Compute
FPGA Fabric
  Majority used for Controller HW
  Partial reconfiguration for user
CPU: Dual-core ARM Cortex-A72
AI Engines
  2D array of Vector Processor + RAM
  Optimized for AI/ML workloads
  4-5x more power efficient than GPUs
Network on Chip (NoC)
  Enables optimized data flow for heterogeneous compute environment

## Slide 13: Performance Specs
Initial target numbers
Likely better in design
Does not account for performance tuning
Metric | Requirement
Capacity | 2 TB
Sustained Read | 2,000 MB/s
Sustained Write | 1,000 MB/s
IO Ops per Second | 10,000 – 30,000
Endurance | 1,200 TBW
Electrical Interface | Data: NVMe over PCIe Gen4 x4 lanes Power: 12 VDC
Volume | 96 x 91 x 15 mm (without enclosure)
Mass | 100 g (without enclosure)
Power | <1 W idle 10 W active, normal reads and writes 30 W absolute maximum, with AI Engines

## Slide 14: Form Factor
First Version: PC104 outline
  96 x 91 mm board area
  Standard mounting holes
  Also considering 3U VPX
Connector
  Nano-d, for external interfaces
  SEAM8, for integrated solutions
  Also considering optical fiber
PC104 outline 96 x 91 mm
Actual Size!

## Slide 15: A Bit About Us
Jason Cerundolo
Alex Swehla
Alex Hiam
CEO
CTO
Head of Software
Managed deployment and design for rad-tolerant compute systems.
Designed software systems for high volume data computation, storage, and transmission.
Developed novel firmware solutions to impossible challenges by bridging open source libraries.

## Slide 16: We’re Backed with NASA Funding, and Mentored by the Canadian Government
Winners of the 2021 NASA Entrepreneurs Challenge for $90,000,
Completed Phase I SBIR - $125,000 Selected for Phase II SBIR - $900,000
Graduate of a 6 month Space Track accelerator program funded by the Canadian Government.

## Slide 17: Our Ambitious Timeline
Controller Development Q1 2023
Q2 2023 NASA SBIR Phase II Starts
Hardware Prototypes Q3 2023
Q4 2023 Qualification Tests
Demo Flight Q1 2024
Q2 2024 Firmware Development Continues

## Slide 18: Questions?
Jason Cerundolo jason@zephyrcomputing.space +1 510.368.1737