## Slide 1
J. Bartunek, C. Jauregui, R. Loehr, M. Marcucci-Rodriguez
PI: Dr. Greg Ogden
Department of Chemical & Environmental Engineering
University of Arizona
Space Debris Remediation: Particle Cloud Momentum Interceptor Method
Notes: Hello, my name is CJ Jauregui and I am a 2nd year master’s student finishing up my degree in chemical engineering
My project is “Title” and my PI is Dr. Greg Ogden

## Slide 2: 2009 Collision of Iridium 33 and Cosmos 2251
(Agi, 2020)
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: operational Iridium 33 satellite and the defunct Cosmos 2251 satellite
considered the most severe accidental fragmentation on record, with more than 1800 debris around 10 cm and larger being produced
– Many more debris smaller than 10 cm have also been detected.
half of the debris was predicted to re-enter 5 years after the collision, some debris will remain in orbit through the end of the century
KS syndrome
Could be accelerated by Antisatellite tests, which occurred in 2021, Russian ASAT missile test resulted in debris which forced the ISS to conduct collision avoidance measures and crew to shelter in place

## Slide 3: Agenda
Background
Solution Concept
Trajectory Modeling and Analysis
Debris-Cloud Interaction
Challenges
Next Steps
Notes: What is orbital debris?
Current Solutions

## Slide 4: Orbital Debris: A Growing Problem
Exponentially increasing
Could lead to Kessler syndrome
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(NASA, 2020)
(“Orbital Debris Quarterly News 24-1”, 2020)
Notes: That collision is a key example of the growing problem of orbital debris
As overall space object mass grows each year, the density of such can become high enough that collisions between objects generate more objects cascading into further collisions and generating an eventual cloud of debris surrounding the Earth
Objects left in orbit after serving their function
Existing problem since 1957
  Sputnik I
Different types and categories

## Slide 5: What debris should we target?
Intact derelict objects (IDO) ~2500
  >10 kg
Catalogued fragments (CF) ~8100
  0.5-10 kg
Lethal nontrackable (LNT) debris ~600,000
  1-500 g
IDO
CF
LNT
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
PAM-D
(Alliant Techsystems Inc., 2008)
Notes: Ido
  Spent rocket stages
  Defunct satellites
CF
  Large pieces of IDO
  Undetermined mass, shape, and density
LNT
  < 10 cm fragments of IDO
  Cannot be detected or regularly tracked
Collisions of IDO or operational objects generate CF and LNT
Remediation for LNT and CF are relatively complex and expensive
Typically involving sweepers or lasers
Will not be considered due to complexity and cost
But if tracking technologies are improved, the proposed method could also remove the debris
Removing IDO mitigates LNT and CF production
IDO preferable target
"In Cluster 850 (C850), conjunctions within 5 km occur on average of about once a day, with the closest miss over the last four years being 87 m with a relative velocity of typically 12 km/s. If a collision were to occur between two objects in this cluster, the catalog population could double in an instant with the liberation of roughly 16,000 trackable fragments and 200,000 or more of non-trackable particles potentially lethal in case of collisions (LNT).“
Spent Payload Assist Module – Delta (PAM-D)
  Rocket body, a stage of a launch vehicle
  STAR-48
    Solid rocket motor (SRM)
    Mass around 110 kg after burnout
    1.2 m in diameter
    2 m in length
    Titanium casing and phenolic nozzle

## Slide 6: Solutions for Orbital Debris
Mitigation
  Eliminating new debris
  Examples
    Satellite design
    Orbit Selection
    Post-mission disposal
    Collision avoidance
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(A. Ledkov & V. Aslanov, 2022)
Notes: Sat design
  Making walls more robust so that they can withstand impacts
Orbit selection
  Selecting orbital regime with less debris so collisions are less likely
Post mission disposal
  A plan in place to deorbit the object after the mission concludes
Collision avoidance
  Maneuvering the object to avoid collisions
Several voluntary standards and guidelines have already been developed, that are reflected in the national legislation and documents of the space agencies

## Slide 7: Orbital Debris Solutions
Remediation
  Active debris removal (ADR)
  Necessary to avoid Kessler Syndrome
  Several methods
    Robotic Arms
    Tethers
    Ion Beams
    Particle Clouds
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(A. Ledkov & V. Aslanov, 2022)
Notes: Remediation is the solution
Although mitigation is vital to keep the number of objects as low as possible, a study conducted by NASA Orbital Debris Program Office (ODPO) demonstrated with a robust model that even if no future launches occurred collisions between existing satellites would increase debris population faster than atmospheric drag would remove objects [7].
Existing studies show that even to stabilize the situation with space debris, at least five large objects need to be removed from orbit every year
Making Kessler syndrome our reality
Can be accelerated by ASAT
There are several adr methods
Plans for satellite constellations mean LEO has to be as clean as possible
Robotic Arms
Tethers
Ion Beams
Cloud of particles aka propulsive tug
  Particle Momentum Cloud Interceptor (PCMI)
There are plenty of other methods but most are hindered by technical complexity at cost
Clouds of particles,
A chemical or ion thrust used to decelerate targeted debris so that its change in velocity results in the debris being deorbited
  typically generated by a propulsive method,
  are relatively cheap,
  low in complexity,
  and lower risks of accidental collisions

## Slide 8: Our ADR Phases
1
Debris is identified, tracked, and its trajectory is modeled
Notes: Typical Phases of ADR
Identifying target debris
Launching a spacecraft
Rendezvous with debris
Contact or contactless ADR
Re-entry or separation of debris
Debris deorbits

## Slide 9: Our ADR Phases
1
2
1st stage is launched into a ballistic trajectory to intercept Low Earth Orbit (LEO)
Notes: Typical Phases of ADR
Identifying target debris
Launching a spacecraft
Rendezvous with debris
Contact or contactless ADR
Re-entry or separation of debris
Debris deorbits

## Slide 10: R3 Rocket Assembly
First stage
  Solid Rocket Motor (SRM)
Support ring
First stage
  Liquid Oxygen (LOX) fuel tank
Second stage fuel tank
Second stage booster
Nose cone
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: The first stage will launch the payload into the desired altitude
  it is reusable, will fall into the gulf of Mexico and be retrieved
2nd stage is focused on more precise maneuvering so that ADR method is positioned correctly
  It will deorbit itself

## Slide 11: Our ADR Phases
2
3
2nd stage deployed positioning the PCMI
Notes: Typical Phases of ADR
Identifying target debris
Launching a spacecraft
Rendezvous with debris
Contact or contactless ADR
Re-entry or separation of debris
Debris deorbits

## Slide 12: Trajectory of Second Stage
Legend
First Stage
Second Stage/ Interceptor
Debris
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: Currently being refined by other members of my research group

## Slide 13: Trajectory Modeling and Analysis
Create rocket and debris trajectory models
  MATLAB numerical propagator models
  OpenRocket for predicting drag coefficient vs. Mach number
Model predictions validated against Black Brant sounding rocket flight data
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(S.R.P.O., 2015)
Notes: The team has been working on developing a flight trajectory modeling tool. This tool shall help the team predict the apogee and flight path the rocket will have on its way to intercept the targeted dedris.
This tool is being developed using the MATLAB numerical propagator models and is being calibrated using the flight heritage left behind by Black Brant sounding rocket.

## Slide 14: Trajectory Modeling and Analysis
Initial conditions
  Launch site: : Matagorda, TX (28.6° N, 95.9° W)
  Drag Coefficient =
  Mass of water: 500 lbs
  Launch Angles: 75° to 85°
Initial results show an error of 0.8%
As the launch elevation angle increases, the error increases.
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Black Brant Launch Angle and Altitude
Notes: The simulation utilizes flight data that needs to be optimized for launches done from the Matagorda Peninsula at Texas.
One challenge encountered by the team was the appropriate aerodynamical modeling of the rocket as its heading up, for this reason, utilizing OpenRocket allowed the team to develop a preliminar model design of the black brant rockets and obtain a drag coefficient plot which was then used to determine the drag coefficient of the rocket as a function of height.
The first simulations were based on the simulation of a 500 lbs of water as payload up to 1200lbs of water.
It was also cosidered to develop the code for the simulation of launches at different launch angles starting at 75 degrees up to 85 degrees.
Initial results showed an error of 0.8% on the first angles, but this error seemed to increase as the angles increased. Further analysis and modifications are being done.

## Slide 15: Trajectory, Vertical Velocity, and Horizontal Velocity MATLAB Simulation Plots
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: This image shows the preliminar results of the simulations done with the 500 lbs of water as payload at different launch angles. The team is focusing on the Trajectory Plot which can help us determine and calibrate the code by comparing it with the black brant experimental graph.

## Slide 16: OpenRocket to model Black Brant V Sounding
Black Brant volume and mass data used to estimate full rocket motor size and shape
Model 4-fin version
  CG and CP values don't match
    Initial Condition Errors
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(S.R.P.O., 2015)

## Slide 17: OpenRocket Simulation Drag Coefficient vs Altitude Graph
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023

## Slide 18: Our ADR Phases
3
4
5
Deploy PCMI that interacts with debris
Altering Debris’ trajectory for rapid deorbit
Notes: Typical Phases of ADR
Identifying target debris
Launching a spacecraft
Rendezvous with debris
Contact or contactless ADR
Re-entry or separation of debris
Debris deorbits
4 is the main part of my project
5 is safety and trajectory

## Slide 19: Debris-Cloud Interaction
Determine the mass of water required
  Momentum calculations
  Drag calculations
  Feasibility assessment
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: This section is the focus of my research
Here is an outline of what I’ll be discussing in this next section

## Slide 20: System Parameters
Braking velocity required to deorbit targeted debris
Heat of collision should not dissociate PCMI
PCMI should not damage the debris
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(A.Jarry et al., 2019)
Notes: Change in velocity required to deorbit the debris
Depicted on the right, a cloud of particles being generated by a SRM seeded with solid particles
This method is being researched but has potential to damage the debris it interacts with
We looked to other materials that could fit these parameter and settled on water
Use a one-gram basis and conservation of momentum to calculate mass of PCMI required.
Compare inelastic to elastic collision cases.
Find the kinematic heat released to the PCMI.
Verify results are feasible for the system.

## Slide 21: Water in LEO
LEO Conditions
  Pressure: 10-6 – 10-4 Pa
  Temperature: -65 – +125 ºC
What happens to water released?
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(H. Fuchs & H. Legge., 1979)
(I. L. Kofsky et al., 1992)
Notes: Can exist in all phases in Low Earth Orbit (LEO)
Can absorb large amounts of energy
Can be released with low thrust
Cheap
Accessible
Phase diagram
All water will eventually turn to ice or vapor in a vacuum
But depending in the time of interaction the debris could interact with the liquid-ice droplet
Depending on the diameter of the nozzle the releases water could experience cavitation
  Where vapor forms bubbles with in the liq causing the stream burst
  As shown in the image here
Vapor, ice spherules, and liq ice droplets are formed

## Slide 22: Momentum Calculations
Elastic Collision
  Kinetic energy and momentum are conserved
  About 0.41% of object mass
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Inelastic Collision
  Momentum is conserved, kinetic energy is not
Notes: For a one-gram debris basis
An elastic collision is when two objects collide and “bounce” off one another
They can move in the same direction but are going at speeds that conserve momentum and kinetic energy
Using these definitions and the parameters given previously, the mass of water can be determined
Perfect elastic collision, when no energy is lost to the system, only really occur within atom
But important to calculate to give the lower limit of mass required
Kinetic energy can be released as sound, light, radiation, or heat depending on the nature of collision
  What we are most worried about is kinematic heat as dissociation is a possibility
  In space, no air no convection
  inelastic means in contact, so conduction can more easily occur
  Conservative calculation to assess safety
About double of elastic, 0.82% of object mass
The frozen PCMI would not melt, just be slight raised in temperature
  -65 C, 173.5 K
Both perfectly elastic or inelastic collisions are unlikely but provide a range of possible masses for imperfect collisions
More elastic collision the better (more momentum transferred) but for conservative assumptions, lean towards inelastic
Temperature change of PCMI would be 14 °C

## Slide 23: Momentum Results
Mass range of PCMI required for a PAM-D debris
  0.45 - 0.90 kg or 1.0 - 2.0 lbs
If the maximum amount of kinematic heat was applied to the PCMI
  PCMI would not disassociate
  Concept is therefore feasible
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: When I scaled up these results for the PAM-D, it was found that

## Slide 24: Drag Calculations
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Braking velocity equation
Drag coefficient is an unknown
  Typically found experimentally
(NASA, 2021)
Notes:   Conservative
  Consistent with nasa definition of drag
  Dependent on:
    Debris speed
    Debris shape
    PCMI state
  Consistent with nasa definition of drag
  S = reference surface area
  Cd = drag coefficient
  p = density of the cloud
  Vref = reference velocity
  U = length of cloud and debris interaction
  V = debris velocity
  dt = time debris spends in cloud
  dvb = velocity change given by cloud
  M = mass of the debris

## Slide 25: Drag Results
Drag results within the same magnitude as the momentum results
Gaseous water more advantageous than solid ice
  Gas phase: 0.72 kg
  Solid phase: 1.89 kg
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(H. Fuchs & H. Legge., 1979)
Notes:   Same magnitude
  On the right track
  Gas more advantageous

## Slide 26: Challenges
Ready access to articles and software
Diverse-Remote Team
  UA & UPRM
Programming learning curve
Finding Black Brant rocket specifications
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(NASA, 2021)
Notes: Key articles had their access blocked
Eventually gained access though library
I come from a chemical engineering background
At first felt overwhelmed by new info but found similarities
  Energy balances, fluid dynamics, thermodynamics
Self taught several functions and toolboxes within matlab
  Plenty of trial and error

## Slide 27: Next Steps
Model PCMI plume & Density Gradient
Optimize cloud configuration
Optimize trajectory models
Integrate orbit and debris scripts
Adapt code for R3 rocket program
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
(A.Jarry et al., 2019)
Notes:   From MODELING OF SPACE SHUTTLE ORBITER WASTE WATER DUMPS
  Once density over path is known can use drag equations to determine other cloud parameters
  Begin from minimum cloud requirements then adjust for 20-40ft of safety
  Adiabatic Compression of the PCMI,
  Dynamic pressure of the impact, will that compression lead to dissociation, does it limit cloud length?

## Slide 28: Acknowledgments
This project is funded by MUREP Institutional Research Opportunity (MIRO), Grant 80NSSC19M0197
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023
Notes: Nasa miro project

## Slide 29: Thank you!
Questions?
ISSC 2023 Beyond LEO, Pasadena, CA, May 2023