## Slide 1
Mars sailplanes subject to stochastic atmospheric conditions.
Wind
Adrien Bouskela
NASA MIRO Site Visit – University of Arizona – 2023-04-18

## Slide 2
Motivations
Airborne exportation vehicles push the limits of science objectives
Increased efficiency by utilizing atmospheric energy – Static and Dynamic soaring
  Risk associated with relance on weather and unsteady atmosphere
  Consider winds as probabilistic phenomena
G. Sachs1, J. Traugott, A. P. Nesterova, and F. Bonadonna

## Slide 3
Variable wind – Melas Chasms
  MRAMS Simulation data
  Strong updrafts along ridge
  Gradients in horizontal winds in plains with high standard deviation
  Slope lift is more reliable than dynamic soaring sources
  Sustained flight limit
  First half day:
  ↑ 3 – 10 m/s ↑
  evening:
  20 – 90 m/s/km

## Slide 4
Dynamic Soaring – Definition
Exploiting horizontal wind gradients to extract energy from atmosphere
Energy Gained
Climb upwind
Leeward turn at higher altitude
Dive downwind
Windward turn at lower altitude
Loitering Upwind
Riding Cross-Wind

## Slide 5
Dynamic Soaring – 3DoF Model
Newton’s second law & Kinematics :
Non dimensional Scaling

## Slide 6
Objective: Maximum Expectation relative energy at final time
Wind gradient as random variable
Integrated Chance Constraints on final states
complete one cycle
Dynamic Soaring – Stochastic Modeling

## Slide 7
Deterministic
SP
VA
Dynamic Soaring – Optimal flight path
Daily Average
Evening Average
8pm local

## Slide 8
Risk – Violating boundaries
Over flat plains highest risk boundary is altitude
Stochastic problem outperforms average value problem
Must introduce a Value at Risk constraint

## Slide 9
Risk – Violating boundaries

## Slide 10
Wind
Oscillating trajectories: Dive and climb can be assumed to travers identical wind environments
Opportunity for a recourse action:
Measure winds during climb
Select the recourse based on measurements
Two stage stochastic problem
Recourse at end of climb
Second stage random variable is probabilistic wind gradient with small measurement standard deviation
Stochastic programing – Two stage formulation
Measured wind
Random variable
stage number

## Slide 11
Trajectories closer to deterministic solution
Significantly lower risk
Better stochastic performance:
Two stage SP
Deterministic
Stochastic programing – Two stage formulation

## Slide 12
Two stage formulation – Robust Navigation Controller
Multi stage stochastic optimization → iterative robust navigation scheme
Similar to Model Predictive control used successfully in thermal soaring
Handles slow solution times by solving for multiple future steps
Two stage SP

## Slide 13
Ongoing flight experiments – Loitering
Flight experiments: Single stage inclined loiters

## Slide 14
Conclusions
Two stage SP
Under winds sailplane is pushed off course and risk is high
SP results in high risk with no recourse
Recourse presents significant advantages
Foundation for iterative navigation controller
Three stage solutions for risk adversity
Compare SP performance with experimental data

## Slide 15
References – Questions ?