## Slide 1
Rebekah Cutler, Athip Thirupathi Raj, Jekan Thangavelautham
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory
Aerospace and Mechanical Engineering Department
University of Arizona
Flatworm-Inspired Robot for Extraterrestrial Exploration
MIRO

## Slide 2: Outline
Introduction and Motivation
Proposed Solution
System Architecture
System Design
  Key Components
  Modular Construction
  Assembled Robot
  Circuit
  Rubber Wing Motion
Testing and Validation
Conclusions and Future Work
References

## Slide 3: Introduction and Motivation
Extreme environment exploration
Need for a versatile extra-terrestrial explorer robot that can traverse across a variety of terrains
  Ice
  Water
  Sand
  Flat ground
Sensors for collecting vital data
Extreme environment lander, courtesy of ESA.

## Slide 4: Proposed Solution: Biologically-Inspired Robotics to Explore Extreme Environments
Shell components created solely using 3D printing
Inspired by the marine flatworm and Velox robot
Velox Robot demonstration

## Slide 5: System Architecture
Slugbot
Structure
Electronics
Locomotion Mechanism
Modular Shell
Holders
Pinchers
Servos
Arduino
9V Battery
LiPo Batteries
Spine
Rubber Wings
Top Cover
End caps
Sensors

## Slide 6: System Design
Fins on either side
  Rubber, driven by servos
  Sinusoidal wave motion
  Various angles for different environments
    Vertical for solid ground/ice, horizontal for swimming, angled for sand
Robot spine
Pinchers
Servos
Servo holders
Rubber fins

## Slide 7: SolidWorks model of robot

## Slide 8: Exploded View for Manufacturing
Servo pincher
Servo holder
Robot spine
Servo
6. Shell
7. Fin
8. Arduino
9. Battery holder
10. Ultrasonic
sensor
11. Motion
sensor
14. AI vision
sensor
18. Front cap
20. Top cover
Notes: LEGEND

## Slide 9: Key Components
Rubber for fins
16 high-torque servo motors
Arduino, wires, servo driver
Motion sensor
Ultrasonic sensor
A.I. Vision Sensor

## Slide 10: Initial printed robot components
Shell and cap, assembled
Shell component
Pinchers
Holders
Modular Construction
Notes: LABELS

## Slide 11: Assembled Robot
VIDEO HERE

## Slide 12: Circuit
Arduino
Servo Driver 1
Servo Driver 2
8 servos
8 servos
9V Battery
Lithium-Polymer Battery
Lithium-Polymer Battery

## Slide 13: Rubber Wing Motion

## Slide 14: Testing and Validation
Locomotion
  Straight line
  Turning
  Turning radius
Incline tests
Terrain tests
  Sandbox under construction for terrain tests
  Concrete, sand, asphalt, ice, and water
Load tests

## Slide 15: Conclusions and Future Work
Begin testing the robot’s capabilities on various terrains
Design modifications for low-gravity conditions (TBD)
Miniaturization for ease of transportation

## Slide 16: Thank you — any questions?

## Slide 17: References
Designboom, Juliana Neira. “Velox, a Creepy Wiggly Robot That Can Move on Land and Water.” Designboom, 28 Dec. 2018, https://www.designboom.com/technology/velox-amphibious-robot-pliant-energy-12-30-2018/.
“Robotics.” Pliant Energy Systems, https://www.pliantenergy.com/robotics.
“Fuel the Future: Energy and Extracting Resources in Extreme Environments.” ESA, https://www.esa.int/About_Us/Business_with_ESA/Global_Space_Economic_Forum/Fuel_the_future_Energy_and_extracting_resources_in_extreme_environments.
Dezeen. “Amphibious Velox Robot Uses Undulating Fins to Swim and Crawl.” YouTube, 7 Feb. 2019, https://www.youtube.com/watch?v=CkZszsl2aIU&amp;ab_channel=Dezeen.

## Slide 18: Circuit Diagram