## Slide 1: Energy Harvesting from Spacecraft Charging: An Initial Study Using WarpX for PIC Simulations
Ashwyn Sam
May 2, 2023
ISSC

## Slide 2: Problem: Current Power Sources Not Great
Four main power sources:
Solar powered
  Low when very far away from Sun
Battery powered
  Internal power source can run out quickly and can also be heavy
Radioisotope Thermoelectric Generators (RTG)
  Dangerous to handle and low supply of plutonium
Nuclear powered
  Produces too much heat
Images credit: NASA

## Slide 3: Spacecraft Charging
Lai, Shu (2012)
Spacecraft charging is when the spacecraft has a net electric charge
Considered bad for spacecraft: 1. Damage to onboard electronic instruments 2. Interference with scientific measurements
Image 1: Lai, Shu T. "Fundamentals of spacecraft charging." Fundamentals of Spacecraft Charging. Princeton University Press, 2012
Image credit: NASA/JPL
Image 2: Evans, H. B. Garrett, S. Gabriel, and A. C. Whittlesey, “A preliminary spacecraft charging
map for the near earth environment,” in Spacecraft Charging Technology Conference

## Slide 4: Research Question: Can energy be harvested from spacecraft charging?
Spacecraft charging can result in large magnitude voltages relative to the ambient plasma
Small spacecraft and CubeSats in particular have power requirements on the order of Watts or less (Jaffe, L. D. and Herrell, L. M., 1997)
- Jupiter is a promising environment
Reference: L. D. Jaffe and L. M. Herrell, “Cassini/Huygens Science Instruments, Spacecraft, and
Mission,” Journal of Spacecraft and Rockets, vol. 34, no. 4, pp. 509–521, Jul 1997.
Young, S. , et al. (2019)
Plot: Young, S., Close, S., & Lee, N. (2019). The Space Environmental Electrical Power Subsystem (SEEPS): Energy Harvesting Supporting
Microsatellite Exploration of the Outer Solar System . International Astronautical Congress.

## Slide 5: Research Impact
Novel power source for spacecraft especially in Jupiter’s environment
Can help mitigate negative consequences of spacecraft charging
Better understanding of background space plasmas
Novel computational tools
Image credit: NASA

## Slide 6: Prior Research and Why Now
The idea of using spacecraft charging to power the spacecraft was first suggested by Grard in 1977
Derived a power law that predicted power per unit area available (ignored ion and secondary electron contributions)
Power requirements of modern small satellites fall under the maximum power available
Possible potential distribution around negative charged body. Grard, R. (1977)
Reference: Grard, Rejean JL. "The magnetospheric plasma as a source of energy for space instrumentation." Planetary and Space Science 25.7 (1977): 615-620.

## Slide 7: Spacecraft Charging Theory
Densities and temperatures being equal, the electron flux will be about 45 times larger than the flux of hydrogen ions, leading to a negative potential
The equilibrium spacecraft potential is one of the roots of :
Young, S. (2021)
Reference: Young, Sean Alden Quigg. Harnessing Energy in the Space Environment for Spacecraft Operations. Stanford University, 2021.

## Slide 8: Spacecraft Charging Theory Cont.

## Slide 9
Approximate Solution Using OML
Widely used in both Langmuir probe and dust charging theories in the large Debye length limit
Assuming that the size of the spacecraft is much smaller than the plasma Debye length, the OML regime is valid and yields analytic expressions for the current densities to the spacecraft surface using energy and angular momentum conservation.
Using OML, we can derive the following expression for total current to a surface:

## Slide 10: Some OML Results
Reference: Young, Sean Alden Quigg. Harnessing Energy in the Space Environment for Spacecraft Operations. Stanford University, 2021.

## Slide 11: Shortcomings
Grard’s theoretical analysis ignored ion and secondary electron contributions
Analytical approximations do not capture many nonlinear effects
Assumption of OML leads to: 1. Limited plasma regimes 2. Inability to analyze more complex geometries 3. Difficulty of analyzing effect of material properties
Inability to capture effects of magnetic field and spacecraft relative velocity
Experiments would be ideal
Notes: using OML theory provides upper bounds on the theoretical power available from spacecraft charging

## Slide 12: Spacecraft Charging Simulations
Particle-in-Cell (PIC)
Basic overview: The motions of charged macroparticles, each of which represents many real plasma particles, are advanced over small time steps, with concurrently updated Lorentz forcefields defined on computational grids
Numerically solving Vlasov equation
Minimum assumptions
Useful for plasma surface interactions
Reference: C. Birdsall, A. Langdon, Plasma Physics Via Computer Simulation (McGraw-Hill, New York, 1985)

## Slide 13: Using a customized version of WarpX
WarpX is an advanced electromagnetic PIC code
Extremely optimized and has great scalability features
Ability to input 3D geometry files
Lot of features including mesh refinement, relativistic effects, various output formats, etc.
We implemented a charging algorithm developed by Roussel (Roussel, J-F, 2001) in WarpX
Reference: Roussel, J-F. "Modelling of spacecraft plasma environment interactions." Spacecraft Charging Technology. Vol. 476. 2001

## Slide 14: Revisiting Young’s Equations to Benchmark
For a sphere, Young solved for the normalized floating potential as:
Where,
1
1
1
0
0
0

## Slide 15: Benchmarking with Young’s Equations Cont.
These plasma parameters are representative of conditions found close to the Sun:
𝞵 = M/m = 1836
= 85 eV
= 0.05
= = 7e9
Using these parameters, Young’s equation predicts a floating potential = -144.5 V
Image Credit: WorldAtlas

## Slide 16: Simulation Setup
10 m x 10 m x 10 m simulation box
Electrostatic
Immersed body is a sphere in the middle (diameter of sphere is smaller than Debye length to be in the OML regime)
Dirichlet boundary conditions on all 6 walls
Particles reflect at all 6 walls
Particles are uniformly distributed at the 0th time step
Particles velocity is Maxwellian
10 m
0 V

## Slide 17: Results
Charge Density
Potential

## Slide 18: Results Cont.

## Slide 19: Spacecraft Body Immersed in a Flowing Plasma (3D)
Charge Density
Potential

## Slide 20: Comparison with Published Results
Deca, J. ,et al. (2013)
Reference: Deca, J., et al. "Spacecraft charging analysis with the implicit particle-in-cell code iPic3D." Physics of Plasmas 20.10 (2013): 102902.

## Slide 21: Ongoing Work
Implement full capacitance matrix method to study current evolution through material and couple it with circuit analysis
Benchmark code against multiple test cases :
- Currently working on writing a benchmark paper

## Slide 22: Possible Implementations
Environments where traditional power sources are not well suited
Additionally, you can also direct the current through a wire at an angle into the background field to use for attitude control

## Slide 23: Future Work
Build a fully functional PIC code coupled with circuit analysis to calculate the power output from spacecraft charging
Use PIC to optimize this power output by analyzing geometry, material properties, magnetic field effects, streaming effects, etc.
Successfully propose design concepts to implement spacecraft charging as a novel power source in future spacecraft

## Slide 24: References
1. Chen, Francis F. Introduction to plasma physics and controlled fusion. Vol. 1. New York: Plenum press, 1984.
2. Lai, Shu T. "Fundamentals of spacecraft charging." Fundamentals of Spacecraft Charging. Princeton University Press, 2012
3. L. D. Jaffe and L. M. Herrell, “Cassini/Huygens Science Instruments, Spacecraft, and
Mission,” Journal of Spacecraft and Rockets, vol. 34, no. 4, pp. 509–521, Jul 1997. 4. Evans, H. B. Garrett, S. Gabriel, and A. C. Whittlesey, “A preliminary spacecraft charging
map for the near earth environment,” in Spacecraft Charging Technology Conference
5. Young, Sean Alden Quigg. Harnessing Energy in the Space Environment for Spacecraft Operations. Stanford University, 2021.
6. Grard, Rejean JL. "The magnetospheric plasma as a source of energy for space instrumentation." Planetary and Space Science 25.7 (1977): 615-620.
7. Young, S., Close, S., & Lee, N. (2019). The Space Environmental Electrical Power Subsystem (SEEPS): Energy Harvesting Supporting
Microsatellite Exploration of the Outer Solar System . International Astronautical Congress.
8. Young, Sean AQ, et al. "Theory of Power Generation From Spacecraft Charging." IEEE Transactions on Plasma Science (2021).
9. Allen, J. E., B. M. Annaratone, and U. De Angelis. "On the orbital motion limited theory for a small body at floating potential in a Maxwellian plasma." Journal of plasma physics 63.4 (2000): 299-309.
10. C. Birdsall, A. Langdon, Plasma Physics Via Computer Simulation (McGraw-Hill, New York, 1985)
11 Deca, J., et al. "Spacecraft charging analysis with the implicit particle-in-cell code iPic3D." Physics of Plasmas 20.10 (2013): 102902.

## Slide 25: 1D Surface Charging: Proof of Concept

## Slide 26: Comparison to Analytical Solution
V = IR ; R = L / (); I = 𝛤
Using: L = 0.1 m
dx = dy = (L / 50) m
dz = 0.003 m
σ = 1e-9 S/m
e = 1.6022e-19 C
𝛤 = 1e14 (m^2* s)^-1
V = 1068 V
V = 1067.3 V

## Slide 27: High Level Design Aspects
Can spacecraft charging be optimized for various plasma environments ?
Proper identification of ambient plasma characteristics
Use spacecraft charging as backup power source
Effects of magnetic field
Optimized geometry of deployable structures to better capture this energy
Effect of material coating on spacecraft
Time varying deployable structures
Effect of spacecraft velocity
Spacecraft charging as power source for spacecraft near the Sun
Mitigate the dangers of spacecraft charging from discharges

## Slide 28: Orbital-Motion-Limited (OML) Theory
Widely used in both Langmuir probe and dust charging theories in the large Debye length limit
OML approximation breaks down when spacecraft potentials approach zero and the structure of the sheath becomes important
Using OML, Young was able to derive the following expressions:
Young, S, et al (2022)

## Slide 29: Prior Research (Additional)
Young, S. , et al. (2019)
Maximum available power for a 5 cm radius spherical spacecraft
Young, S. , et al (2022)
Provides an upper bound on power generation
Studied magnetic field and streaming plasma effects
Young, S. , et al (2022)

## Slide 30: Additional slide (Derivation of optimal load)

## Slide 31: Additional Slide (Maximum Power available ignoring all positive current terms)
Take derivative and substitute
Take derivative and substitute
To find
Reference: Young, Sean AQ, et al. "Theory of Power Generation From Spacecraft Charging." IEEE Transactions on Plasma Science (2021).

## Slide 32: Results
Young, Sean, et al (2022)

## Slide 33: Customized WarpX
Most PIC simulations that involve calculating the potential of an immersed body in a plasma do it one of three ways: 1. Uniformly distribute the charge between all nodes in the body 2. Nonuniform permittivity in the field to denote perfect conductors 3. Capacitance Matrix Method (most accurate)
Roussel developed an easier version of method 3 that gets simplified for perfect conducting bodies (Roussel, J-F, 2001)

## Slide 34: Additional Slide (Roussel Algorithm)