## Slide 1
Vivek Verma, Massimo Biella, Jekan Thangavelautham
Space and Terrestrial Robotic Exploration (SpaceTREx) Laboratory
Aerospace and Mechanical Engineering Department
University of Arizona
A Swarm Approach for Interstellar Object Intercept Missions

## Slide 2: Outline
Introduction
Related Work
Objectives
Challenges
Simulations Approach
Results
Conclusion and Future work

## Slide 3: Introduction
The ISOs are thought to have come from outside of the solar system.
In last decade, the researcher have identified 2 ISO’s.
  Oumuamua
  Borisov.
Figure 1: The track of first-known interstellar object, Oumuamua, relative to the inner solar.
(Credit: Nasa JPL, 2019)
Notes: They may have launched away from their parent solar system in some violent accendent.

## Slide 4: Introduction
ISOs are potential carriers of material from the other solar systems
Samples from these objects can help us gain insight into planetary formation and galaxy evolution.
Transiting interstellar objects are more common than we thought [1]
Notes: Although we have deducted two ISO, but recent estimation my astronomers shows with improved surveillance and detection capabilities at least one ISO per year can be spotted.

## Slide 5: Related Work
Utilize big, heavy spacecraft to carry out all measurements
  Single-point failure
  Generic trajectory – not tailored toward any instrument
Long mission duration times – 3 or more years
Notes: Before getting started on the design we looked at the previously published work about ISOs both for guidance, and to compare different concept to the approach we wanted to propose. What we found was that most papers planned on utilizing big heavy spacecraft to carry out all the different aspects of the mission. Although at times beneficial, or even necessary, this approach presents the possibility of a single point failure, while also not being able top tailor its trajectory and operations toward any specific measurement or instrument, as they are all carried onboard a single bus. Furthermore, we found that for similar concepts, the mission duration time was often required to be 3 or more years.

## Slide 6: Objectives
Identify and characterize ISO’s
  Physical properties: shape and size.
  Chemical properties: material and composition.
Conduct surface mapping and characterize spin behavior
Figure 3: Artist’s representation of 1I/2017 U1 ‘Oumuamua
(Credit: Y. Zhang)
Notes: Faster than any thing in solar system.

## Slide 7: Challenges
The ISOs travel in hyperbolic orbit with very fast speed.
Unbounded trajectory limits the close observation of an ISO (one chance).
The odd nature of orbit orientation makes it hard to generalize a trajectory problem.
Notes: Faster than any thing in solar system.

## Slide 8: Approach – Using a Swarm
Utilizing a multi-spacecraft approach to carry out multiple simultaneous high-risk, high-rewards missions
N-sized swarms are considered to carry out a variety of missions
Notes: - The concept proposed hereby takes advantage of ESPA ring architectures to decrease the cost of the mission while providing multi-spacecraft capabilities. This allows us to explore a variety of high-risk, high-reward mission concepts such as intercepts and close flyby’s.
The underlying assumption that guided our approach to these initial phases of the project are that we would be employing n-sized spacecraft swarms of ESPA Class spacecraft.
Here is an example CAD representation of a sample spacecraft that could be used as an impactor next to a Northrop Grumman’s ESPAStar platform that could fit the purpose of carrying each swarm to their parking orbits.

## Slide 9: Approach
Spatial discretization to quantify the ecliptic plane in order to identify “hot spots”.
  Orbital Velocity of each grid cell center:
Notes: - To increase the chances of usefully intercepting an interstellar object, we first want to determine where in the solar system it would make the most sense to park our swarms while they await for detection. We will call these areas “hot spots”.
- To do this, we carried out a preliminary spatial discretization analysis in which we sliced the solar system in a 2D grid. The grid might look confusing at first, but each grid cell center represents the mean orbital radius of each planet in our solar system, starting from Mercury to Jupiter, at different times during their orbit.
- Any intercept mission considered here will have to perform a gravity assist maneuver by Jupiter, shown in the pictures by a red diamond, hence the grid is let rotate following the planet’s orbital motion as reference, and is centered at the Sun.
- What these center points allow us to do, is to fit different orbits through each one of them, effectively yielding a range of orbital velocities associated to each grid cell.
- The position and velocity of the revolving mass at some time t, is calculated using Lagrange coefficients F and G, where capital PHI is used to denoted the transition matrix that allows us to convert the states from their initial conditions to an arbitrary time t.

## Slide 10: Approach
Measure 4 Key “Performance” Metrics
    (Jupiter-ISO at 6AU)
  where:
Notes: The fitness of a range of parking orbits is calculated by measuring 4 key performance metrics, starting from the relative position and velocity of the ISO with respect to the grid points.
To get a better idea of the heading of the ISO relative to Jupiter while leaving our solar system, PHI is defined to be the angle between the position vector from Jupiter to the ISO when the ISO is at a distance of 6AU from the Sun. For this analysis, a value of pi/2 is chosen as a threshold, meaning an angle between –pi/2 and pi/2 is treated as a favorable condition. Outside this boundary, a gravity assist from Jupiter is not considered a feasible maneuver to boost the spacecraft’s velocity.

## Slide 11: Simulations and Results
Figure 9: Relative position ∆r ranking for 1I/2017 U1 ‘Oumuamua
Best locations are near or about Mercury’s orbit.
Notes: The trajectory of ‘Oumuamua is treated as the reference case used to validate the model. By measuring metrics from the previous slide, we are able to populate a heatmap that gives an insight into which parking orbits might be offer a bigger advantage based on the mission to be conducted. In fact, although we considered an intercept mission to be the primary goal of this mission, in our paper we explore the feasibility of other types of missions and relate them to the different scientific measurements that can be conducted.
Heatmap representing the relative position ranking of the different grid cells shown earlier. It can be noted that in the case of ‘Oumuamua, parking a spacecraft near or about Mercury’s orbit would offer the greatest benefits in terms of smallest relative position.

## Slide 12: Simulations and Results
Figure 10: Relative velocity ∆v ranking for 1I/2017 U1 ‘Oumuamua
Best locations are near Sun and Mercury.
Notes: This heatmap shows the relative velocity between the grid centers and the ISO in km/s. The smallest and largest velocities corresponds to the orbits of the same planets, as expected. Larger relative velocities might be more desirable depending on the kind of impact mission that is to be carried over, with the smaller ones being around the general lower-right part of the map.

## Slide 13: Simulations and Results
Figure 11: Lambert’s ∆r ranking for 1I/2017 U1 ‘Oumuamua
Smallest values of delta-v being close to Jupiter’s orbit though not too close.
Notes: Here, a heatmap that ranks the required Delta – V to carry out a direct impact trajectory from the parking orbit of the spacecraft is created by solving Lambert’s problem. This assumes a TOF of 1 year, with the spacecraft starting its intercept trajectory injection burn 6 months prior to the ISO’s crossing of the ecliptic plane, and impacting 6 months after that. Here we do not take into account any gravity-assist maneuvers by Jupiter.
A different picture is portrayed here, with the smallest values of Delta-V being close to Jupiter’s orbit. Obviously if we were to park our spacecraft around Jupiter, we would not be able to execute a gravity assist from it, so other parking orbits, such as around Venus or Mars might be more desirable in certain scenarios.

## Slide 14: Simulations and Results
Table 1: Minimum Values of KPP recorded from Different ISO Orbital Parameters
Different ISO trajectories are simulated.
Nominal orbital elements:
Notes: Finally, this table collects the minimum values for different ISO’s trajectories, simulated by varying one orbital element at a time while keeping the others constant to study if and how the grid “hot spots” vary.
Here we vary the semi-major axis, the argument of periapsis, and the eccentricity along with the true anomaly of the ISO’s trajectory. The other parameters are taken from ’Oumuamua’s trajectory.
A trend can then be noticed, as when we increase any of the orbital elements, the Delta-V also required increases, while the minimum relative distance between the ISO and the parking orbits decrease, and vice versa.

## Slide 15: Conclusions and Future Work
Discretization of space helps in optimizing parking orbits
Varying the ISO’s OEs has a profound effect on the “hot spots” generated in the domain
Forming a distributed network of the swarm to carry the mission autonomously
Development of GNC algorithm to guide a swarm of spacecraft towards ISO upon detection
Notes: - We concluded that discretizing the solar system could effectively help us better plan for a variety of missions based on the science measurements that are to be carried out and on the different instrumentation, GNC, and propulsion constraints.
Additionally, for the trajectories simulated, parking orbits around Earth’s neighboring planets seem to offer more advantages when compared to farther ones, both in terms of relative distance and delta-V required for a direct trajectory calculated from Lambert’s problem.
Future work includes the development of a GNC algorithm that will guide the different actors of the swarm toward an impact point on the ISO after detecting it.
We will also want to simulate different scenarios and integrate the GNC algorithm with a refined spatial discretization model to take into account the possibility of different gravity assists and longer mission times.

## Slide 16
Thank You
Questions?

## Slide 17: References
[1] D. J. Hoover, D. Z. Seligman, M. J. Payne, The Population of Interstellar
Objects Detectable with the LSST and Accessible for In Situ Rendezvous
with Various Mission Designs, The Planetary Science Journal 3 (3) (2022)
71, publisher: IOP Publishing. doi:10.3847/PSJ/ac58fe.
[2] A. M. Hein, T. M. Eubanks, M. Lingam, A. Hibberd, D. Fries, J. Schneider, P. Kervella, R. Kennedy, N. Perakis, B. Dachwald, Interstellar Now! Missions to Explore Nearby Interstellar Objects, Advances in Space Research (Jul. 2021). doi:10.1016/j.asr.2021.06.052.