## Slide 1
Role of Small Satellites in Planetary
and Earth Exploration
presented by
Dr. Charles Elachi
Professor, Electrical Engineering and Planetary Science, Caltech
JPL Director 2001- 2016

## Slide 2
March 2016
Mars
Earth
Sept 28, 2016
Entry, Descent, and Landing

## Slide 3
MarCO Fast Facts:
2 x 6U (14 kg) spacecraft launched as auxiliary tech demo payload with InSight
Both spacecraft healthy post launch
Comm and Nav tech demo complete
6.5 month cruise (157 million km) to Mars
Next objective is to provide an 8kbps real-time relay for InSight’s Mars Entry, Descent and Landing
MarCO
Mars CubeOne

## Slide 5
Ingenuity
Mars Helicopter

## Slide 6: Third Flight on Mars
Notes: The Rover’s mastcam video’d the helicopter’s third flight.

## Slide 8: Sample Recovery Helicopter (SRH)
2x Ingenuity-like rotorcraft with:
  Ground mobility
  Tube manipulator
  Stereo vision
  Inflight, absolute localization
+ 1x Base station and antennas
Parameter | Ingenuity | SRH
Rotor Diameter | 1.21 m | 1.21m
Mass, no payload | 1.8 kg | ~2.3 kg
Max payload | 0 g | 150 g
Max Flight Time | ~3 mins | ~3 min
Groundspeed | ~5 m/s | ~5 m/s
Max range per daily charge | ~700m | ~700m
x2
x1
Artist concept
Pre-Decisional Information – For Planning and Discussion Purposes Only. This document has been reviewed and determined not to contain export controlled technical data.

## Slide 9
Lunar Flashlight
Launched Dec 11, 2022

## Slide 10
Lunar Flashlight in development

## Slide 11
reflected VSWIR light (HVM3)
emitted thermal MIR light (LTM)
Lunar Trailblazer Smallsat Mission
Launch Configuration
w/in ESPA Grande volume
GOAL: Understand the form, abundance, and distribution of water on the Moon and the lunar water cycle
NASA SMD (PSD managed; ESSIO funded)
NASA Class-D , 7120.5e, SIMPLEx
Launch Type: Rideshare
Launch Date: Mid-2023 (Intuitive Machines, IM-2)
Propulsion: Hydrazine (~1000 m/s delta-v)
Lunar Orbit: 100±30 km polar | Primary Sci Ops: ≥1 year
PI: Bethany Ehlmann (Caltech)
DPI: Rachel Klima (APL)
PM: Calina Seybold (JPL) | PSE: Andy Klesh (JPL)
Flight System: Lockheed Martin
Mission Ops & Student Collaboration: Caltech
High-resolution Volatiles & Minerals Moon Mapper (HVM3; NASA/JPL)
(Hyperspectral Vis-Shortwave IR imaging spectrometer)
LTM (UKSA, U. Oxford)
Lunar Thermal Mapper (Multispectral Thermal Imager)
2 Payload Instruments (20 kg):
40-70 m/pixel
4 thermal channels (6-100 μm, +/- 2 K, 110-400K)
11 compositional channels (7-10 μm, < 0.5 μm)
50-90 m/pixel
0.6 – 3.6 μm @10nm
SNR > 100

## Slide 12
Lunar Trailblazer: Driving Motivations
Addresses two major scientific questions for the Moon directly from the Planetary Science Decadal Survey:
How are volatile compounds distributed, transported, and sequestered in near-surface environments on the Moon?
What are the inventories and distributions of volatile elements and compounds in...crusts of the inner planets?
Faustini crater interior (PSR) from terrain-scattered light (Cisneros et al., 2016)
OH/H2O absorption (blue) at 3-μm from M3 (Pieters et al., 2009)
In addressing these questions, Trailblazer also blazes a trail for human future exploration by evaluating
What is the form of lunar water and where are operationally useful deposits of lunar water?
What are the composition and thermophysical properties of the surface in prioritized future landing sites?

## Slide 13
Lunar Trailblazer Approach: Simultaneous Mapping Water, Temperature, Composition
LTM provides simultaneous temperature
Enhanced Spatial Resolution (3-6x), Spectral Range, Spectral Resolution relative to best-existing lunar data (M3, Diviner) → will determine the form, abundance, and distribution of OH, bound H2O, H2O ice plus enable the best surface compositional maps for geology
Simultaneous water, composition, and temperature enables thermal correction for accurate water wt%
Sensitive SNR enables surface ice detection + abundance mapping in permanently shadowed regions
Multiple Time of Day coverage → will answer the question: does volatile content change?
Will be the Orbital State-of-the-Art
existing M3 range
LTM provides simultaneous temperature
HVM3 spectra directly detect and determine the form and abundance of water at <100m/pixel.
Observations from 100±30km orbit
40-70 m/pixel
4 thermal channels
HVM3
LTM
50-90 m/pixel
0.6 – 3.6 μm @10nm

## Slide 14
Janus
Dual Space Probes, Serenity and Mayhem, designed to visit asteroids. Currently looking for a ride.

## Slide 15: DROID
Apophis (~340m) will pass within GEO distance from Earth in 2029 – a once-in-a-millennium event
The 2029 Apophis-Earth flyby creates unique opportunities:
Pre- and post-encounter observations yield unique insights how a small body responds to tidal forces
High-profile opportunity to image Apophis in close proximity to Earth
Will be a global event: More than a billion people will be able to see Apophis - Magnitude 5-6
Apophis ground track below GEO altitude
Credit: NASA/JPL-Caltech
Distributed Radar Observations of Interior Distributions
Notes: First-of-a-kind mission to escort Apophis through its closest approach, identifying surface changes and mapping its interior structure

## Slide 16
Pre-Decisional Information – For Planning and Discussion Purposes Only

## Slide 17: Penetrating Radar Will Map Interior
DROID: The Mission to Apophis
Rosetta, Hera/Juventas heritage
Image 3D interior structure at 10s of meters resolution
Simultaneous radar reflections from multiple spacecraft and viewing angles provide interior mapping analogous to medical CAT scans
Opportunity to compare data between:
  distant radar observations (DSN),
  ground-based radar observation during the close approach (DSN, HAARP, EISCAT),
  in-situ optical/radar data (DROID, OSIRIS-APEX).
CubeSats perform bistatic radar to map interior
Mothership communicates with CubeSats and Earth and maps surface

## Slide 18: Goals
DROID: The Mission to Apophis
Geophysical Characterization: Imaging, radar, and radio science
Understand Effect of Earth Flyby: Images through encounter
Rapid Response Reconnaissance Pathfinder: Using COTS
Coordination across agencies: Exercise and refine operational coordination
Mothership carries its own payload* plus 2 CubeSats
Inter-SC Link Radio
60 MHz radar
Inter-SC Link Radio
WAC
2 x 6U CubeSats
Narrow Angle Camera
AutoNav FSW
?
?
Room for small payload

## Slide 19: Novel Concurrent Radar Observations of Apophis (Overview)
The 2029 Apophis encounter is a unique opportunity to potentially observe an NEA using novel combinations of radar assets and operating bands in different geometries: ground-to-ground, in-situ, ground-to-space, monostatic, bistatic.
We will have the opportunity to compare data between a) distant radar observations (DSN), b) ground-based radar observation during the close approach (DSN, HAARP, EISCAT), and c) in-situ optical/radar data (DROID, OSIRIS-APEX).
Such a comparison would reveal what we can know about NEAs from the ground versus in-situ observation in addition to demonstrating novel bistatic radar measurement techniques.
JPL and Caltech (M. Haynes, C. Elachi) are currently exploring the use of ground-based long-wavelength radar (10-500 MHz) for interior sensing of NEAs (e.g., population studies, Apophis 2029).
DROID/Caltech are exploring the potential of novel ground-to-space bistatic radar observations of Apophis using the DROID 60 MHz radar or telecom frequencies.
Apophis 2029
~400 m
DSN
(X-, S-band)
DSN Range-Doppler (pre-CA/CA/post-CA)
HAARP (9.5 MHz)
UNM-LWA
Long-wavelength interior sensing (CA)
In-situ Bistatic Radar Imaging (post-CA)
DROID (60 MHz)
Ground-to-space bistatic (CA)
OVRO-LWA (60 MHz)

## Slide 20
Cloudsat
Hurricane Maria & Hurricane Jose
Notes: Figure 5: This scene shows two tropical cyclones from September 20, 2017 — Hurricane Maria near the Caribbean Sea and Tropical Storm José off the northeast U.S. coast. Data from the CALIPSO lidar and CloudSat radar appear as vertical slices in the atmosphere. CALIPSO lidar data is visualized as a bluish slice, with red and yellow colors denoting more scattering off of clouds and aerosols. CloudSat radar data is superimposed on the CALIPSO slice in brighter colors. Areas of heavier precipitation, found in each storm’s spiral bands, appear in red and pink (image credit: NASA/Roman Kowch)

## Slide 21
Notes: Figure 12: Cross section of CloudSat and GOES imagery (image credit: NASA/JPL-Caltech/CloudSat Data Processing Center, Ref. 20)

## Slide 22
RainCube

## Slide 23
Notes: Figure 22: Proposed RaInCube constellation configuration. The vertical sections in this picture are actual W-band data from CloudSat, here used only as graphic aid (image credit: NASA/JPL RainCube Team)

## Slide 24
INCUS will directly address why convective storms, heavy precipitation, and clouds occur exactly when and where they form
INCUS - Investigation of Convective Updrafts
2026 Launch

## Slide 25
Illustration of INCUS Flying Formation

## Slide 26
Tempest-D
Notes: Figure 6: Three images of Hurricane Dorian, as seen by a trio of NASA's Earth-observing satellites on 27-29 August 2019. Left: image of the MM instrument on the 6U CubeSat TEMPEST-D; Center: image of AIRS on Aqua satellite; Right: image of the CloudSat satellite. The data sent by the spacecraft revealed in-depth views of the storm, including detailed heavy rain, cloud height and wind (image credit: NASA/JPL-Caltech)

## Slide 27
Tempest-D Satellite Engineering Model
Notes: Figure 9: Steven Reising, professor of electrical and computer engineering, holds a model of the TEMPEST-D satellite. After meeting all its benchmarks for demonstrating small-satellite weather forecasting capabilities during its first 90 days, a Colorado State University experimental satellite is operating after more than one year in low-Earth orbit (image credit: Bill Cotton).
INCUS will showcase how proven technologies can be combined in innovative ways. The mission instrumentation includes a copy of Reising’s TEMPEST-D radiometer, along with three copies of a precipitation radar called RainCube. Funded by NASA and built by Jet Propulsion Laboratory, RainCube was a 2018 technology demonstration mission that featured a miniaturized Ka-band radar within a low-cost, quick-turnaround platform.